96 Cobra

1996 Ford SVT Mustang Cobra Specifications

Engine/Drivetrain
Engine Displacement    4.6L 281cid DOHC Modular
Compression Ratio    9.85:1
Horsepower    305 hp @ 5800 rpm
Torque    300 lbs-ft @ 4800 rpm
Transmission    Borg Warner T45 Five speed
Rear end    8.8" Solid axle  3.27:1 ratio w/Traction Lock

Suspension
Front    Modified Macpherson strut type, with progressive rate coil spings, and 29mm anti-roll bar
Rear    Solid axle located by four trailing arm setup, with linear rate coil springs, and 27mm anti-roll bar

Brakes
Front    13 in. vented disc PBR twin-piston caliper
Rear    11.65 in. vented disc, single-piston caliper
Anti-lock Brakes/Traction Control    Four wheel antilock standard

Wheels/Tires
Wheels    17 x 8 in. 5-spoke cast aluminum
Tires    BFGoodrich Comp T/A 245/45ZR-17

Other General Specifications
Wheelbase    101.3
Length    181.5
Width    71.8
Height    53.4
Front/Rear Track    60/58.7
Weight    Coupe :3391  Conv: 3531