## Slide 1
Robert Westby
Principal Engineer, Power Systems Engineering
Power You Can Trust

## Slide 2: Application Areas Requiring Robust Power
Data Center
Industrial
Aerospace
Digital Healthcare
Instrumentation
Notes: Just some of the application areas where we see tremendous potential and interest from customers

## Slide 3: Robust Power System Block Diagram
System Voltage Protect & Prioritize
SuperCap Controller
Alarm for Over-Temperature
LED Alert for Switch to Backup Power
Source 1
Main
Power Supply
(bench)
Source 2
Backup Power Supply
(laptop adapter)
LTC4421
Prioritized PowerPath Controller
LTC2977 DPSM
System Voltage Monitor
12 V
12 V or 19.5 V
19.5 V
5.6 V
5.6 V
7.5 V
3.7 V
Inductor
MAX31827 Temp Sensor
Input Voltage
SuperCap Voltage
Regulator Voltage
Output Voltage
GND
Super
Capacitor
LT8392 Buck Converter
LTM4656
Boost Regulator
MAX38890
Reversible Buck/Boost Regulator
3

## Slide 4: Power Glitches will NOT Stop the Robot
System Voltage Protect & Prioritize
SuperCap Controller
Alarm for Over-Temperature
LED Alert for Switch to Backup Power
LTC4421 Prioritized PowerPath Controller
Connects Valid Supply to Output Load
OV & UV & OC Detection
Limit Inrush Current
4
Source 1
Main
Power Supply
(bench)
Source 2
Backup Power Supply
(laptop adapter)
LTC4421
Prioritized PowerPath Controller
LTC2977 DPSM
System Voltage Monitor
12 V
12 V or 19.5 V
19.5 V
5.6 V
5.6 V
7.5 V
3.7 V
Inductor
MAX31827 Temp Sensor
Input Voltage
SuperCap Voltage
Regulator Voltage
Output Voltage
GND
Super
Capacitor
LT8392 Buck Converter
LTM4656
Boost Regulator
MAX38890
Reversible Buck/Boost Regulator
Notes: Demo Interaction: 1, 2 ,3

## Slide 5: No Power is No Problem for this Robot
System Voltage Protect & Prioritize
SuperCap Controller
Alarm for Over-Temperature
LED Alert for Switch to Backup Power
MAX38890 Super Capacitor Controller
Controlled Shutdowns – Current & Voltage
SuperCap Charge & Discharge Regulation
94% Efficiency
5
Source 1
Main
Power Supply
(bench)
Source 2
Backup Power Supply
(laptop adapter)
LTC4421
Prioritized PowerPath Controller
LTC2977 DPSM
System Voltage Monitor
12 V
12 V or 19.5 V
19.5 V
5.6 V
5.6 V
7.5 V
3.7 V
Inductor
MAX31827 Temp Sensor
Input Voltage
SuperCap Voltage
Regulator Voltage
Output Voltage
GND
Super
Capacitor
LT8392 Buck Converter
LTM4656
Boost Regulator
MAX38890
Reversible Buck/Boost Regulator
Notes: Demo Interaction: 1, 2 ,3

## Slide 6: Monitor Temperature and Catch Problems Early
System Voltage Protect & Prioritize
SuperCap Controller
Alarm for Over-Temperature
LED Alert for Switch to Backup Power
MAX31827 Temperature Monitor & Switch
Low Power with I2C and SMBus Support
-45°C to 145°C Temperature Range
Tiny 6-bump WLP: 1.048 x 1.268 mm
6
Source 1
Main
Power Supply
(bench)
Source 2
Backup Power Supply
(laptop adapter)
LTC4421
Prioritized PowerPath Controller
LTC2977 DPSM
System Voltage Monitor
12 V
12 V or 19.5 V
19.5 V
5.6 V
5.6 V
7.5 V
3.7 V
Inductor
MAX31827 Temp Sensor
Input Voltage
SuperCap Voltage
Regulator Voltage
Output Voltage
GND
Super
Capacitor
LT8392 Buck Converter
LTM4656
Boost Regulator
MAX38890
Reversible Buck/Boost Regulator
Notes: Demo Interaction: 5

## Slide 7: Keep Your System in the Know
Source 1
Main
Power Supply
(bench)
Source 2
Backup Power Supply
(laptop adapter)
LTC4421
Prioritized PowerPath Controller
LTC2977 DPSM
System Voltage Monitor
12 V
12 V or 19.5 V
19.5 V
5.6 V
5.6 V
7.5 V
3.7 V
Inductor
MAX31827 Temp Sensor
Input Voltage
SuperCap Voltage
Regulator Voltage
Output Voltage
GND
Super
Capacitor
LT8392 Buck Converter
LTM4656
Boost Regulator
MAX38890
Reversible Buck/Boost Regulator
System Voltage Protect & Prioritize
SuperCap Controller
Alarm for Over-Temperature
LED Alert for Switch to Backup Power
LTC2977 PMBus Power System Manager
Monitor up to 8 voltages
Automatic fault logging to internal EEPROM
LTpowerPlay for setup, config & debug
7
Notes: Demo Interaction: 1, 2 ,3

## Slide 8: Power You Can Trust
Maintain Stable Power
Mitigate Environment Impact
Manage & Monitor the Power System
Shut Down Gracefully
8

## Slide 9: Power You Can Trust
Maintain Stable Power
Mitigate Environment Impact
Manage & Monitor the Power System
Shut Down Gracefully
9