## Slide 1: DDEC Report Familiarization
Rev 8-16-17

## Slide 2: Launching DDEC Reports
Make sure that the ignition is in the <off> position
Connect datalink link connector
Turn Ignition to the <On> position
Launch DDEC Reports program by double clicking on DDEC Reports icon
Source:

## Slide 3: Possible Pop-Up
Enter unit # in Vehicle ID field and click OK

## Slide 4: Connection is automatic
With the ignition key on, as soon as you launch the DDEC Reports program it will start trying to connect
The default settings have auto extraction disabled, so while connection is automatic, data extraction is manual
While DDEC Reports is trying to connect, “Connecting” will be displayed

## Slide 5: Connected Screen
After connection has been established:
Available vehicle information fields will populate
“Start Extraction” bar will turn from gray to black

## Slide 6: Vehicle ID
If Vehicle ID does not reflect unit # of tractor”, click on “Tools”, then “Setup Vehicle”
Enter unit # in “New” field, then click “Send”

## Slide 7: Extraction Settings
Check on Reset Trip if you want to reset trip data on the vehicle.
Check on Reset Time if you want to synchronize the vehicle's time with your PC time.

## Slide 8: Extraction
Click on “Start Extraction”

## Slide 9: Extraction
Dash gage will show progress of extraction until 100% complete

## Slide 10: Extraction
New window will open entitled “DDEC Reports – Trip Activity”
File automatically saved in: C:\Detroit Diesel\DDEC Reports\Diagnostic\DATA PAGES
File name format is date (month,day,year) and computer name. Sample:

## Slide 11: DDEC Reports – Engine Trip
  Driving
  Vehicle Speed Limiting
  Top Gear
  Top Gear – 1
  Cruise
  Top Gear Cruise
  Speeding A
  Speeding B
  Highest Speed
  Coasting Time
  Coasting %
  Stop Idle
  Over Rev Limit
  Highest RPM
  Diag Records
  Hard Brake Count
  Firm Brake Count
  Brake Count
  Fan On Time
  Engine Utilization
  Vehicle Utilization
  DPF Regeneration
  DEF
The engine trip report is the report displayed in the window that opens after the extraction is complete
Information available in the Engine Trip report is as follows:

## Slide 12: DDEC Reports – Transmission Trip
  Economy Mode
  Performance Mode
  Manual Mode
  Launching
  eCoast
  Clutch Overload/Clutch Overtemp
  Creep Mode
To view transmission trip report, click on “View”, then “Activity”, then “Transmission Trip”
Information available in the Engine Trip report is as follows:

## Slide 13: Printing / Sharing
“Print” will print current screen report displayed
“Print All” will generate pop-up where you can select which reports you want
The best way to share DDEC Report data is to have a “print to PDF” printer set-up and print desired reports to PDF printer
Be sure to select “Print selected reports into a single file”
NOTE: Selecting all reports will result in a 50 page report
If the recipient has DDEC Report software, you can send them the XTR file from C:\Detroit Diesel\DDEC Reports\Diagnostic\DATA PAGES
There is an Export function but it is not recommended

## Slide 14: Accessing Saved Reports
Click on “File”
Click on “Quick Open”
Select desired file to open