## Slide 1
Optimizing Colonoscopy: A Triad of Success
Endoscope Choice, Stiffness, and Bowel Preparation
Dr Faiz Ibrahim
Senior Consultant Physician/Gastroenterologist

## Slide 2: Introduction & Learning Objectives
Select the appropriate endoscope for the clinical scenario.
Understand the role and control of endoscope stiffness.
Implement strategies to achieve and assess optimal bowel preparation.

## Slide 3: Endoscope Choice – Matching the Tool to the Task
Standard Adult Colonoscope
Specs: ~133 cm working length, 12-13 mm
diameter.
Key Features: Standard accessory channel (3.2-3.8mm), water-jet capability.
Best For: Routine diagnostic & therapeutic colonoscopy in average anatomy.
Considerations: May be challenging in
redundant colons or after complex surgery.
Pediatric/Thin Colonoscope
Specs: Similar length, but narrower diameter
(11-12 mm).
Best For: Tight strictures, severe diverticulosis, pediatric patients, or patients with significant angulation/fibrosis.
Trade-off: Smaller suction channel (2.8mm) can be slower with poor prep; may loop more easily due to increased flexibility.

## Slide 4: Endoscope Choice – Matching the Tool to the Task
Enteroscope & Balloon-Assisted Disposables Endoscopes
Types: Single-Balloon (SBE), Double-Balloon
(DBE), Spiral Overtube.
Specs: Longer (200-250 cm), often with a thinner shaft.
Best For: Deep small bowel enteroscopy, intraoperative endoscopy, altered anatomy (e.g., Roux-en-Y).
Pros: Eliminates reprocessing delays/costs, guaranteed function, no cross-contamination risk.
Cons: Environmental impact, potential differences in "feel," cost structure.
Ideal For: ERCP in infected ducts, rapid turnover units, ICU bedside procedures.
Cap-Assisted Colonoscopy (Transparent Cap): Can improve mucosal views and stabilize scope tip for polypectomy in difficult locations.

## Slide 5: Endoscope Choice- when to use what?
Routine Screening --> Standard Adult Colonoscope
Diverticulosis, Stricture, Pain --> Pediatric/Thin Colonoscope
Small Bowel Bleeding, Altered Anatomy --> Balloon-Assisted Enteroscope.
ICU Patient, ERCP for PSC, post OLT --> Disposable Colonoscope/Duodenoscope.
Difficulty at Flexures/ICV --> Consider Cap-Assisted

## Slide 6: What is Scope Stiffness and why does it matter? The Art of Loop Control
Definition: The resistance of the endoscope shaft to bending (forming a loop).
The Core Principle: Transmission of Force. A stiffer shaft transmits torque from your hands more efficiently to the tip, preventing and reducing loops.
Consequence of Looping: Patient discomfort, prolonged procedure, missed lesions, increased sedation needs, risk of perforation.

## Slide 7: Variable Stiffness Colonoscopes
How it Works: Dialing knob tightens a wire within the shaft, increasing its rigidity.
Standard Practice: "Soft in, Stiff Out"
  Insertion (Soft/Low): For navigating sigmoid and flexures with minimal force.
  Withdrawal & Therapy (High/Stiff): Once a straight position is achieved (e.g., in transverse/cecum), increase stiffness to maintain position, stabilize scope for polypectomy, and improve mucosal inspection on withdrawal.
Caution: Overuse of high stiffness during insertion can increase patient’s pain and risk
of stretching mesentery.

## Slide 8: Techniques for Loop Reduction
Use stiffness control appropriately.
Abdominal Pressure: The first-line maneuver. Nurse-applied pressure to fix the sigmoid or transverse colon.
Position Change: Rotating patient (Lt lateral/supine/Rt lateral/prone) using gravity to open angles.
Shaft Shortening ("Pull-and-Twist"): The definitive manual technique. Withdraw
scope while torquing to pleat colon onto the stiffened shaft.
Magnetic Imaging/scope-guide: Real-time 3D visualization of loops to guide reduction maneuvers.

## Slide 9: Bowel Preparation – The Foundation of Quality
Adenoma Detection Rate (ADR): Inadequate prep halves ADR. Missed lesions are in poorly cleansed segments.
Procedure Efficiency: Increased withdrawal time, frustration, incomplete procedures.
Safety: Impaired visualization increases risk of perforation and missed pathology.
Cost: Need for repeat procedure sooner than recommended interval.

## Slide 10: Choice of Prep: It's Not One-Size-Fits-All
Key Factors: Patient age, comorbidities (renal, cardiac), tolerance, prior prep failure.
Personalize: Consider patient's medical history and preferences.
High-Volume vs. Low-Volume: Split-dose low-volume regimens now standard for best tolerance and efficacy.

## Slide 11: Common Effective Regimens
Split-Dose 4L PEG: Gold standard for efficacy; tolerance is an issue.
Split-Dose 2L PEG + Ascorbate: Better taste, better compliance and similar efficacy.
Split-Dose Sodium Picosulfate/Mg Citrate: Very low volume, good for cardiac/renal patients.
Oral Sulfate Solution: Lower volume than PEG, specific electrolyte considerations.

## Slide 12: The Critical Importance of Split-Dosing
Definition: The majority of prep is taken the night before, and the final dose is taken 4-6 hours before the procedure start time.
Goal: Cleaning the right colon (most difficult to cleanse) just before the exam.
Evidence: Superior in every quality metric—cleansing, ADR, patient willingness to
repeat.
Mandate: Should be the default scheduling protocol for all afternoon and most
morning procedures.

## Slide 13: Standardizing Assessment: The Boston Bowel Preparation Scale (BBPS)
A 10-point validated scale (0-3 per segment: Right, Transverse, Left).
0 = Unprepared. Solid stool, unable to visualize.
1 = Poor. Murky fluid, >90% mucosa seen.
2 = Good. Minor residue, >90% mucosa seen.
3 = Excellent. Clean, no residue.
Why Use It? Objectively documents quality, guides follow-up intervals, improves communication. A total score ≥6 with all segments ≥2 is generally considered "adequate for screening."

## Slide 14: Managing Inadequate Prep
Intra-procedure:
Use water-jet or pump irrigators aggressively.
Suction/re-suction fluid.
Consider changing patient position
to move fluid.
Document BBPS score clearly.
Post-procedure:
Communicate Clearly: Explain why the prep was inadequate.
Personalize Next Prep: Switch to a different regimen.
Schedule Appropriately: Recommend repeat in <1 year, not the standard
10-year interval for a truly "clean" exam.

## Slide 15: References
Quality Indicators for Colonoscopy“ Gastrointest Endosc. 2015;81(1):31-53.
Performance measures for lower gastrointestinal endoscopy: a European Society of Gastrointestinal Endoscopy
(ESGE) Quality Improvement Initiative.“ Endoscopy. 2017;49(4):378-397.
Practice Guidelines for Preoperative Fasting...“ Anesthesiology. 2017;126(3):376-393.
Impact of colonoscopy preparation quality on detection of suspected colonic neoplasia.“ Gastrointest
Endosc. 2003;58(1):76-9.
The Boston bowel preparation scale: a valid and reliable instrument for colonoscopy-oriented research.“ Gastrointest Endosc. 2009;69(3 Pt 2):620-5.
A randomized clinical study comparing reduced-volume oral sulfate solution with standard 4-liter sulfate-free
electrolyte lavage solution as preparation for colonoscopy.“ Gastrointest Endosc. 2010;72(2):328-36. (Covers the
mechanism)
Mechanism of action and toxicities of purgatives used for colonoscopy preparation.“ Expert Opin Drug Metab Toxicol. 2016;12(10):1237-45.
Variable stiffness colonoscopes: a randomized controlled trial on efficacy and patient tolerance.“ Gastrointest Endosc. 2009;70(2):349-54.
Usefulness of a pediatric colonoscope for colonoscopy in adults.“ Gastrointest Endosc. 2000;51(3):314-7.
Cap-assisted colonoscopy: a meta-analysis of high-quality randomized controlled trials.“ Endosc Int Open. 2018;6(10):E1214-E1223.

## Slide 16: References
A randomized, controlled, parallel-group study of low-volume sodium picosulfate plus magnesium citrate versus standard-volume polyethylene glycol solution for colonoscopy preparation.“ Gastroenterology. 2011;140:S-144.
Acute phosphate nephropathy following sodium phosphate bowel purgative: an underrecognized cause of chronic renal failure.“ J Am Soc Nephrol. 2005;16(11):3389-96.
  The safety of polyethylene glycol 3350 solution in chronic renal failure patients undergoing colonoscopy.“ J Clin
Gastroenterol. 2014;48(1):55-9.
Bowel preparation for colonoscopy: 2017 update." Expert Rev Gastroenterol Hepatol. Vol: 2017;11(1):57-67.
Optimizing adequacy of bowel cleansing for colonoscopy: recommendations from the US multi-society task force
on colorectal cancer.“ Gastroenterology. Vol: 2014;147(4):903-24.

## Slide 17: Thank You for your attention Visit our online platform and learn more
www.muscatendoscopyacademy.com