## Slide 1: University of South Florida BIOSat: Botany in Orbit Satellite
Subsystem: Embedded System, Sensors, Wireless Communication, and Environmental Control
Team Name: Astroflora
Team Members Names: Phillip Cornett, Joseph Moore, Christopher Serrano, and Abigail Wittenbrook
Date: February 9, 2024
Notes: Fill out the information according you your team

## Slide 2: Subsystem Requirements
ID | Requirement | Rationale
Payload-1 | Payload shall be capable of circulating air through the chamber at a velocity of 0.3-0.5 m/s using fans and compression tanks. | Proper air circulating is necessary to sustain plant growth.
Payload-2 | The grow light shall provide an intensity of 200-250 umol/m2/s with a light wavelength of 400-700 nm for 16-18 hours daily. | To sustain red romaine lettuce growth, specific light intensities and wavelengths for set intervals are necessary.
Payload-3 | Payload shall be capable of collecting data through the sensor array, including humidity, pH, alcohol, ethylene, temperature, CO2, and O2. | To analyze red romaine lettuce growth, specific measurements are required, including humidity, pH, alcohol, ethylene, temperature, CO2, and O2
Payload-6 | Payload shall include optical/fisheye camera imaging on the root and sprout zones. | Root and leaf images are required for visual assessment of growth patterns.
Payload-8 | Thermal Insulation and heating shall be capable of always keeping the temperature between 18-22C. | Keeping the plant's temperature at a healthy level is crucial for sustaining red romaine lettuce growth.
Notes: Remind everyone what you are trying to accomplish and the requirements that are driving your decisions.

## Slide 3: Current Design
Power Control
MPPT maximizing solar power efficiency multi-output
Sensor Array
5 different sensors: O2, CO2, VOC, Light, Alcohol, and Temp/Humidity
COMM
DIGI XBee Radio Frequency Module
Data Collection
Microcontroller sent via modules to antennas
Payload/Life Support
1 Hyperspectral camera
2 Optical cameras
Sensor Array
Notes: Any 3D models, schematics, or diagrams are appreciated so add them to demonstrate the progress you are making. Its ok if its not final but let us know what you are doing to meet your requirements. Add more slides as needed.

## Slide 4: Power Budget
Component | Voltage | Current | Time usage | Max Expected Current Draw | Power Draw
Solar Panels | 10V | 2A | N/A | N/A | 20W
Battery | 3.7V | 6Ah | N/A | N/A | 22.2WH
Temp and VOC Sensor | 3.3V | 2mA | 2 ms | 2mA | 6.6mW
O2 Sensor | 3.3V - 5V | 6.5mA | 1 min | 6.5mA | 21.45mW
CO2 Sensor | 3.3V - 5V | 4mA | 1 min | 4mA | 13.2mW
Alcohol Sensor | 3.3V - 5V | 10mA | 5 mins | 10mA | 33mW
Light Sensor | 3.3V | 2uA - 45uA | 24hr | 45uA | 148.5uW
Heater | 5V | 200mA | As needed | 200mA | 1W
Fan | 5.5V | .03A | As needed | 73mA | .4W
LED | 3.3V - 5V | 16mA(per light) | 24hr | 320mA | 1.056W
OV2640 | 2.75V | 50mA 600uA (Stand-by) | Depends | 20mA | 140mW
GPS | 3.6V | 10mA 100mA | N/A | N/A | 360mW 36mW
Receiver | 2V | 8mA | N/A |  | 16mW
Wireless Module | 3.6V | Transmit (215mA) Receive (29mA) Sleep (2.5uA) | N/A | N/A | 774mW 104.4mW
SD Card Module | 5V | .2mA 200mA | N/A | N/A | 1mW 1W

## Slide 5: Electric Schematic

## Slide 6: This Week's Tasks
All sensors and environmental devices, other than the alcohol sensor, have been integrated into a single code.
This code waits for user input, then turns on the environmental subsystem, runs through one full measurement cycle, returns all sensors to sleep mode, and turns off the environmental subsystem.

## Slide 7: This Week's Tasks
Integrated necessary libraries within Java IDE and resolved JDK issues within XBee's RXTX library.
Used API construction to transmit and receive messages, source address information, and data.
Created a network across multiple nodes.
Notes: What did you accomplish this week?! Add slides as needed.

## Slide 8: This Week's Tasks
Begin/Test final coding that will replicate day cycle and assign intervals for data collection, light cycle, and photo capture.
Notes: What did you accomplish this week?! Add slides as needed.

## Slide 9: Next Week's Goals
Implement cameras into the sensor subroutine. Test physical implementation.
Configure sensors and camera to store data into the SD card for transmission.
Wirelessly transfer packets of data from SD card and module using the basic communication system.
Begin physical test of day cycle code for all sensors.
Order PCB.
Notes: What will you get done next week?

## Slide 11: Light Sensor (VEML7700-TR)

## Slide 12: Temperature/Humidity (BME680)

## Slide 13: Alcohol (ZMOD4510 )

## Slide 14: Light Sensor (VEML7700-TR)

## Slide 15: SEN053A & SEN0496