University of South Florida
BIOSat: Botany in Orbit Satellite
Subsystem: Embedded System, Sensors, Wireless Communication, and Environmental Control
Team Name: Astroflora
Team Members Names: Phillip Cornett, Joseph Moore, Christopher Serrano, and Abigail Wittenbrook
Date: February 2, 2024
[Speaker Notes: Fill out the information according you your team]

---
Subsystem Requirements
ID	Requirement	Rationale
ENV	Regulate capsule climate and illumination internally.	Vitality of the red lettuce depends on the precise control these systems give, each addressing a fundamental need for growth.
MCC	Power-efficient microcontroller with sufficient processing power and I/O for environmental control	Chosen for its energy efficiency and processing speed, the Arduino microcontroller structure ensures sustained, accurate environment management.
PCS	Provision of reliable energy from solar panels to all components.	The system ensures optimal energy distribution from solar panels and storage, enabling the CubeSat to function autonomously for its 30-day mission.
SPS	Equip a sensor suite to monitor for plant health.	Sensors must precisely monitor temperature, humidity, CO2, and ethylene levels, as well as air flow and light intensity, essential for plant survival.
WCT/R	Transmit and receive infallible data over long ranges.	Monitoring the health of the plant and the success of our system will be shown through the data collected from the receiving system. This is how we will know the status of our project.
[Speaker Notes: Remind everyone what you are trying to accomplish and the requirements that are driving your decisions.]

---
Current Design
Power Control
MPPT maximizing solar power efficiency multi output
Sensor Array
5 different sensors: O2, CO2, VOC, Light, Alcohol, and Temp/Humidity
COMM
DIGI XBee Radio Frequency Module
Data Collection
Microcontroller sent via modules to antennas
Payload/Life Support
1 Hyperspectral camera
2 Optical cameras
Sensor Array
Fans
Water reservoir
LED light
Heater
[Speaker Notes: Any 3D models, schematics, or diagrams are appreciated so add them to demonstrate the progress you are making. Its ok if its not final but let us know what you are doing to meet your requirements. Add more slides as needed.]

---
Current Task:
Tasks: Plant Health Monitoring System Check
Create unit tests for individual components and record their power characteristics
Construct code to operate individual components in an isolated environment
Identify power complications and plan for solutions depending on the duty cycle and sleep mode capabilities
Modify custom PCB design to accommodate any change in requirements
[Speaker Notes: What did you accomplish this week?! Add slides as needed.]

---
Next Week's Goals
Document system architecture, including how sensors are connected and communicate.
Troubleshooting guide for common sensor integration issues
Begin to implement code sections into one program
Control power consumption cycles of environmental controls
[Speaker Notes: What will you get done next week?]

---
Light Sensor (VEML7700-TR)

---
Temperature/Humidity (BME680)

---
Alcohol (ZMOD4510 )

---
Light Sensor (VEML7700-TR)

---
SEN053A & SEN0496

---
Power Budget
Component	Voltage	Current	Time Usage	Max expected Current Draw	Power Draw
Solar Panels	10V	2A	N/A	N/A	20W
Battery	3.7V	6Ah	N/A	N/A	22.2WH
Temp,Humid / VOC Sensor	3.3V	2mA	2 ms	2mA	6.6mW
Oxygen Sensor	3.3V - 5V	6.5mA	1 min	6.5mA	21.45mW
Carbon Dioxide Sensor	3.3V - 5V	4mA	1 min	4mA	13.2mW
Alcohol Sensor	3.3V - 5V	10mA	5 mins	10mA	33mW
Light Sensor	3.3V	2uA - 45uA	24hr	45uA	148.5uW
Heater	5V	200mA	As needed	200mA	1W
Fan	5.5V	.03A	As needed	73mA	.4W
LED	3.3V - 5V	16mA(per light)	24hr	320mA	1.056W
OV2640	2.75V	50mA / 600uA (Stand-by)	Depends	20mA	140mW
GPS	3.6V	10mA / 100mA	N/A	N/A	360mW / 36mW
Receiver	2V	8mA	N/A		16mW
Wireless Module	3.6V	Transmit (215mA) / Receive / (29mA) / Sleep / (2.5uA)	N/A	N/A	774mW / 104.4mW
SD Card Module	5V	.2mA / 200mA	N/A	N/A	1mW / 1W