## Slide 1
GROUNDING AND BONDING
FOR
AMATEUR RADIO
BY PAUL MELVIN K4PGM

## Slide 2: GROUNDING & BONDING
WHY IS IT SO
COMPLICATED?
BY
PAUL MELVIN
K4PGM

## Slide 3: ELECTRICAL CIRCUIT

## Slide 4: ELECTRICAL CIRCUIT

## Slide 5: HOW MUCH CURRENT ?
FEEL THE SENSATION.

## Slide 6: Where it all began!
Telegraph was the first nationwide electrical system.

## Slide 7: GROUNDING & BONDING EXPLAINED
Grounding is the connection of the electrical circuit to the earth.
  This allows a safe means for unused current to be returned to the source and removed from conductive surfaces.
Bonding is the connection of equipment so there is no potential voltage between equipment.
  Both bonding and grounding must be used to assure a safe environment.

## Slide 8: GROUNDING and BONDING
TYPICAL GROUNDING/BONDING CONNECTION

## Slide 9: CALL IT WHAT YOU WANT!
Grounding
Earthing
Protective earth conductor
That green wire?

## Slide 10: REASONS FOR GROUNDING
SAFETY
  REDUCES ELECTRICAL SHOCK HAZARDS
    CURRENT AMOUNTS AND EFFECTS
LIGHTNING
  REDUCES STATIC BUILD UP
  HELPS TO RETURN SURGES SAFELY TO GROUND.
RF BURNS AND SHOCK HAZARDS
  RADIO FREQUENCY INJURY

## Slide 11: It’s The Law!
General requirements
  Grounding of electrical equipment
  Bonding of electrical equipment
  Bonding of electrically conductive materials and other equipment
  Effective ground fault current path

## Slide 12: 2017 NEC
National Electrical Code
  Enacted as law by NC legislators
  Insurance concerns.
Article 250
  Covers grounding and bonding.
  Ensures safety and fire protection.
Notes: It is the law
Will your insurance pay for damages that are not connected to ground per law?

## Slide 13: EQUIPMENT GROUNDING
Normally non-current-carrying conductive materials enclosing electrical equipment, or forming part of such equipment, SHALL be connected to earth so as to limit the voltage to ground on these materials.
Metal cases
  Radio
  Tuner
  Meters
  amplifiers

## Slide 14: EQUIPMENT BONDING
Normally non-current-carrying conductive materials enclosing electrical conductors or equipment, or forming part of such equipment, SHALL be connected together and to the electrical supply source in a manner that establishes an effective ground-fault current path.
Connect it all together
  Everything listed in previous grounding slide!

## Slide 15: CONDUCTIVE MATERIALS AND OTHER EQUIPMENT
Normally non-current-carrying electrically conductive materials that are likely to become energized SHALL be connected together and to the electrical supply source in a manner that establishes an effective ground-fault current path.
If it is conductive and can become energized then bond it and ground it!

## Slide 16: EFFECTIVE GROUND-FAULT CURRENT PATH
Electrical equipment, wiring and other electrically conductive material likely to become energized SHALL be installed in a manner that creates a low impedance circuit facilitating the operation of the over current device.
Grounding must allow for the correct operation of:
  Circuit Breakers
  Fuses
  Circuit interrupters

## Slide 17: ELECTRICAL SAFETY GROUNDING
#1 REASON FOR GROUNDING
  PERSONAL SAFETY
  SAFETY OF PERSONS VISITING
  FIRE SAFETY
  PROTECTION OF EQUIPMENT

## Slide 18: YOUR STATION
DESIGN YOUR STATION
  Use best practices to install electrical
  Power equipment with low DC voltage
    Less likely to cause serious injury
  Mitigate areas of high current
    High current causes more serious injuries
  GROUNDING IS YOUR BEST PROTECTION!

## Slide 19: AREAS OF CONCERN
OUTLETS
  Are outlets grounded per NEC?
  Are all ground prongs intact?

## Slide 20: STATION GROUNDING
DON’T LEAVE ANYTHING UNGROUNDED

## Slide 21: LIGHTNING PROTECTION
LIGHTING SURGES AND STRIKES
  CANNOT BE PREVENTED
  CAN BE DIVERTED TO GROUND
  CAN REDUCE THE AMOUNT OF CURRENT FLOWING THROUGH EQUIPMENT.
MOST RADIO EQUIPMEN IS SOLID STATE
  THE COMPONENTS OPERATE AT LOW VOLTAGE
  HIGHER VOLTAGE FROM SURGES DAMAGE THEM BEYOND REPAIR.
  YES IT IS A GAMBLE. INCREASE YOUR ODDS.

## Slide 22: BOND THAT EQUIPMENT!

## Slide 23: ANTENNA/TOWER
GROUNDING AT THE CONNECTION POINT
  GROUND THE SHIELD AND ALL METALLIC PARTS THAT DO NOT CONNECT TO THE CENTER CONDUCTOR.
GROUND THE TOWER OR POLE AT THE BASE ON EACH LEG OR MULTIPLE TIMES.
  DRIVE 8’ GROUND RODS
  BOND THEM TOGETHER WITH COPPER CONDUCTOR.

## Slide 24: TOWER AND ENTRY GROUNDING

## Slide 26: LIGHTNING SURGE PROTECTORS

## Slide 27: RF MANAGEMENT
RADIO FREQUENCY VOLTAGE AND CURRENT CAN DISRUPT NORMAL OPERATION (RFI).
“THERE IS NO RF GROUND”
  EQUALIZE AUDIO AND RF THROUGHOUT YOUR STATION
    BOND ALL CONDUCTIVE MATERIALS
    BONDING DOES NOT ASSURE “0” AUDIO AND RF VOLTAGE BUT KEEPS IT THE SAME SO CURRENT WILL BE REDUCED.

## Slide 28: REMEMBER!
YOU CANNOT OVER GROUND!
KEEP ALL EQUIPMENT BONDED TO REDUCE POTENTIAL VOLTAGE AND CURRENT.
KEEP ALL GROUND CONDUCTORS AS SHORT AS POSSIBLE.
ALL GROUNDING ELECTRODES MUST BE BONDED TOGETHER.

## Slide 29
GROUNDING AND BONDING
FOR
AMATEUR RADIO
BY PAUL MELVIN K4PGM