Armored Star Shower Pan Installation

Installation of a shower pan is a two trip process.

Day One:

Block seat and threshold are constructed as required. The shower pan is then trimmed and formed, after which it is then pre-sloped.

Day Two:

After a couple of days of drying time for the pre-slope, the pan is ready for waterproofing. Waterproofing material is applied using a heated high pressure proportioning system. The product is applied at a minimum thickness of 30 mils. The shower pan is ready for water testing immediately after waterproofing is completed.