## Slide 1
Telesound: Can Real-Time Video Streaming of Ultrasound Imaging from Remote Locations Yield an Accurate Diagnosis?
Department of Pediatrics, Section of Emergency Medicine, Yale University School of Medicine, New Haven, CT
Rachel E Whitney MD, Antonio Riera MD, Lei Chen MD, MHS
Background
Ultrasound (US) aids medical decision-making in remote locations.
Use of cell phones in medical care has become a popular trend, and 85% of the world has access to a 3G network.1
Objectives
To evaluate live-stream video for interpretation of ultrasound using a 3G network.
Results
Conclusions
Live-stream video conference using two cellphones over a 3G network is a feasible and accurate method for ultrasound scan consultation from a remote location.
Methods
We evaluated the inter-rater reliability of US assessment for abdominal free fluid, ileo-colic intussusception, and hip effusions.
De-identified 6-second video clips in .mp4 format were downloaded to a laptop:
- 58 FAST scans (23 positive)
- 44 intussusception scans (16 positive)
- 28 hip scans (7 positive)
  Scan interpretation was dichotomized into positive or negative for pathology.
  A bedside US expert evaluated each scan on the laptop screen.
  Remote/Bedside Comparison
  Using two iPhone 3Gs for ‘telesound’ consultation, a Skype connection was used to link a second US expert located in Ethiopia. A remote interpretation was done via a live-stream video connection.
  Bedside/Bedside Comparison
  Upon return from Ethiopia, evaluation of the scans was repeated by the remote reviewer on the same laptop.
  Inter-rater reliability analysis using the Kappa statistic and percent agreement was done.
US scan | Reviewer Comparison | Kappa (95% CI) | Percent Agreement
FAST | Remote/Bedside | 0.748 (0.576-0.92) | 86%
 | Bedside/Bedside | 0.851 (0.71-0.992) | 92%
Ileo-colic intussusception | Remote/Bedside | 0.816 (0.648-0.984) | 80%
 | Bedside/Bedside | 0.8 (0.616-0.984) | 81%
Hip effusion | Remote/Bedside | 0.764 (0.519-1.0) | 88%
 | Bedside/Bedside | 0.747 (0.479-0.884) | 88%
Kappa Agreement2: None to slight: 0.0-0.2; Fair: 0.21-0.4; Moderate: 0.41-0.6; Substantial: 0.61-0.8; Almost perfect: 0.81-1.0
4G/LTE
3G
2G/GSM
References
1. http://www.worldtimezone.com/4g.html
2. McHuch, M. Interrater reliability: the kappa statistic. Biochem Med (Zagreb). 2012 Oct; 22(3): 276-282.