## Slide 1: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response (ABR)
James W. Hall III, PhD
Professor
Osborne College of Audiology
Salus University
Extraordinary Professor
University of Pretoria South Africa
jwhall3phd@gmail.com www.audiologyworld.net

## Slide 2: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response (ABR)
Review of ABR anatomy and physiology … the ABR is NOT a test of hearing
Pediatric applications of ABR measurement
Four advances in pediatric hearing assessment with ABR
  Chirp stimuli (click and tone burst)
  The B-81 oscillator for bone conduction ABR measurement
  Options for un-sedated ABR measurement
  Efficient ABR measurement in < 30 minutes
Kindle Direct Publishing (www.amazon.com) 2015

## Slide 3
Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response ABR is Generated by Axons … Not Nuclei

## Slide 4
Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response ABR is Generated by Onset Neurons (Octopus Cells)

## Slide 5
Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Generators of ABR Waves
Wave I is generated on the side of the stimulus (ipsilateral)
Wave III is generated by ipsilateral and midline pathways
Wave V is generated by contralateral pathways

## Slide 6: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response The ABR is Not a Test of “Hearing”
Generated by axons, not nuclei
Click evoked ABR is generated only by “onset” neurons
Highly dependent on synchronous firing of these neurons
Does not assess structures rostral to brainstem (e.g., thalamus and auditory cortex)
Can be recorded from persons who are:
  Comatose
  Sedated
  Anesthetized persons
Usually elicited with simple non-speech signals

## Slide 7: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response How is “Hearing” Assessed in Children
Behavioral Audiometry (if feasible)
Otoacoustic Emissions (OAEs)
Aural Immittance Measurements
  Tympanometry and Wideband Reflectance/Absorbance
  Acoustic Reflexes (ipsi- and contralateral conditions)
Auditory Brainstem Response (ABR)
  Click, Tone Burst and Chirp Stimulation
  Speech stimuli (e.g., da or ga)
Auditory Steady State Response (ASSR)
Electrocochleography (ECochG)
Cortical Auditory Evoked Responses

## Slide 8: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response (ABR)
Review of ABR anatomy and physiology … the ABR is NOT a test of hearing
Pediatric applications of ABR measurement
Four advances in pediatric hearing assessment with ABR
  Chirp stimuli (click and tone burst)
  The B-81 oscillator for bone conduction ABR measurement
  Options for un-sedated ABR measurement
  Efficient ABR measurement in < 30 minutes
Kindle Direct Publishing (www.amazon.com) 2015

## Slide 9
Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response
> 50 Years of Clinical Experience with ABR
Jewett D and Williston J. Auditory evoked far fields averaged from the scalp of humans. Brain 4: 681-696, 1971.

## Slide 10
Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response
> 50 Years of Clinical Experience with ABR

## Slide 11: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Pediatric Applications of ABR (> 3000 publications)
Infant hearing screening (automated ABR)
Differential diagnosis of childhood hearing loss
  Sensory hearing loss
  Conductive hearing loss
  Neural auditory dysfunction
  Auditory neuropathy spectrum disorder (ANSD)
Frequency-specific estimation of auditory thresholds (an electrophysiologic audiogram)
Monitoring auditory function to document effective management
Confirmation of normal hearing thresholds in suspected false hearing loss
Objective assessment of auditory processing disorder

## Slide 12: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response (ABR)
Review of ABR anatomy and physiology … the ABR is NOT a test of hearing
Pediatric applications of ABR measurement
Four advances in pediatric hearing assessment with ABR
  Chirp stimuli (click and tone burst)
  The B-81 oscillator for bone conduction ABR measurement
  Options for un-sedated ABR measurement
  Efficient ABR measurement in < 30 minutes
Kindle Direct Publishing (www.amazon.com) 2015

## Slide 13: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Evidence Based ABR Protocol: Stimulus Parameters
Parameter Selection Comment
Transducer Insert earphone A dozen good reasons; BC also O.K.
Type Click or tone bursts Both are essential; Chirps are available
Polarity Rarefaction Larger amplitude; change as indicated
Rate > 20/sec Faster rate saves time
Intensity dB nHL Verify stimulus intensity
Repetitions Variable Whatever is needed for good SNR
Masking Rarely needed Only if ABR is abnormal and no wave I
Mode Monaural Provides ear-specific information

## Slide 14: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Evidence Based ABR Protocol: Acquisition Parameters
Parameter Selection Comment
Electrodes
Noninverting Fz High forehead preferred to vertex
Inverting Ai Ipsilateral earlobe, not mastoid
Ground Fpz Low forehead for common electrode
Filters (HP) 30 Hz Especially in infants
(LP) 3000 Hz 1500 Hz O.K. if high frequency artifact
Notch None Removes critical low frequency energy
Amplification 100,000 Or sensitivity of +/- 25 or 50 mV
Analysis time 15 ms Encompasses ABR in all cases
Pre-stim baseline - 1 ms Information on response quality
Sweeps (# stimuli) Variable Whatever yields adequate SNR (3:1)

## Slide 15: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Broad Band and Narrow Band Chirp Stimuli

## Slide 16
Low Frequencies
High Frequencies
Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Broad Band and Narrow Band Chirp Stimuli

## Slide 17: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Efficient Pediatric ABR Measurement
Larger amplitudes for wave I and V (up to twice as large)
More confident identification of ABR
Detection of clear ABR restless children
Possibility of more accurate ABR threshold estimation
Quicker ABR test time (larger ABR increases SNR)

## Slide 18: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response (ABR)
Review of ABR anatomy and physiology … the ABR is NOT a test of hearing
Pediatric applications of ABR measurement
Four advances in pediatric hearing assessment with ABR
  Chirp stimuli (click and tone burst)
  B-81 oscillator for bone conduction ABR measurement
  Options for un-sedated ABR measurement
  Efficient ABR measurement in < 30 minutes
Kindle Direct Publishing (www.amazon.com) 2015

## Slide 19: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Clinical Indications for Bone Conduction ABR
Craniofacial anomalies associated with middle ear dysfunction
Syndrome associated with conductive hearing loss
History of middle ear disease
Abnormal tympanometry findings
Abnormal delay in wave I latency for air conduction ABR
Before and/or after surgical management for middle ear disease

## Slide 20: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response A Newer Bone Oscillator Design

## Slide 21: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response A Newer Bone Oscillator Design
Slightly Greater Output
Lower Harmonic Distortion

## Slide 22
Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response
Ipsilateral Wave I Verifies Ear-Specific Findings
Ipsi Channel
Wave I
Contra Channel
No Wave I

## Slide 23
Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response
Estimation of Air-Bone Gap with ABR
0
100
Click Intensity in dB nHL
Wave V Latency in msec
8
6
4
20
40
60
80
Air conduction
35 dB
Bone conduction

## Slide 24: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Reasons for Only Using Click Stimuli for Bone Conduction ABR
Test time is unacceptably lengthy with addition of tone burst bone conduction recordings
Confident identification of ABR is more likely with click versus tone burst stimulation
Provides the information that is needed for management decisions, i.e., referral to otolaryngology for medical or surgical intervention

## Slide 25: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response (ABR)
Review of ABR anatomy and physiology … the ABR is NOT a test of hearing
Pediatric applications of ABR measurement
Four advances in pediatric hearing assessment with ABR
  Chirp stimuli (click and tone burst)
  The B-81 oscillator for bone conduction ABR measurement
  Options for un-sedated ABR measurement
  Efficient ABR measurement in < 30 minutes
Kindle Direct Publishing (www.amazon.com) 2015

## Slide 26: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response ABR Measurement: Detecting a Signal (ABR) within Electrical “Noise”
0 10 20 40 80 100 250 500 1000 2000 4000 Hz
µV
EEG sleep
500
250
125
60
30
0
EEG awake
ECG
EMG
EOG (ENG)
ABR
Amplitude 0.1 – 1 μV
Frequencies 30 – 3000 Hz
Rectified RF noise
Power line noise
60 Hz

## Slide 27
Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response
The Goal = A Sleeping and Quiet Child

## Slide 28: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Un-Sedated (Natural Sleep) ABR Measurement is Feasible
Detailed instructions for parents/caregivers
Atypically late bedtime for the child
Two adults transport the child to the clinic
ABR is scheduled early in the morning
Preparation for ABR begins immediately upon patient arrival at the clinic
Make the child as comfortable as possible
Record the ABR after feeding in a dark and quiet room

## Slide 29: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Comfortable Options for Pediatric ABR Measurement
For Mother & Child

## Slide 30: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Melatonin as a Sleep Aid
Hormone naturally produced by pineal gland
Controls circadian rhythm
Inhibited by light
Enhanced by darkness
Strong antioxidant activity
Exogenous melatonin causes rapid induction of sleep without sedation
Peak serum concentration reached in about 60 minutes
Concentration declines within 4 hours

## Slide 31: Advances in Pediatric Hearing Assessment with the Audito ry Brainstem Response Melatonin is Used to Induce Sleep in Medicine
Management of a variety of diseases and disordera
Management of bothersome tinnitus
Complimentary use during anesthesia
Imaging studies
  CT scans
  Magnetic resonance imaging (MRI)
Electrophysiological studies
  EEG studies
  Sensory evoked responses … including ABR

## Slide 32: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Melatonin in Pediatric ABR Measurement
Schmidt et al. Melatonin is a useful alternative to sedation in children undergoing brainstem audiometry with an age dependent success rate: A field report of 250 investigations. Neuropediatrics 38: 2-4, 2007.
Guerlain et al (2016). Efficiency of melatonin as compared to pentobarbital for audiometry brainstem response in children with associated disorders. American Journal of Audiology, 25, 206-210, 2016
Casteil et al (2017). Study of the efficacy of melatonin for auditory brainstem response (ABR) testing in children. Eur Ann Otorhinolaryngol Head Neck Dis, pii: S1879-7296(17)30075-3. doi: 10.1016/j.anorl.2017.03.006. [Epub ahead of print]

## Slide 33: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response Melatonin in Pediatric ABR Measurement

## Slide 34: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response (ABR)
Review of ABR anatomy and physiology … the ABR is NOT a test of hearing
Pediatric applications of ABR measurement
Four advances in pediatric hearing assessment with ABR
  Chirp stimuli (click and tone burst)
  The B-81 oscillator for bone conduction ABR measurement
  Options for un-sedated ABR measurement
  Efficient ABR measurement in < 30 minutes
Kindle Direct Publishing (www.amazon.com) 2015

## Slide 35: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response (ABR) Rationale for Efficient ABR Assessment
ABR assessment includes multiple stimulus conditions for two ears
  Air conduction clicks
  Bone conduction clicks (as needed)
  Multiple tone burst frequencies (3 or 4 per ear)
ABR measurement with natural sleep is feasible if the total test time is < 30 minutes
Sedation or anesthesia is typically not required
ABR assessment can be performed in the audiology clinic rather than a remote location (e.g., hospital clinic or operating room)
All necessary information can be obtained in one test session
  More convenient for family
  Timely test results for more prompt management

## Slide 36
Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response
Frequency-Specific Estimation of Auditory Thresholds

## Slide 37: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response (ABR) How to Complete an ABR Assessment in < 30 Minutes
Develop an ABR test strategy in advance based on available information
Take all possible steps to enhance a sleep state
Use chirp stimuli
Use fast stimulus presentation rates
  Click stimuli: ~ 21.1/sec
  Tone burst stimuli: ~ 37.7/sec
Discontinue the averaging process when SNR reaches 3:1 (ABR amplitude is three times higher than background activity)
Replicate ABR waveforms only for the initial high intensity level and the estimated threshold level
Decrease stimulus intensity in 40 dB steps if ABR appears normal at a high intensity level
Notes: Ta

## Slide 38: Evidence-Based ABR Protocol for Infant Hearing Assessment What is the Optimal Stimulus Presentation Rate? Run Your ABR at the Stimulus Speed Limit
General Guideline: Fastest rate that still produces an optimal response
Click stimulus: 21.1/sec
  Extensive normative data for latency
  Slow enough to identify wave I
  Fast enough for rapid data collection
  Odd number not in sync with 50 Hz or 60 Hz current
Tone burst stimulus: 37.7/sec
  Quicker test time
  Not interested in wave I
  No negative impact of rate increase on waveform morphology

## Slide 39
Signal-to-noise ratio (SNR) =
Signal Amplitude X Number of Averages
_______________________________
Noise Amplitude
where Signal = ABR and
Noise = any electrical activity that is NOT ABR
Adequate SNR = 3
(ABR wave V is 3 times larger than residual background noise)
The Optimal Number of Stimuli (Signal Averages) … Just Enough
The Number That Produces an ABR to Noise Ratio (SNR) of 3:1

## Slide 40: The Optimal Number of Stimuli (Signal Averages) (British NHS Guidelines, 2013)

## Slide 41: Advances in Pediatric Hearing Assessment with the Auditory Brainstem Response (ABR)