SCO-011

product data

SCO-011 is a general purpose synthetic metal working fluid.  It is recommended for use with most ferrous metal grinding, machining and sawing operations.  It combines effective cooling, corrosion inhibition and excellent lubrication.

SCO-011 promotes longer tool life.  Its non-emulsifying characteristics enables the easy skimming of any foreign oil or residue (i.e. tramp oils from sump tank).  Its high-soiled contents enable SCO-011 to work on hard metals under elevated pressures.

This synthetic metal working fluid leaves no residue and is easier to clean than the standard oil soluble products.  It is completely water soluble and biodegradable.  Its synthetic nature and active biocide enables SCO-011 to be used for long periods of time without rancidness.

Typical Properties

Appearance					Blue-Green

Density					8.79 lbs./gal.

Specific Gravity				1.054

pH						9.0-9.5

Viscosity @ 77 deg. F				105 S.U.S.

Flash Point					>210 deg. F

Application

General Machining and Sawing		Dilute 20:1

Grinding					Dilute 40:1

Packaging

5 Gallon Buckets

55 Gallon Drums

275 Gallon Totes