## Slide 1: BitStone Energy
Product Series and Datasheet
Powered by HEGATECH

## Slide 2
Part One
Product Series
Part Two
Part Three
Part Four
CONTENTS
solar module Datasheet
Inverter Datasheet (HV)
Battery Datasheet (HV)

## Slide 3: Product Series
 |  |  |  |  |  |  | System Upgrade | Basic | Essential | Plus | Luxery | Premium
Product Series | Total kwp | Number of Panels | Panel Brand | Panel Type | Inverter | Max. kwp | Max Panels | Battery | Battery | Battery | Battery | Battery
BSLV486 | 4.86 | 12 | HEGATECH | HGT-S108¦M10H-XXX-BG | SUN-5K-SG04LP3-EU | 7.5 | 19 | N/A | 10kwh | 15kwh | 20kwh | 30kwh
BSLV648 | 6.48 | 16 | HEGATECH | HGT-S108¦M10H-XXX-BG | SUN-5K-SG04LP3-EU | 7.5 | 19 | N/A | 10kwh | 15kwh | 20kwh | 30kwh
BSLV729 | 7.29 | 18 | HEGATECH | HGT-S108¦M10H-XXX-BG | SUN-6K-SG04LP3-EU | 9.0 | 22 | N/A | 10kwh | 15kwh | 10kwh | 30kwh
BSHV729 | 7.29 | 18 | HEGATECH | HGT-S108¦M10H-XXX-BG | SUN-6K-SG01HP3-EU-AM2 | 9.0 | 22 | N/A | 8kwh | 12kwh | 20kwh | 24kwh
BSHV1053 | 10.53 | 26 | HEGATECH | HGT-S108¦M10H-XXX-BG | SUN-8k-SG01HP3-EU-AM2 | 12.0 | 30 | N/A | 8kwh | 12kwh | 20kwh | 24kwh
BSHV1296 | 12.96 | 32 | HEGATECH | HGT-S108¦M10H-XXX-BG | SUN-10K-SG01HP3-EU-AM2 | 15.0 | 37 | N/A | 8kwh | 12kwh | 20kwh | 24kwh
BSHV1620 | 15.39 | 38 | HEGATECH | HGT-S108¦M10H-XXX-BG | SUN-12k-SG01HP3-EU-AM2 | 18.0 | 44 | N/A | 8kwh | 12kwh | 20kwh | 24kwh
BSHV1944 | 19.44 | 48 | HEGATECH | HGT-S108¦M10H-XXX-BG | SUN-15K-SG01HP3-EU-AM2 | 22.5 | 56 | N/A | 8kwh | 12kwh | 20kwh | 24kwh
BSHV2430 | 25.92 | 64 | HEGATECH | HGT-S108¦M10H-XXX-BG | SUN-20K-SG01HP3-EU-AM2 | 30.0 | 74 | N/A | 8kwh | 12kwh | 20kwh | 24kwh

## Slide 4: BS Redsdential PV power system
QUALIFIED ORIGINAL COMPONENTS
PROFESSIONAL FULL SYSTEM DESIGN
RELIABLE DELIVERY
LONG TERM AFTER-SALE SERVICE
FULL PV POWER SYSTEM VALUE CHAIN
Deye Inverter
HEGA MODULE
DEYE Energy
Storage System

## Slide 5: BS Home PV System 4.86W
48
100
108 Cells
410W
12 pics
1722 x 1134 x 30 mm
Mono MBB cell solar module
Output power
Numbers of modules
Dimensions (L x W x T)
Redsdential PV Power System-BSLV486
4.86W
Higher Bifacial Dual Glass Module
Takes 182 mm silicon wafer with the power to 410W
More suitable for inslalled capacity.
Mature MBB technology, enabing lower curent loss;
Lower temperature coefficient, to bring with higher power generation.
Innovative high tech & half cut
Original Quality Assurance
Stringent quality control system;Professional design qualification,safe and reliable
After-sales service
PV smart cloud platform monitoring; Big data analysis,speedy service
HGT-S108|M10H-410-BG
HGT Bifacial Dual Glass Module
Deye Three Phase Hybrid Inverter - 5kW
SUN-5K-SG04LP3-EU
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multiple batteries parallel
240
Max. charging/discharging current of 240A
48V low voltage battery, transformer isolation design
6
6 time periods for battery charging/discharging

## Slide 6: BS Home PV System 6.48W
48
100
108 Cells
410W / 21.0%
16 pics
1722 x 1134 x 30 mm
Mono MBB cell solar module
Output power / Enfficiency
Numbers of modules
Dimensions (L x W x T)
Redsdential PV Power System-BSLV648
6.48W
Higher Bifacial Dual Glass Module
Takes 182 mm silicon wafer with the power to 410W
More suitable for inslalled capacity.
Mature MBB technology, enabing lower curent loss;
Lower temperature coefficient, to bring with higher power generation.
Innovative high tech & half cut
Original Quality Assurance
Stringent quality control system;Professional design qualification,safe and reliable
After-sales service
PV smart cloud platform monitoring; Big data analysis,speedy service
HGT-S108|M10H-410-BG
HGT Bifacial Dual Glass Module
Deye Three Phase Hybrid Inverter - 5kW
SUN-5K-SG04LP3-EU
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multiple batteries parallel
240
Max. charging/discharging current of 240A
48V low voltage battery, transformer isolation design
6
6 time periods for battery charging/discharging

## Slide 7: BS Home PV System 7.29W
48
100
108 Cells
410W / 21.0%
18 pics
1722 x 1134 x 30 mm
Mono MBB cell solar module
Output power / Enfficiency
Numbers of modules
Dimensions (L x W x T)
Redsdential PV Power System-BSLV729
7.29W
Higher Bifacial Dual Glass Module
Takes 182 mm silicon wafer with the power to 410W
More suitable for inslalled capacity.
Mature MBB technology, enabing lower curent loss;
Lower temperature coefficient, to bring with higher power generation.
Innovative high tech & half cut
Original Quality Assurance
Stringent quality control system;Professional design qualification,safe and reliable
After-sales service
PV smart cloud platform monitoring; Big data analysis,speedy service
HGT-S108|M10H-410-BG
HGT Bifacial Dual Glass Module
Deye Three Phase Hybrid Inverter - 6kW
SUN-6K-SG04LP3-EU
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multiple batteries parallel
240
Max. charging/discharging current of 240A
48V low voltage battery, transformer isolation design
6
6 time periods for battery charging/discharging

## Slide 8: BS Home PV System 10.53W
48
100
108 Cells
410W / 21.0%
26 pics
1722 x 1134 x 30 mm
Mono MBB cell solar module
Output power / Enfficiency
Numbers of modules
Dimensions (L x W x T)
Redsdential PV Power System-BSHV1053
10.53W
Higher Bifacial Dual Glass Module
Takes 182 mm silicon wafer with the power to 410W
More suitable for inslalled capacity.
Mature MBB technology, enabing lower curent loss;
Lower temperature coefficient, to bring with higher power generation.
Innovative high tech & half cut
Original Quality Assurance
Stringent quality control system;Professional design qualification,safe and reliable
After-sales service
PV smart cloud platform monitoring; Big data analysis,speedy service
HGT-S108|M10H-410-BG
HGT Bifacial Dual Glass Module
Deye Three Phase Hybrid Inverter - 8kW
UN-8k-SG01HP3-EU-AM2
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multiple batteries parallel
240
Max. charging/discharging current of 240A
48V low voltage battery, transformer isolation design
6
6 time periods for battery charging/discharging

## Slide 9: BS Home PV System 12.96W
48
100
108 Cells
410W / 21.0%
32 pics
1722 x 1134 x 30 mm
Mono MBB cell solar module
Output power / Enfficiency
Numbers of modules
Dimensions (L x W x T)
Redsdential PV Power System-BSHV1296
12.96W
Higher Bifacial Dual Glass Module
Takes 182 mm silicon wafer with the power to 410W
More suitable for inslalled capacity.
Mature MBB technology, enabing lower curent loss;
Lower temperature coefficient, to bring with higher power generation.
Innovative high tech & half cut
Original Quality Assurance
Stringent quality control system;Professional design qualification,safe and reliable
After-sales service
PV smart cloud platform monitoring; Big data analysis,speedy service
HGT-S108|M10H-410-BG
HGT Bifacial Dual Glass Module
Deye Three Phase Hybrid Inverter - 10kW
SUN-10K-SG01HP3-EU-AM2
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multiple batteries parallel
240
Max. charging/discharging current of 240A
48V low voltage battery, transformer isolation design
6
6 time periods for battery charging/discharging

## Slide 10: BS Home PV System 15.39W
48
100
108 Cells
410W / 21.0%
38 pics
1722 x 1134 x 30 mm
Mono MBB cell solar module
Output power / Enfficiency
Numbers of modules
Dimensions (L x W x T)
Redsdential PV Power System-BSHV1539
15.39W
Higher Bifacial Dual Glass Module
Takes 182 mm silicon wafer with the power to 410W
More suitable for inslalled capacity.
Mature MBB technology, enabing lower curent loss;
Lower temperature coefficient, to bring with higher power generation.
Innovative high tech & half cut
Original Quality Assurance
Stringent quality control system;Professional design qualification,safe and reliable
After-sales service
PV smart cloud platform monitoring; Big data analysis,speedy service
HGT-S108|M10H-410-BG
HGT Bifacial Dual Glass Module
Deye Three Phase Hybrid Inverter - 12kW
SUN-12K-SG04LP3-EU
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multiple batteries parallel
240
Max. charging/discharging current of 240A
48V low voltage battery, transformer isolation design
6
6 time periods for battery charging/discharging

## Slide 11: BS Home PV System 19.44W
H
100
108 Cells
410W / 21.0%
48 pics
1722 x 1134 x 30 mm
Mono MBB cell solar module
Output power / Enfficiency
Numbers of modules
Dimensions (L x W x T)
Redsdential PV Power System-BSHV1944
19.44W
Higher Bifacial Dual Glass Module
Takes 182 mm silicon wafer with the power to 410W
More suitable for inslalled capacity.
Mature MBB technology, enabing lower curent loss;
Lower temperature coefficient, to bring with higher power generation.
Innovative high tech & half cut
Original Quality Assurance
Stringent quality control system;Professional design qualification,safe and reliable
After-sales service
PV smart cloud platform monitoring; Big data analysis,speedy service
HGT-S108|M10H-410-BG
HGT Bifacial Dual Glass Module
Deye Three Phase Hybrid Inverter - 15kW
SUN-15K-SG01HP3
-EU-AM2
100% unbalanced output, each phase
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multiple batteries parallel
50
Max. charging/discharging current of 50A
High voltage battery, higher efﬁciency
6
6 time periods for battery charging/discharging

## Slide 12: BS Home PV System 24.30W
H
100
108 Cells
410W / 21.0%
64 pics
1722 x 1134 x 30 mm
Mono MBB cell solar module
Output power / Enfficiency
Numbers of modules
Dimensions (L x W x T)
Redsdential PV Power System-BSHV2430
24.30W
Higher Bifacial Dual Glass Module
Takes 182 mm silicon wafer with the power to 410W
More suitable for inslalled capacity.
Mature MBB technology, enabing lower curent loss;
Lower temperature coefficient, to bring with higher power generation.
Innovative high tech & half cut
Original Quality Assurance
Stringent quality control system;Professional design qualification,safe and reliable
After-sales service
PV smart cloud platform monitoring; Big data analysis,speedy service
HGT-S108|M10H-410-BG
HGT Bifacial Dual Glass Module
Deye Three Phase Hybrid Inverter - 20kW
SUN-20K-SG01HP3-EU-AM2
100% unbalanced output, each phase
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multiple batteries parallel
50
Max. charging/discharging current of 50A
High voltage battery, higher efﬁciency
6
6 time periods for battery charging/discharging

## Slide 13: SOLAR MODULE
HGT Bifacial Dual Glass Module-182mm
410W
21.0%
0~+5W
Module Efficiency
Power Tolerance
bifacial dual glass half cut cell technology
ELECTRICAL DATA (STC) | 
Maximum Power (Pmax) | 410W
Maximum Power Voltage (Vmp) | 31.6V
Maximum Power Current (Imp) | 12.98A
Open Circuit Voltage (Voc) | 37.5V
Short Circuit Curren | 13.88A
Efficiency m(%) | 21.0%
ELECTRICAL DATA (NMOT) | 
Maximum Power (Pmax) | 302W
Maximum Power Voltage (Vmp) | 29.18V
Maximum Power Current (Imp) | 10.35A
Open Circuit Voltage (Voc) | 37.5V
Short Circuit Curren | 13.88A
MECHANICAL DATA | 
No.of cells | 108 cells (6x18)
Module Dimensions | 1722 × 1134 × 30 mm
Weight | 21 kg
Glass | 2.0+2.0 mm , High Transmission, AR Coated Heat Strengthened Glass
Encapsulant Material | EVA
Frame | Anodized Aluminium Alloy (silver/balck)
J-Box | IP 68 rated（3 bypass diodes）
Cables | 4.0mm , cable length +350mm/-350mm or customized length
Connector | MC4 Compatible
WARRANTY
12 year Product Workmanship Warranty
30 year Power Warranty
2% first year degradation
0.45% Annual Power Attenuation
PACKAGING CONFIGURATION | 
Pieces per pallet | 36
Pallets per container | 26
Pieces per container 40’HC | 936
Packaging box dimensions | 1770x1120x1270mm
Packaging box weight | 795kg

## Slide 14: Three Phase Hybrid Inverter
SUN-5K-SG04LP3-EU
48
100
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multi-batteries parallel
240
Max. charging/discharging current of 240A
48V low voltage battery, transformer isolation design
6
6 time periods for battery charging/discharging
Model | SUN-5K-SG04LP3-EU
Battery Input Data | 
Battery Type | Lead-acid or Lithium-ion
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 120
Max. Discharging Current (A) | 120
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-adaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 6500
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Technical Data
Model | SUN-5K-SG04LP3-EU
Battery Input Data | 
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 120
Max. Discharging Current (A) | 120
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-aadaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 6500
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Model | SUN-5K-SG04LP3-EU
AC Output Data | 
Rated AC Output Active Power (W) | 5000
Max AC Output Active Power (W) | 5500
AC Output Rated Current (A) | 7.6/7.2
Max AC Output Current (A) | 8.4/8
Max. Three-phase Unbalanced Output Current (A) | 11.4/10.9
Max Output short circuit current (A) | 75
Max. Continuous AC Passthrough (A) | 45
Peak Power (off grid) | 2 time of rated power, 10 S
Power Factor Adjustment Range | 0.8 leading to 0.8 lagging
Rated Input/Output Voltage/Range(V) | 220/380, 230/400 0.85Un-1.1Un
Rated Input/Output Grid Frequency/Range | 50Hz/45Hz-55Hz 60Hz/55Hz-65Hz
Grid Connection Form | 3L+N+PE
Total Harmonics Current Distortion (THDi) | <3% (of nominal power)
DC Current Injection | <0.5% In

## Slide 15: Three Phase Hybrid Inverter
SUN-6K-SG04LP3-EU
48
100
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multi-batteries parallel
240
Max. charging/discharging current of 240A
48V low voltage battery, transformer isolation design
6
6 time periods for battery charging/discharging
Model | SUN-6K-SG04LP3-EU
Battery Input Data | 
Battery Type | Lead-acid or Lithium-ion
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 150
Max. Discharging Current (A) | 150
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-adaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 7800
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Technical Data
Model | SUN-5K-SG04LP3-EU
Battery Input Data | 
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 120
Max. Discharging Current (A) | 120
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-aadaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 6500
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Model | SUN-6K-SG04LP3-EU
AC Output Data | 
Rated AC Output Active Power (W) | 6000
Max AC Output Active Power (W) | 6600
AC Output Rated Current (A) | 9.1/8.7
Max AC Output Current (A) | 10/9.6
Max. Three-phase Unbalanced Output Current (A) | 13.6/13
Max Output short circuit current (A) | 75
Max. Continuous AC Passthrough (A) | 45
Peak Power (off grid) | 2 time of rated power, 10 S
Power Factor Adjustment Range | 0.8 leading to 0.8 lagging
Rated Input/Output Voltage/Range(V) | 220/380, 230/400 0.85Un-1.1Un
Rated Input/Output Grid Frequency/Range | 50Hz/45Hz-55Hz 60Hz/55Hz-65Hz
Grid Connection Form | 3L+N+PE
Total Harmonics Current Distortion (THDi) | <3% (of nominal power)
DC Current Injection | <0.5% In

## Slide 16: Three Phase Hybrid Inverter
SUN-6K-SG01HP3-EU-AM2
H
100
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multi-batteries parallel
50
Max. charging/discharging current of 50A
High voltage battery, higher efﬁciency
6
6 time periods for battery charging/discharging
Model | SUN-6K-SG01HP3-EU-AM2
Battery Input Data | 
Battery Type | Lithium-ion
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 150
Max. Discharging Current (A) | 150
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-adaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 7800
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Technical Data
Model | SUN-5K-SG04LP3-EU
Battery Input Data | 
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 120
Max. Discharging Current (A) | 120
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-aadaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 6500
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Model | SUN-6K-SG01HP3- EU-AM2
AC Output Data | 
Rated AC Output Active Power (W) | 6000
Max AC Output Active Power (W) | 6600
AC Output Rated Current (A) | 9.1/8.7
Max AC Output Current (A) | 10/9.6
Max. Three-phase Unbalanced Output Current (A) | 13.6/13
Max Output short circuit current (A) | 75
Max. Continuous AC Passthrough (A) | 45
Peak Power (off grid) | 2 time of rated power, 10 S
Power Factor Adjustment Range | 0.8 leading to 0.8 lagging
Rated Input/Output Voltage/Range(V) | 220/380, 230/400 0.85Un-1.1Un
Rated Input/Output Grid Frequency/Range | 50Hz/45Hz-55Hz 60Hz/55Hz-65Hz
Grid Connection Form | 3L+N+PE
Total Harmonics Current Distortion (THDi) | <3% (of nominal power)
DC Current Injection | <0.5% In

## Slide 17: Three Phase Hybrid Inverter
SUN-8K-SG01HP3-EU-AM2
H
100
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multi-batteries parallel
50
Max. charging/discharging current of 50A
High voltage battery, higher efﬁciency
6
6 time periods for battery charging/discharging
Model | SUN-8K-SG04LP3-EU
Battery Input Data | 
Battery Type | Lithium-ion
Battery Voltage Range (V) | 160-700
Max. Charging Current (A) | 37
Max. Discharging Current (A) | 37
Number of Battery Input | 1
Charging Strategy for Li-Ion Battery | Self-adaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 10400
Max. DC Input Voltage (V) | 1000
Start-up Voltage (V) | 180
MPPT Range (V) | 150-850
Full Load DC Voltage Range (V) | 260-850
Rated DC Input Voltage (V) | 600
PV Input Current (A) | 20+20
Max. PV ISC (A) | 30+30
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Technical Data
Model | SUN-5K-SG04LP3-EU
Battery Input Data | 
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 120
Max. Discharging Current (A) | 120
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-aadaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 6500
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Model | SUN-8K-SG04LP3-EU
AC Output Data | 
Rated AC Output Active Power (W) | 8000
Max AC Output Active Power (W) | 8800
AC Output Rated Current (A) | 12.2/11.6
Max AC Output Current (A) | 13.4/12.8
Max. Three-phase Unbalanced Output Current (A) | 18
Max. Continuous AC Passthrough (A) | 40
Peak Power (off grid) | 1.5 time of rated power, 10 S
Power Factor Adjustment Range | 0.8 leading to 0.8 lagging
Rated Input/Output Voltage/Range(V) | 220/380, 230/400 0.85Un-1.1Un
Rated Input/Output Grid Frequency/Range | 50Hz/45Hz-55Hz 60Hz/55Hz-65Hz
Grid Connection Form | 3L+N+PE
Total Harmonics Current Distortion (THDi) | <3% (of nominal power)
DC Current Injection | <0.5% In

## Slide 18: Three Phase Hybrid Inverter
SUN-10K-SG01HP3-EU-AM2
100
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multi-batteries parallel
6
6 time periods for battery charging/discharging
Model | SUN-10K-SG01HP3-EU-AM2
Battery Input Data | 
Battery Type | Lithium-ion
Battery Voltage Range (V) | 160-700
Max. Charging Current (A) | 37
Max. Discharging Current (A) | 37
Number of Battery Input | 1
Charging Strategy for Li-Ion Battery | Self-adaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 13000
Max. DC Input Voltage (V) | 1000
Start-up Voltage (V) | 180
MPPT Voltage Range (V) | 150-850
Full Load DC Voltage Range (V) | 325-850
Rated DC Input Voltage (V) | 600
PV Input Current (A) | 20+20
Max. PV ISC (A) | 30+30
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Technical Data
Model | SUN-5K-SG04LP3-EU
Battery Input Data | 
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 120
Max. Discharging Current (A) | 120
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-aadaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 6500
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Model | SUN-10K-SG01HP3- EU-AM2
AC Output Data | 
Rated AC Output Active Power (W) | 10000
Max AC Output Active Power (W) | 11000
AC Output Rated Current (A) | 15.2/14.5
Max AC Output Current (A) | 16.7/16
Max. Three-phase Unbalanced Output Current (A) | 22
Max. Continuous AC Passthrough (A) | 40
Peak Power (off grid) | 1.5 time of rated power, 10 S
Power Factor Adjustment Range | 0.8 leading to 0.8 lagging
Rated Input/Output Voltage/Range(V) | 220/380, 230/400 0.85Un-1.1Un
Rated Input/Output Grid Frequency/Range | 50Hz/45Hz-55Hz 60Hz/55Hz-65Hz
Grid Connection Form | 3L+N+PE
Total Harmonics Current Distortion (THDi) | <3% (of nominal power)
DC Current Injection | <0.5% In
H
50
Max. charging/discharging current of 50A
High voltage battery, higher efﬁciency

## Slide 19: Three Phase Hybrid Inverter
SUN-12K-SG01HP3-EU-AM2
100
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multi-batteries parallel
6
6 time periods for battery charging/discharging
Model | SUN-12K-SG01HP3-EU-AM2
Battery Input Data | 
Battery Type | Lithium-ion
Battery Voltage Range (V) | 160-700
Max. Charging Current (A) | 37
Max. Discharging Current (A) | 37
Number of Battery Input | 1
Charging Strategy for Li-Ion Battery | Self-adaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 15600
Max. DC Input Voltage (V) | 1000
Start-up Voltage (V) | 180
MPPT Voltage Range (V) | 150-850
Full Load DC Voltage Range (V) | 340-850
Rated DC Input Voltage (V) | 600
PV Input Current (A) | 26+20
Max. PV ISC (A) | 39+30
No.of MPP Trackers | 2+1
No.of Strings per MPP Tracker | 2+1
Technical Data
Model | SUN-5K-SG04LP3-EU
Battery Input Data | 
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 120
Max. Discharging Current (A) | 120
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-aadaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 6500
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Model | SUN-12K-SG01HP3- EU-AM2
AC Output Data | 
Rated AC Output Active Power (W) | 12000
Max AC Output Active Power (W) | 13200
AC Output Rated Current (A) | 18.2/17.4
Max AC Output Current (A) | 20/19.2
Max. Three-phase Unbalanced Output Current (A) | 25
Max. Continuous AC Passthrough (A) | 80
Peak Power (off grid) | 1.5 time of rated power, 10 S
Power Factor Adjustment Range | 0.8 leading to 0.8 lagging
Rated Input/Output Voltage/Range(V) | 220/380, 230/400 0.85Un-1.1Un
Rated Input/Output Grid Frequency/Range | 50Hz/45Hz-55Hz 60Hz/55Hz-65Hz
Grid Connection Form | 3L+N+PE
Total Harmonics Current Distortion (THDi) | <3% (of nominal power)
DC Current Injection | <0.5% In
H
50
Max. charging/discharging current of 50A
High voltage battery, higher efﬁciency

## Slide 20: Three Phase Hybrid Inverter
SUN-15K-SG01HP3-EU-AM2
H
100
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multi-batteries parallel
50
Max. charging/discharging current of 50A
High voltage battery, higher efﬁciency
6
6 time periods for battery charging/discharging
Model | SUN-15K-SG01HP3-EU-AM2
Battery Input Data | 
Battery Type | Lithium-ion
Battery Voltage Range (V) | 160-700
Max. Charging Current (A) | 37
Max. Discharging Current (A) | 37
Number of Battery Input | 1
Charging Strategy for Li-Ion Battery | Self-adaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 19500
Max. DC Input Voltage (V) | 1000
Start-up Voltage (V) | 180
MPPT Range (V) | 150-850
Full Load DC Voltage Range (V) | 420-850
Rated DC Input Voltage (V) | 600
PV Input Current (A) | 26+20
Max. PV ISC (A) | 39+30
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 2+1
Technical Data
Model | SUN-5K-SG04LP3-EU
Battery Input Data | 
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 120
Max. Discharging Current (A) | 120
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-aadaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 6500
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Model | SUN-15K-SG01HP3-EU-AM2
AC Output Data | 
Rated AC Output Active Power (W) | 15000
Max AC Output Active Power (W) | 16500
AC Output Rated Current (A) | 22.8/21.8
Max AC Output Current (A) | 25/24
Max. Three-phase Unbalanced Output Current (A) | 30
Max. Continuous AC Passthrough (A) | 80
Peak Power (off grid) | 1.5 time of rated power, 10 S
Power Factor Adjustment Range | 0.8 leading to 0.8 lagging
Rated Input/Output Voltage/Range(V) | 220/380, 230/400 0.85Un-1.1Un
Rated Input/Output Grid Frequency/Range | 50Hz/45Hz-55Hz 60Hz/55Hz-65Hz
Grid Connection Form | 3L+N+PE
Total Harmonics Current Distortion (THDi) | <3% (of nominal power)
DC Current Injection | <0.5% In

## Slide 21: Three Phase Hybrid Inverter
SUN-20K-SG01HP3-EU-AM2
H
100
100% unbalanced output, each phase; Max. output up to 50% rated power
AC couple to retrofit existing solar system
10
Max.10 pcs parallel for on and off-grid operation; Support multi-batteries parallel
50
Max. charging/discharging current of 50A
High voltage battery, higher efﬁciency
6
6 time periods for battery charging/discharging
Model | SUN-20K-SG01HP3-EU-AM2
Battery Input Data | 
Battery Type | Lithium-ion
Battery Voltage Range (V) | 160-700
Max. Charging Current (A) | 37
Max. Discharging Current (A) | 37
Number of Battery Input | 1
Charging Strategy for Li-Ion Battery | Self-adaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 26000
Max. DC Input Voltage (V) | 1000
Start-up Voltage (V) | 180
MPPT Range (V) | 150-850
Full Load DC Voltage Range (V) | 500-850
Rated DC Input Voltage (V) | 600
PV Input Current (A) | 26+26
Max. PV ISC (A) | 39+39
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 2+2
Technical Data
Model | SUN-5K-SG04LP3-EU
Battery Input Data | 
Battery Voltage Range (V) | 40-60
Max. Charging Current (A) | 120
Max. Discharging Current (A) | 120
External Temperature Sensor | yes
Charging Curve | 3 Stages / Equalization
Charging Strategy for Li-Ion Battery | Self-aadaption to BMS
PV String Input Data | 
Max. DC Input Power (W) | 6500
Rated PV Input Voltage (V) | 550 (160-800)
Start-up Voltage (V) | 160
MPPT Voltage Range (V) | 200-650
Full Load DC Voltage Range (V) | 350-650
PV Input Current (A) | 13+13
Max. PV ISC (A) | 17+17
No.of MPP Trackers | 2
No.of Strings per MPP Tracker | 1+1
Model | SUN-20K-SG01HP3-EU-AM2
AC Output Data | 
Rated AC Output Active Power (W) | 20000
Max AC Output Active Power (W) | 22000
AC Output Rated Current (A) | 30.4/29
Max AC Output Current (A) | 33.4/31.9
Max. Three-phase Unbalanced Output Current (A) | 35
Max. Continuous AC Passthrough (A) | 80
Peak Power (off grid) | 1.5 time of rated power, 10 S
Power Factor Adjustment Range | 0.8 leading to 0.8 lagging
Rated Input/Output Voltage/Range(V) | 220/380, 230/400 0.85Un-1.1Un
Rated Input/Output Grid Frequency/Range | 50Hz/45Hz-55Hz 60Hz/55Hz-65Hz
Grid Connection Form | 3L+N+PE
Total Harmonics Current Distortion (THDi) | <3% (of nominal power)
DC Current Injection | <0.5% In

## Slide 22: DEYE Energy Storage System
Type: GB-L
Structural safety
Meet high seismic grade zone 4.
High-voltage stack
Modules are connected in series without cable connection,
and high-voltage platform improves system eﬃciency.
Thermal management
Temperature detection of key parts, cell, power plug-in, etc.
Wide temperature operation
The heating function is optional to meet the application
scenarios with low temperature and no sense.
Environmental friendliness
IP protection grade 65, anti-corrosion grade ≥C2,
environmental protection battery.
Intelligent and visual
Support remote upgrade, real-time battery warning
information push,LCD data display.
Main Parameter |  |  |  |  |  | 
Cell Chemistry |  | LiFePO4 |  |  |  | 
Module Energy (kWh) |  | 4.09 |  |  |  | 
Module Nominal Voltage (V) |  | 102.4 |  |  |  | 
Module Capacity (Ah)) |  | 40 |  |  |  | 
Battery Module Qty In Series (Optional) |  | 2 | 3 | 4 | 5 | 6
System Nominal Voltage (V) |  | 204.8 | 307.2 | 409.6 | 512 | 614.4
System Operating voltage(V) |  | 179.2~691.2 |  |  |  | 
System Energy (kWh) |  | 8.18 | 12.27 | 16.36 | 20.45 | 24.56
System Usable Energy (kWh) |  | 7.36 | 11.04 | 14.72 | 18.40 | 22.10
Charge/Discharge Current (A) | Recommend | 20 |  |  |  | 
 | Max | 40 |  |  |  | 
 | Peak Discharge (2mins,25°C) | 50 |  |  |  | 
Working Temperature (°C) |  | Charge:0~55/Discharge:-20~55 |  |  |  | 
LCD Display |  | SOC%,Power,Total Voltage |  |  |  | 
Communication Port |  | CAN2.0, RS485 |  |  |  | 
Humidity |  | 5%~90% |  |  |  | 
Altitude |  | ≤2000m |  |  |  | 
IP Rating of Enclosure |  | IP65 |  |  |  | 
Storage Temperature (°C) |  | 0~35 |  |  |  | 
Dimension (W/D/H,mm) |  | 540*385* 650 | 540*385* 870 | 540*385*1090 | 540*385*1310 | 540*385* 1530
Weight(kg) |  | 76 | 108 | 140 | 172 | 204
Installation Location |  | Floor Mount |  |  |  | 
Recommend Depth of Discharge |  | 90% |  |  |  | 
Cycle Life |  | 25±2,0.5C/0.5C, EOL70%≥6000 |  |  |  | 
Warranty |  | 10 years |  |  |  | 
Certiﬁcation |  | CE, IEC62619, VDE2510-50, UKCA, UN38.3 |  |  |  | 
Technical Data