## Slide 1: Advancing the Diffusive Gradients in Thin-Films Passive Sampling Device for Monitoring PFAS in Drinking Water Systems
Samuel D. Hodges, M.S., E.I.T., Huong T. Pham, Ph.D., and Julian L. Fairey, Ph.D., P.E.
Department of Civil Engineering, University of Arkansas, Fayetteville, AR
David G. Wahman, Ph.D., P.E., and Levi Haupert, Ph.D.
Drinking Water Treatment & Distribution Branch, US Environmental Protection Agency, Cincinnati, OH
Notes: Introduce yourself and lab group “the experimental work contributors” Dave and Levi contributed heavily to the modeling.

## Slide 2
Grab vs. Passive Sampling
Grab sampling  snapshot in time, i.e., PFOA, weekly for 12 weeks
Passive sampling device (PSD)  time-weighted average
PSD does not capture extremes
Fewer PSDs vs. grab samples
  Potential cost savings
PSD more representative of chronic exposures
Notes: If you are targeting any measurement above a threshold, PSD may not be ideal
If you’re looking for chronic exposure could be excellent tool.

## Slide 3
Diffusive Gradients in Thin-Films (DGT)
DGT-PSDs are kinetic samplers (as opposed to equilibrium samplers)
  Longer deployment times  more analyte uptake and lower MDLs
  Analyte mass transport restricted to diffusion through gel layer
  Binding layer maintains maximal diffusive flux with bulk water
Conceptual profile of a DGT-PSD
DGT-PSD with gel layer uplifted by forceps
Diffusive Gel
Gel
Membrane filter (optional)
DBL
DBL
Bulk Water
CBulk
Binding
layer
Housing
CDGT
Diffusion Boundary Layer thickness (𝛿DBL) in-situ
Diffusive gel
  No PFAS sorption
  PFAS diffusion coefficients (DGel)
Rapid and complete PFAS uptake in binding layer
Notes: Summary=Where are we going
Longer deployment = more analyte uptake = lower MDL

## Slide 4
Analyte Diffusion Coefficients in Gel
DGel measured in polyethylene two-compartment diffusion cell
Source
Sink
Diffusive Gels of four thicknesses, 𝛿Gel
0.08 cm
0.12 cm
0.16 cm
0.20 cm
Diffusive Gel
Gel
DBL
DBL
DBL
DBL
Sink
CSink
Source
CSource
CSource
CSink
Used nitrate to determine 𝛿DBL vs. Mixing Speed
  50-, 100-, 200-, 300-, 400-, and 500 RPM experiments
  Identified Mixing Speed for which 𝛿DBL ≪ 𝛿Gel  applied to PFAS DGel measurements
Notes: Summary of the DCell DGel measurement goal
Used gel thickness to vary the expected mass uptake. Values should equate to same concentration, but may be off by a DBL thickness.

## Slide 5
Finite Difference Model (FDM)
Diffusive Gel
DBL
DBL
Source
C1
Sink
q1
0
x
L
C2
L + 𝛿DBL
−𝛿DBL
x1
xN
J1
J2
Δ
Gel
DBL
DBL
  Fick’s first law (conc. gradients)  flux through DBL
  Fick’s second law (conc. gradients in time)  flux through gel
  Initial value problem solved using deSolve package in R
1-dimensional diffusion problem  DGel and 𝛿DBL
  Analyte diffusion from Source to Sink

## Slide 6
Source Compartment Nitrate Profiles
Six mixing speeds
  50–500 RPM
Four gel thicknesses
  0.08–0.20 cm
Replicate tests
  Data replicate
  Simulation replicate
Source Nitrate
  t = 0  10–23 mg•L⁻¹-N
  Decreased <10 % over 200-min test
50 RPM
100 RPM
200 RPM
300 RPM
400 RPM
500 RPM

## Slide 7
Sink Compartment Nitrate Profiles
No Initial Sink Nitrate
  Final: 0.2–0.7 mg•L⁻¹-N
Increased diffusion with decreasing Gel Thickness
  Greater slopes with thinner gels
FDM captures trends
  Time
  Gel thickness
  Mixing speed
50 RPM
100 RPM
200 RPM
300 RPM
400 RPM
500 RPM

## Slide 8
DBL Thickness vs. Mixing Speed
Diffusive Gel
DBL
DBL
Source
C1
Sink
q1
0
x
L
C2
L + 𝛿DBL
−𝛿DBL
x1
xN
J1
J2
Δ
Gel = 0.08–0.20 cm
DBL
FDM fit of nitrate data  𝛿DBL vs. Compartment Mixing Speed
DBL
At 50 RPM
  𝛿DBL = 111 μm
  11–28 % of the total diffusive pathlength
At 500 RPM
  𝛿DBL = 1 μm
  0.1–0.3 % of the total diffusive pathlength
Used 500 RPM mixing speed to measure PFAS diffusion coefficients
  Made the DBL thickness insignificant in the FDM
  Determined DGel for the target PFAS

## Slide 9
Two-compartment diffusion cell tests with PFAS mixtures
  500 RPM Mixing Speed (insignificant DBL thickness)
  Agarose Gel type
  Spiked Source Compartment with 10,000 ng•L⁻¹ of each PFAS
    C4–C14 PFCAs
    C4–C10 PFSAs
    4:2-, 6:2-, 8:2 FTSs; PFOSA; N-EtFOSAA and M-MeFOSAA
Water Chemistry
  pH 5, 7, and 9 > pKa’s of most PFAS  assess gel chemistry
Temperature:
  5 and 22 °C
PFAS Diffusion Coefficients in Gel

## Slide 10
Source Compartment PFAS Profiles
Source Compartment PFAS Concentrations for Agarose Gel (ng/L)
Time (minutes)
Initial PFAS ~10,000 ng/L
Final PFAS ~7,500 ng/L
Captured well by FDM for 19 PFAS
  Poor fits for five PFAS
PFPeS
Notes: 16-25 hrs
40-48 hrs
62-72 hrs

## Slide 11
Sink Compartment PFAS Profiles
No initial PFAS
Final PFAS ~2,500 ng/L
  About one-third of final source
  Diffusive flux varies  FDM
Captured well by FDM for 16 of 24 PFAS
Source Compartment PFAS Concentrations for Agarose Gel (ng/L)
Time (minutes)

## Slide 12
DGel for PFCAs at pH 7 and 22 °C
DGel decreased with increasing chain length
  Expected trend
  PFBA ≅ 7.2×10⁻⁶ cm²•s⁻¹
  PFDA ≅ 4.2×10⁻⁶ cm²•s⁻¹
Reproducibility amongst triplicate tests
  PFHxA ≅ 6.4–6.6×10⁻⁶ cm²•s⁻¹
  PFPeA ≅ 6.9–7.8×10⁻⁶ cm²•s⁻¹
    3–12% variation
    Well within the 30% range commonly attributed to PFAS

## Slide 13
DGel for PFCAs: pH Impact
DGel at pH 7 ≅ DGel at pH 5
Notes: pH drop

## Slide 14
DGel for PFCAs: pH Impact
DGel at pH 7 ≅ DGel at pH 5
  Fang et al. 2021 pH 5.6
Notes: pH increase
Leads to restricted diffusion

## Slide 15
DGel for PFCAs: pH Impact
DGel at pH 7 ≅ DGel at pH 5
  Fang et al. 2021 pH 5.6
DGel at pH 7 ≳ DGel at pH 9
  Similar for PFBA and PFNA
  ~30 % lower for other PFCAs
DGel at pH 9 less than those at pH 5 and 7
  Negative surface charge on agarose at pH 9 restricting diffusion of anionic PFAS?

## Slide 16
DGel for PFCAs: Temperature Impact
DGel at 22 ℃ > DGel at 5 ℃
  Expected result
  Lower at 5 ℃ by 2–3×

## Slide 17
DGel for PFCAs: Temperature Impact
DGel at 22 ℃ < DGel at 5 ℃
  Expected result
  Lower at 5 ℃ by 2–3×
Stokes-Einstein Equation
Captures DGel at 5 ℃ based on values at 22 ℃
Need to deploy temperature logger with DGT-PSDs
  Use Stokes-Einstein to adjust DGel
Notes: Viscoscity

## Slide 18
DGel for PFCAs and PFSAs
PFCAs
PFSAs
Similar DGel for PFCAs and PFSAs
PFAS chain length important
Functional group type less important

## Slide 19
Binding Layer of DGT-PSDs
DGT-PSDs are kinetic samplers
  Measured DGel for 13 PFAS as a function of pH and temperature
  Need binding layer to maintain maximal diffusive flux with bulk water
Conceptual Profile of a DGT-PSD
DGT-PSD with Gel Layer Uplifted by forceps
Diffusive Gel
Gel
Membrane filter (optional)
DBL
DBL
Bulk Water
CBulk
Binding
layer
Housing
CDGT
Assessed Weak Anion Exchange (WAX) and Strong Base Anion (SBA) resins
  PFAS uptake and recovery
  Used best-performing resin in DGT-PSDs
Notes: Summary of the binding layer development

## Slide 20
PFAS Extraction Efficiency from WAX
No PFAS with extraction efficiency ≳ 70 % using MeOH only

## Slide 21
PFAS Extraction Efficiency from WAX
No PFAS with extraction efficiency ≳ 70 % using MeOH only
14 PFAS with extraction efficiency ≳ 70 % using MeOH and 50 μM NH₄OH
Notes: Ammonium Hydroxide

## Slide 22
PFAS Extraction Efficiency from WAX
No PFAS with extraction efficiency ≳ 70 % using MeOH only
14 PFAS with extraction efficiency ≳ 70 % using MeOH and 50 μM NH₄OH
50 μM ammonium acetate and formate good as well
Notes: Ammonium Hydroxide

## Slide 23
PFAS Extraction Efficiency from SBA
8 PFAS with extraction efficiencies ≳ 70 %
Selected WAX resin with MeOH/NH₄OH for PFAS extraction
Notes: Ammonium Hydroxide

## Slide 24
Box Tests with DGT-PSDs
pH 7 and 22 ℃
Spiked Box with the 24 target PFAS, each at ~5,300 ng•L⁻¹ into 750 mL water
Deployment times of 2-, 6-, and 11-days
  Grab samples at start, middle, and end
  Calculated TWA Grab sample for each PFAS
Extracted binding layer after deployment time
  Used DGel values to back-calculate CDGT
  Averaged four DGT-PSDs
Compared PFAS TWA-Grab vs. DGT-PSDs
  Goal of ± 40 %
3D-rendering of 1-L Box (grey) with DGT-PSDs (magenta) installed in each side-wall
Notes: Summary of the box tests
High concentration for initial validation

## Slide 25
Box Tests with DGT-PSDs
2-day test
DGT-Average and TWA-Grab samples within 40 % for five of seven PFCAs
  PFBA, PFPeA, PFHxA, PFOA, PFNA
  DGT-PSDs over-estimated TWA-Grab samples for PFHpA and PFDA
Notes: DON’T LIST THE COMPOUNDS

## Slide 26
Box Tests with DGT-PSDs
6-day test
DGT-Average and TWA-Grab samples within 40 % for four of seven PFCAs
  PFBA, PFPeA, PFHxA, PFNA
  DGT-PSDs over-estimated TWA-Grab samples for PFHpA, PFOA, and PFDA

## Slide 27
Box Tests with DGT-PSDs
11-day test
DGT-Average and TWA-Grab samples within 40 % for four of seven PFCAs
  PFHpA, PFOA, PFNA, PFDA
  DGT-PSDs under-estimated TWA-Grab samples for PFBA, PFPeA, and PFHxA
    Resin at capacity?
    More WAX resin?

## Slide 28
Box Tests with DGT-PSDs
2-, 6-, and 11-day tests
DGT-Average and TWA-Grab samples within 40 % for all seven PFCAs
  13 of 21 PFCA–Deployment Time combinations

## Slide 29
Box Tests with DGT-PSDs
2-, 6-, and 11-day tests
DGT-Average and TWA-Grab samples within 40 % for all six PFSAs
  13 of 18 PFSA–Deployment Time combinations

## Slide 30
Summary of Results to Date
DGT-PSDs are kinetic samplers
  Mass transport to binding layer restricted to molecular diffusion through a thin gel layer
Measured DGel for C4–C10 PFCAs and C4–C9 PFSAs
  Decreased with increasing carbon chain length
  Similar at pH 5 and 7 but ~30 % lower at pH 9  charge on agarose?
  Decreased 2–3× at 5 ℃ compared to 22 ℃  temperature logger
WAX binding layer
  Maximized PFAS extraction efficiency using MeOH with 50 μM NH₄OH
Box experiments with DGT-PSDs
  2-, 6-, and 11-days
  ± 40 % of TWA-Grab samples for majority of the PFAS
Notes: Ammonium Hydroxide

## Slide 31
Next Steps
DGel measurements as a function of conductivity
Box experiments with lower initial PFAS concentration
  500 ng•L⁻¹ (previously 5,300 ng•L⁻¹)
Estimate number of binding sites in the DGT binding layer
  Increase WAX dose in binding layer to overcome capacity limitations and competitive sorption effects

## Slide 32
Strategic Environmental Research and Develop Program (SERDP)
  ER20-1363
Arkansas Water Resources Center (AWRC) student grant to SDH
Acknowledgements and Disclaimer
Research was not performed or funded by EPA and was not subject to EPA’s quality system requirements. Views expressed are those of the authors and do not necessarily represent views or policies of EPA.