## Slide 1: COVE Repeater Association
Serving Copperas Cove
&
Operators throughout Coryell, Bell, Burnet and Lampasas Counties

## Slide 2: Activities and Membership Open to All Hams (and families too…)
VHF and UHF Contacts on Club Repeaters
Monthly Meetings
Social Events
National Field Day Events in Summer and Winter
Repeater maintenance and other technical stuff
Impromptu field set-ups and operations

## Slide 3: K5CRA Club Repeaters
Copperas Cove location with high elevation for widest coverage
  2 meters VHF
    147.26 with a positive offset (+) and a tone of 88.5
    FM Analog and Yaesu System Fusion C4FM Digital
  70 centimeter UHF (Also referred to as the 440 machine)
    443.325 with a positive offset (+) and a tone of 88.5
    FM Analog and Yaesu System Fusion C4FM Digital
  Yaesu System Fusion Digital capable with DR-1X Repeaters for each band
    Set on Automatic Mode Select for FM or Digital
    Transmit in traditional FM and you will hear FM out
    Transmit in new C4FM Digital and you will hear Digital out
Solar Powered battery back-up
Open to all amateur operators

## Slide 4: Helpful Hints on Repeater Operations
What you will hear
  Traditional every day FM vhf contacts between stations
  Contacts using Yaesu digital transmissions
    On a digital radio that is set to digital you will hear a digital voice
    On an FM vhf radio, old school scanner, or digital radio set to FM, you will hear static noise
    On a digital radio set to Auto Mode, the radio will switch to digital and you will hear voice. Auto Mode is the recommended setting for those with digital capable radios.
Breaking in to a Digital communication between stations
  Go to FM, listen for a break and transmit “Break” and the repeater will switch to digital and transmit your “Break.”
  Operators with radios in the preferred Auto Mode will experience the shift back to FM and hear your break in transmission and be able to talk with you.
Turning off the noise from digital operations on an FM VHF radio
  Set your receive mode to tone squelch mode (TSQ on some radios, CT on others) so your receiver will listen for a tone of 88.5 before sound comes out of the speaker. Since digital mode does not send a tone, you will not hear any noise.

## Slide 5: Why System Fusion?
Learning new technology is one of the pleasures of amateur radio.
Can communicate using AM, SSB, PSK, RTTY FM and several digital modes. Yaesu C4FM is one of those digital modes.
One of the benefits of digital communication is the ability to send large amounts of data. So, besides somewhat improved voice communication, other data can be sent along with the voice data:
  Call sign
  Locations and distance between locations
  Speed and tracking
  Those stations on frequency and within range (group monitoring function)
  Weather information
  Images
  Text messages
  Beacon messages

## Slide 6: A Few Quick Questions About Digital
I have no plans to buy a digital radio, so where does that leave me?
  The repeaters operate on traditional FM VHF and UHF and are set in the Auto Mode to switch between FM and Digital as needed. Just transmit on your current into the repeater and it will switch and everyone will hear your transmission as always.
How do I get rid of the noise when someone is operating digital?
  Set your receiver squelch to listen for a tone (88.5) before sending sound to the speaker. The Digital mode does not send a tone when transmitting voice you otherwise hear as noise so your radio won’t play the noise without a tone. Clear as mud? Feel free to ask one of the repeater trustees or other club members for assistance.
Does the digital system get better distance coverage?
  Generally no, it doesn’t. The digital operation requires a fairly strong signal to meet requirements. If the signal drops below a certain point the signal drops. It’s all or nothing. An FM signal may drop below the same cut off point but can continue to be heard in a weak or faint condition. Digital operators who are told their signal cut off may need to increase power, or if mobile, wait for a better or closer location.

## Slide 7: Sources
Cove Repeater Association website:
  https://coverepeaterassociation.shutterfly.com
  Cove Repeater Association on Facebook
A Digital Communications Guide for Amateur Radio Operators, Yaesu Vertex Standard, 2011.

## Slide 8: COVE Repeater Association
Notes:
Prepared for November 2016 Club meeting by Robert KA5VVD, Bruce KD6UY and Brian WH2ACT