## Slide 1
FIBRINOGEN
as
FIB CONCENTRATE
or
CRYOPRECIPITATE
RETEST
RETEST
RETEST
GENERAL SURGICAL / OBSTETRIC HAEMORRHAGE ROTEM & TEG GOAL DIRECTED BLEEDING MANAGEMENT ALGORITHM (2025)
Adjust dose of blood products for patients <50kg after consulting senior clinician
Poor Platelet Contribution
Low Fibrinogen
Low Coagulation Factors or Oral anticoagulants
Hyperfibrinolysis
FIBRINOGEN
PLATELETS
FACTORS
FIBRINOLYSIS
NORMAL
YES
YES
ELP/ FFP
OR
PCC
YES
When clinically possible always complete the algorithm in a stepwise manner and check the ROTEM between steps as indicated. This reduces unnecessary transfusion especially of platelets/ELP/ Beriplex.
PROCEED WITH ALGORITHM
Tranexamic Acid
1 gram
Or 15mg/kg
Clinician discretion for Fibrinogen Concentrate
Usually for massive obstetric haemorrhage or severely low FIBTEM or CFF
YES
CLOT INSTABILITY Early diagnosis | 
EXTEM A5 <35mm | CRT A10 <47mm
Flat line FIBTEM or CRT at 5min | 
NORMAL FIBTEM A5 ≥ 12mm AND IS EXTEM A5 < 35mm? | NORMAL CFF A10 > 15mm AND IS CRT A10 < 47mm?
Or abnormal Multiplate | 
NORMAL FIBTEM A5 ≥ 12mm AND IS EXTEM CT > 85 sec? | NORMAL CFF A10 > 15mm? AND Is CKH-R > 10 minutes
Ensure core temp >36C and Fibrinogen corrected first TEG has no dedicated extrinsic test & cannot detect warfarin | 
PLATELETS
Temp >36 C, pH >7.2, iCalcium >1.1 mmol/L, Platelets >70x109/L, Hb >75 g/L
High risk of Fibrinolysis?
E.g. trauma, obstetric, major ortho Consider Tranexamic Acid 1g IV now
Results in 10 min
Observe
YES
NO
IS THERE CLINICALLY SIGNIFICANT BLEEDING?
Then
Repeat test 10 mins
AFTER EACH INTERVENTION
IF BLEEDING CONTINUES
CLOT INSTABILITY after 30 minutes | 
IS FIBTEM ML ≥ 10 %? | Is CRT (LY30) > 2.2%
Clot should be stable for 1 hour, not tapering away | 
FIBRINOLYSIS
Hyperfibrinolysis
YES
Consider additional tranexamic acid
IS FIBTEM A5 < 12mm? (close correlation to Clauss fibrinogen) | Is CFF A10 < 15mm? (Local validation recommended)
Including flat line at 5 minutes | 
NO
NO
NO
NO
NO
STILL BLEEDING? Consider SURGICAL PROBLEM and discuss with surgeon and blood bank/haematologist | 
Make a stronger clot? Give cryo to FIBTEM A5 > 14mm Give platelets to EXTEM A5 > 40 mm or consider Platelet Function testing Consider ELP to shorten clotting time to EXTEM CT < 80 sec | Re check temperature, pH, iCalcium, platelets and haemoglobin Consider other contributors to bleeding Platelet inhibitors (do Multiplate Platelet Function test) Consider Von Willebrands Disease, warfarin (INR), enoxaparin etc.