Part 1 – General

  - Description of work

1. 	Provide all materials, labor, tools, equipment and services required to install Steni

Colour composite panels.

  - RELATED SECTIONS

- 05100 Structural framing

- 05400 Metal Framing

- 07200 Insulation

- 07600 Metal flashing

- 07900 Sealants

- 09800 Finishes

  - REFERENCES

  - ASTM E-84-05 Standard Test Method For Surface Burning Characteristics

Of Building Materials

2. 	Can/ULC S-134 Standard Method of Fire Test of Exterior Wall Assemblies

  - SUBMITTALS

- Product data including : preparation instuctions and recommendations, storage

and handling, and installation methods.

- Samples : Architects selection from full range of color and texture combinations.

- Two copies of the manufacturer’s literature for the composite panels.

- Provide copy of manufacturer’s 60 year warranty.

  - QUALITY ASSURANCE

- Manufacturer shall have a minimum of 15 years experience in manufacturing

composite wall panels of this nature.

- Installer to have successfully completed installations of similar size and scope as specified in this section.  References provided upon request.

- Maximum deviation from vertical and horizontal alignment of erected panels 		shall be no more than 6mm in 6.1m.

  - DELIVERY, STORAGE AND HANDLING

- Delivery: Deliver materials in original, unopened packages bearing brand names and identification of manufacturer.

- Handling: Exercise care in unloading, storing, and installing panels to prevent 		damage.

- Storage: Store panels on skids above grade and cover in a dry place that will allow ventilation.

PART 2 – PRODUCTS

  - MANUFACTURERS

1.	The design is based on Steni Nature Aggregate Composite Wall Panels as manufactured by Steni AS and distributed in Canada by :

- Colico Architectural Products Inc.; 4099, boul. St-Jean-Baptiste, Montreal, Qc., H1B 5V3, Telephone 1 877 640-8928

- Represented in Ontario by Façade Systems Inc.

blair@facadesystemsinc.com                                                                                           (647)923-8967

- Substitutions are not permitted

- Substitutions will only be considered if received in writing no 				less than 10 days prior to bid date and must comply fully with				specified requirements.

2.02	MATERIALS													1.	Panels shall be Steni Vision Composite wall Panels as manufactured 					by Steni AS												2.	Composite panels shall have a Class A building material rating when tested in				accordance with ASTM E84-05 and shall exhibit a flame spread of 15 or less				and a smoke developed rating of 150 or less.

3.	Composite panel thickness: 6mm or 15/64’’ (nominal).						4.	Composite panel weight: 11 kg/square meter or 2.2 lbs/square foot.				5.	Composite panel finish: select from Matt, Half Matt, High Gloss

6.	Composite panel color: select from manufacturer’s standard colors range.			2.03	FABRICATION												1.	Smooth polyester Fiberglass panel with color Electron cured acrylic finish

manufactured by a continuous on-line process which chemically bonds

the acrylic finish into the base matrix to form an integral composite of the

elements.

2.	Tolerances												a. Panel bow shall not exceed 0.8% of panel overall dimension.				b. Length and width shall not vary by more than 1.5mm or 1/16’’.				c. Panels shall be square.

3.	Standard panel length shall not exceed 3.2m or 10’6’’.

4.	Maximum panel width is 1213mm or 3’11 3/4’’

5.	Fabricate trim, flashings, and accessories to detailed profiles.

2.04	ACCESSORIES												1.	All exposed fasteners shall be #410 stainless and have a colored head to match				the panel as closely as possible.  Fasteners shall be supplied by panel 					distributer.												2.	All extrusions shall have a Kynar 500 finish or equivalent and supplied by 				panel distributer.  Color to be selected from manufacturer’s standard color chart.			3.	Recommended sealants shall be Dow ‘’CWS’’ and supplied by panel distributer.			4.	All sheet metal flashings shall meet requirements of section 07600.																PART 3 – EXECUTION										3.01	INSPECTION													1.	Panel substructure shall be level and plumb								2.	Panel substructure shall be structurally sound as determined by architect/engineer		3.	Panel substructure shall be free of defects detrimental to work.					4.	Panel installer shall inspect substructure and not proceed with panel erection				until any deviations are corrected.							3.02	INSTALLATION												1.	Erect panels level and plumb, in proper alignment and relation to substructure				framing and established lines.									2.	If field cutting or drilling of panels is required, follow manufacturer’s					instructions and recommendations.									3.	Where panel and aluminum materials come in contact with dissimilar materials,				PVC compressive tape shall be installed to insulate between the dissimilar				materials.										3.03	CLEANING AND PROTECTION										1. 	Dispose excess materials and remove debris from site after completion.				2.	Upon completion of installation and curing of adhesive and sealants, clean panels			as per manufacturer’s recommendations.								3.	Protect installed panels from subsequent construction activities until final 				acceptance by architect and owner.

End of section