## Slide 1: 59th Meeting of JTC1 SC31 Working Group 1
NAVSEA WARFARE CENTERS
NAVSEA WARFARE CENTERS
NAVSEA WARFARE CENTERS
NAVSEA WARFARE CENTERS
IUID 2.0
Craig MacDougall
April 2025
Distribution Statement
Presented by:
1

## Slide 2: Overview
The US DoD changed its IUID policy with the revision of DoDI 8320.04, released in November 2024
The updated version of IUID has been branded “IUID 2.0”
  IUID 2.0 always uses NCAGE code, Original Part Number, and Serial Number
  IUID 2.0 uses either: Data Identifiers 25V, 1P, and S
OR
Text Element Identifiers MFR , FAB , PNO , and SEQ
Revised policy is backward compatible (“historic IUID”) with all previously released policy
Historic IUID marks do not require replacement to IUID 2.0 marks
Determining criteria for IUID marking no longer includes acquisition cost
US = United States
DoD = Department of Defense
IUID = Item Unique Identification
DoDI = Department of Defense Instruction

## Slide 3: IUID 2.0 Differences Can Look Trivial
Historic IUID
IUID 2.0
[)>RS06GS17V12345GS1PABCGSS67890RSEOT
[)>RS06GS25V12345GS1PABCGSS67890RSEOT
NCAGE
Original Part Number
Serial Number
Manufacturer NCAGE
Original Part Number
Serial Number

## Slide 4: IUID 2.0 Has Fewer Options
Historic IUID
IUID 2.0
[)>RS06GSI4Y1SL65848Z411439RSEOT
[)>RS06GS25V12345GS1PABCGSS67890RSEOT
Manufacturer NCAGE
Original Part Number
Serial Number
Vehicle Identification Number

## Slide 5: Decoding IUID
Historic IUID uses format codes 05, 06, 12, or DD (very early IUID authorized format code “DD” prior to 12 being included in ISO/IEC 15434 for Text Element Identifiers. Format code “DD” should be treated as an exact equivalent to format code 12)
IUID 2.0 uses format codes 06 or 12
Historic IUID may use the following data qualifiers:
  Application Identifiers1 (format code 05) 01, 10, 21, 95, 8002, 8003, 8004
  Data Identifiers2 (format code 06) 3V, 12V, 17V, 18V, 7L, 1P, 1T, S, 18S, 22S, 25S, I, 4N
  Text Element Identifiers3 (format code 12) MFR , SPL , CAG , DUN , EUC , PNO , LOT , LTN , BII , SER , SEQ , UCN , UID , USN , UST
IUID 2.0 uses the following data qualifiers:
  Data Identifiers2 25V, 1P, S
  Text Element Identifiers3 MFR , FAB , PNO , SEQ
1 GS1 General Specification
2 MH10.8.2
3 A4A Common Support Data Dictionary (CSDD)

## Slide 6: Encoding IUID 2.0
New IUID marking must be compliant with IUID 2.0 requirements
Data Identifiers 25V, 1P, and S should be used
Text Element Identifiers FAB , MFR , PNO , SEQ may be used if required by other law, policy or institutional practice

## Slide 7: Encoding IUID 2.0
Data Identifiers used under format code 06
  (25V) NCAGE codes are exactly 5 characters [0-9A-Z]
  (1P) Original Part Numbers are 32 or less characters [0-9A-Z/-]
  (S) Serial Numbers are 30 or less characters [0-9A-Z/-]
Text Element Identifiers used under format code 12
  (FAB , MFR ) NCAGE codes are exactly 5 characters [0-9A-Z]
  (PNO ) Original Part Numbers are 15 or less characters [0-9A-NP-Z-]
    The last character cannot be a dash (-)
  (SEQ ) Serial Numbers are 15 or less characters [0-9A-Z-]
    Neither the first nor the last character can be a dash (-)
[0-9A-Z] means characters are restricted to the capital Latin alphabet (A-Z) and/or digits (0-9)
[0-9A-Z/-] means characters are restricted to the capital Latin alphabet (A-Z) and/or digits (0-9) and/or the two special characters, dash (-) and forward slash (/)
[0-9A-NP-Z-] means characters are restricted to the capital Latin alphabet, excluding the letter “O” (A-NP-Z), and/or digits (0-9) and/or the special character dash (-)

## Slide 8
Questions?