## Slide 1: Firearm Safety for the Stage
Never an Injury
Never an Excuse

## Slide 2: John Spiegel, President/CEO
john@spiegelfilms.com
USDoD, US Army, GANG, GADoD, NRA, AGI, BSA

## Slide 4: Why is production using a Firearm?
Is it REQUIRED?
Is it the BEST Answer
Are We Using the SAFEST Option

## Slide 5: The Negatives
They are Scary
Audience Watch Firearms/Guns
Risk Increases Significantly
Guns = Expense
Safety = Expense
Are They REALLY Necessary

## Slide 6: The Positives
Uhm… Yep

## Slide 7: Stage Combat
This is a Dance NOT a Fight!

## Slide 8: ALWAYS SAFETY FIRST
ALWAYS keep your gun pointed in a safe direction
ALWAYS keep your finger off the trigger until ready to shoot
ALWAYS keep your gun unloaded until ready to use

## Slide 9: Types of Stage Firearms

## Slide 10: Types of Stage Firearms
1 Replica
  Non firing Rubber, Plastic or Metal

## Slide 11: Types of Stage Firearms
2 Shrapnel Gun
  Airsoft or Toy that can discharge a projectile

## Slide 12: Types of Stage Firearms
3 Plug Fire
  Manufactured to be only a blank gun

## Slide 13: Types of Stage Firearms
4 BFA- Adapted Real Weapon

## Slide 14: Types of Stage Firearms
5 Real Weapon with Blank

## Slide 15: Some Other Options
Electronic Ignition
Coolfire
Green Gas
CO2 BB
Magic Fireball with Plug and Flashpaper
Pyrodex?

## Slide 16: Action Types
Single Action- Hammer Must be Reset each Time
Double Action- Pulling Trigger Sets Hammer
Bolt/Lever/Pump Action- Action must be worked each time to reset firearm
Semi-Automatic- Pulling Trigger Discharges Round
Select Fire- Safety Switch determines rate of fire
Fully Automatic- Pulling trigger discharges rounds until trigger pull is ceased

## Slide 17: Inspection- Always and Constant
Always Assume Firearm is Loaded
Never Rush
Always Keep Breach Open
Look at ALL Parts

## Slide 18: Inspection- What to Look for…
Foreign Objects in barrel
Discharged Powder
Loose Parts
Missing Parts
Oiled and Clean

## Slide 19: Types of Blanks

## Slide 20: Cartridge ID
Crimped Real

## Slide 21: Cartridge ID
Molded Real

## Slide 22: Cartridge ID
Plug Free Real

## Slide 23: Cartridge ID- NO!!!!!!!
Wadded Real

## Slide 24: Ready to Discharge

## Slide 25: Discharging
Never Underestimate Discharge Pattern
Depends on Weapon
Never Stand directly In-front
There is Always a Discharge Pattern
  Front
  Side
  Top

## Slide 26: So, What is the Dangerous Part?
High Pressure Gasses
High Velocity Debris
“Hot” Brass
Action of the Weapon

## Slide 27: Who is Responsible?
You
Armourer/ Properties/ Gun Wrangler
Director
Producer
Weapon Operator

## Slide 28: Safety Protocols
Always Written
Log Everything
Waivers
NEVER LIVE USE
Sign-Out with Inspection
Sign-In with Inspection
The Theatrical Firearms Handbook- Inouye