## Slide 1: Designing LED Circuits for Model Railroaders
Prepared for ARHS
February 2021

## Slide 2: Electronic Symbols—common to model railroad use
Passes current only from Positive to Negative—in the direction of the “arrow” in the symbol.
The direction of installation is important
In practice, from anode (the long leg) to the cathode (which is the short leg).
Stores electricity—like a mini battery. Units are farads, microfarads and picofarads
Direction of installation is not usually important (electrolytics are exception and are marked).
Creates a magnetic field. Units are Henrys.
Direction of installation is not important
Creates resistance—like an orifice in a hose. Units are Ohms
Direction of installation is not important
Source of AC power—usually a power supply
Units are AC Volts
Same characteristics as a Diode but in addition emits light when passing current in the forward direction.
Source of DC power—usually a battery, but could be a power supply
Units are DC Volts
LED
Current only flows this way
Anode
(long leg)
Cathode
(short leg)
An LED is a current device—A resistor must be sized to control the current

## Slide 3: Resistors—those colored bands have a meaning
Standard Resistor Values
Standard Resistor Values are at about a 10% interval.
The tolerance on the value (silver band) is 10%.
Always pick the next higher resistance value to limit current.
Any calculation in electricity within 10% is accurate enough!

## Slide 4: Direct current is like water flowing in pipe
This Photo by Unknown Author is licensed under CC BY-SA
O
A battery stores energy. The higher the (water level) the higher the voltage.
Water pressure is analogous to Voltage.
The flow in the wire is current and is analogous to the volume of water flowing in a pipe.
Water flow in GPM is analogous to current in Amps
A resistor is similar to an orifice in a pipe—it restricts the flow.
A diode act like a check valve—current can only flow in one direction.
Orifice
Check Valve
Ground has zero potential energy. Everything is measured from ground.

## Slide 5: There are only two equations that are needed to calculate a resistor value.
Resistance (units are Ohms) is calculated from:
V= i * R (Where V is volts, i is Amps and R is Ohms)
Which can be rewritten as
R = V / i
Power (units are watts) is the energy converted to heat in a resistor and is calculated from:
P = V * A or P = V * i
(Where P is watts, V is volts, and I is amps.)
Typical Power ratings for resistors are:
  1/8, 1/4, 1/2 , 1 Watt
The units for electrical values can be tricky
Some units have a prefix of:
  Milli which is x 10 -3 or times .001
    So, 20 milliamps is 0.020 Amps
  Other prefixes are shown in the chart below: below:

## Slide 6: Tricks with Resistors
What is the Equivalent Single Resistor replacing two Resistors in Series?
The Equivalent single resistor is the sum of the two individual resistors.
If you need a higher resistance value than any resistor that you stock, then just add small resistors in series until you have the necessary resistance.
The power capability of the equivalent resistor is usually twice the rating of the lowest individual resistor but the power across each resistor should be checked.
What is the Equivalent Single Resistor replacing two Resistors in Parallel?
The Equivalent single resistor is a bit more complicated…….
Re = (R1 * R2) / (R1 + R2 )
Multiply the two resistors and divide by the sum of the resistors
A special case is when both resistors are the same value, then
Re = (R * R ) / 2R = R/2
The equivalent of two equal resistors in parallel is one half of the individual resistor value.
If each resistor is a ¼ Watt, the equivalent resistor carries twice the power and is rated at ½ Watt.
A trick here is if you need a ½ Watt resistor but only stock ¼ watts, then double the resistance value and put two in parallel.
Trick question—what is the equivalent resistor if four equal resistors are in parallel? Answer is Re = R / 4 (one fourth of R)

## Slide 7: Alternating Current and Direct Current are different
There are variations on the types of current
DCC is a form of AC, but uses a square wave
The decoder looks at the width and frequency of the pulses and “decodes” the message being sent.
AC can be converted to DC using a Wheatstone Bridge (also known as a Rectifier)
Adding a capacitor “smooths” the ripple
A capacitor or a battery produces a reasonably constant DC voltage.
AC
Half Wave
Full Wave
Full Wave
With Capacitor
Full Wave
With Capacitor
DC

## Slide 8: A Resistor is “Sized” by defining TWO Values: Resistance (in Ohms) and Power Rating (in Watts)
O
This is the simplified circuit you are building.
The circuit has:
A constant voltage source (a power supply or a battery)
A resistor that you must size, and
A LED which has two known characteristics
  It’s forward voltage, Vf, and
  It’s operating current, if
Redraw this circuit as a simple “stick” diagram where:
VS is the Source (or battery) voltage in Volts
Vf is the Forward Voltage of the LED (usually on the LED package) in Volts
”i” is the Forward Current of the LED (Also usually on the LED package) in Amps or if in milliamps then multiply the resistance value by 1000.
Vf
if
VS
The equation for the Resistance of the Resistor is:
R = (VS – Vf) / if in Ohms
And, the power dissipated in the Resistor is:
P = (VS – Vf) * if in Watts
if

## Slide 9: Example Problem Using a “Typical” LED
All LEDs have peculiar operating characteristics, and you should always use the values associated with that LED.
If you don’t know, then you can use a “typical” LED set of values to ”get in the Ballpark”
For a Typical LED:
Vf = 2 Volts
If = 20 milliamps
Drawing the simple circuit using a 12- volt DC power supply and solving the equations gives:
O
The equation for the Resistance Value of the Resistor is:
R = (VS – Vf) / if in Ohms
R = (12 – 2 ) / 0.020
R = 10 / 0.020
R = 10,000 / 20
R= 500 Ohms
And, the power dissipated in the Resistor is:
P = (VS – Vf) * if in Watts
P = (12 – 2) X 0.020
P = 10 X 0.020
P = .2 Watts
if
= 0.020 A
VS = 12V
Vf = 2V
O
The proper size resistor is 500 Ohms rated at ¼ Watt
The most important step is to draw the circuit picture!!
V = 2V
}
VR = 10V

## Slide 10: Now a couple of “What if” Problems
The equation for the Resistance Value of the Resistor is:
R = (VS – Vf) / if in Ohms
R = (12 – 2 – 2 ) / 0.020
R = 8 / 0.020
R = 800 / 20
R= 400 Ohms
And, the power dissipated
in the Resistor is:
P = (VS – Vf) * if in Watts
P = (12 – 2 -2 ) X 0.020
P = 8 X 0.020
P = .16 Watts (Greater than .125 but less than .25)
if = 0.020 A
VS = 12V
Vf = 2V
“What if” you have two LEDs in series?
Assume a “standard” LED and a 12 VDC power supply
Draw the circuit:
The Proper Resistor is a 400 Ohm, 1/4 Watt
Vf = 2V
O
VR = 8V
O
O
IR= 0.040 A
The Proper Resistor is a 250 Ohm, 1/2 Watt
The equation for the Resistance Value of the Resistor is:
R = (VS – Vf) / if in Ohms
R = (12 – 2) / 0.020
R = 10 / 0.040
R = 1000 / 40
R= 250 Ohms
And, the power dissipated
in the Resistor is:
P = (VS – Vf) * if in Watts
P = (12 – 2) X 0.040
P = 10 X 0.040
P = .4 Watts
“What if” you have two in parallel?
Assume a “standard” LED and a 12 VDC power supply
Draw the circuit:
Vf = 2V
VR = 10V
O
O
VS = 12V
O
if = 0.020 A
if = 0.020 A
V = 2V
V = 2V
V = 4V

## Slide 11: Here are some variations using different power sources
O
The equation for the Resistance Value of the Resistor is:
R = (VS – Vf) / if in Ohms
R = (5 – 2 ) / 0.020
R = 3 / 0.020
R = 300 / 20
R= 150 Ohms
And, the power dissipated
in the Resistor is:
P = (VS – Vf) * if in Watts
P = (5 – 2) X 0.020
P = 3 X 0.020
P = .06 Watts
if = 0.020 A
VS = 5V
Vf = 2V
O
“What if” you are using a 5 Volt Power supply?
Then Vs becomes 5 and the solution follows:
The Proper Resistor is a 150 Ohm, 1/8 Watt
O
Now, you try it using a 9 Volt Power supply
O
The equation for the Resistance Value of the Resistor is:
R = (VS – Vf) / if in Ohms
R =
R= _______ Ohms
And, the power dissipated in the Resistor is:
P = (VS – Vf) * if in Watts
P = _______Watts
if = ____
VS =___
Vf = ___
O
The Proper Resistor is a ___ Ohm, ___ Watt
V = 2V

## Slide 12: More Examples…..
Does somebody have an LED????
VS = ____
Vf = _____
If = _____
O
The equation for the Value
Resistance of the Resistor is:
R = (VS – Vf) / if in Ohms
R =
R= _______ Ohms
And, the power dissipated
in the Resistor is:
P = (VS – Vf) * if in Watts
P = _______Watts
if= ____
VS =___
Vf = ___
O
The Proper Resistor is a ___ Ohm, ___ Watt
Does somebody have another LED????
VS = ____
Vf = _____
If = _____
O
Resistance:
R= _______ Ohms
Power:
P = _______Watts
if = ____
VS =___
Vf = ___
O
The Proper Resistor is a ___ Ohm, ___ Watt