## Slide 1: FISSION CROSS SECTIONS
PRACTICAL SESSION FIESTA 2024
Maria DIAKAKI
National Technical University of Athens,
GREECE

## Slide 2: OUTLINE OF PRACTICAL SESSION
GOAL:
1) To extract n-induced fission cross section (cs- «σ») from real data. (ΕΧ. 1)
2) Understand the importance of the reference reaction chosen (EX. 2,3)
3) Understand the differences of the different techniques (white neutron beam, monoenergetic neutron beam) (EX. 2,3)
Implementation of course in Jupyter Notebook (many thanks to Thanos Stamatopoulos (LANL))
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024

## Slide 3
GENERAL REMARKS / ASSUMPTIONS :
1) Detection of fission fragments (FF) with gaseous detector
2) Thin disks of the target under study (tar)
FF
FF
tar
e-
GAS
Φtar
: No of FF detected,
with the necessary
correction factors
NEUTRON BEAM
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024

## Slide 4
GENERAL REMARKS / ASSUMPTIONS :
3) Measurement of Φtar: WITH REFERENCE TARGET (ref),
(very well-known n-induced cs – “primary standard”, ”secondary standard”, “reference”)
FF
FF
tar
e-
GAS
Φtar
NEUTRON BEAM
ref
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024

## Slide 5
GENERAL REMARKS / ASSUMPTIONS :
3) Measurement of Φtar: WITH REFERENCE TARGET (ref),
(very well-known n-induced cs – “primary standard”, ”secondary standard”, “reference”)
FF
FF
tar
e-
GAS
Φtar
NEUTRON BEAM
ref
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024

## Slide 6
GENERAL REMARKS / ASSUMPTIONS :
3) Measurement of Φtar: WITH REFERENCE TARGET (ref),
(very well-known n-induced cs – “primary standard”, ”secondary standard”, “reference”)
FF
FF
tar
e-
GAS
Φtar≈ Φref
NEUTRON BEAM
ref
=>
Φtar≈ Φref
: FF losses due to absorption in the tar/ref, detection and analysis procedure (dead time/pile-up/ more specific corrections not taken into account at this course).
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024

## Slide 7: EXERCISE 1: n-induced fission cs («σ») at given energy E 232Th(n,f) (reference: 238U(n,f) reaction)
1a) Application of properly chosen threshold in the Counting spectra
heavy FF
light FF
alpha background
threshold
Choose threshold (BEAM-OFF)
to cut the alpha background
and integrate above threshold
=>
integral_target
integral_reference
200
600
1000
channels

## Slide 8: 1a) integral_target and integral_reference
channel_min = chosen threshold
Notes: 13

## Slide 9
1b) Correction of subthreshold fission fragment counts with Monte Carlo simulations (given)
EXERCISE 1: n-induced fission cs («σ») at given energy E 232Th(n,f) (reference: 238U(n,f) reaction)
A) Threshold (ADC channels) -> Threshold (Energy):
From calibration (given):
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024

## Slide 10
1b) Correction of subthreshold fission fragment counts with Monte Carlo simulations (given)
EXERCISE 1: n-induced fission cs («σ») at given energy E 232Th(n,f) (reference: 238U(n,f) reaction)
= * (1 + /
A) Threshold (ADC channels) -> Threshold (Energy):
From calibration (given):
B) Estimate from simulated spectra:

## Slide 11
EXERCISE 1: n-induced fission cs («σ») at given energy E 232Th(n,f) (reference: 238U(n,f) reaction)
1c) Calculation of efficiency (from the same Monte Carlo simulations): FF counts absorbed in the actinide target
FF
FF
= eff
(for tar and ref)

## Slide 12
1d) Extraction of the final cross section value (finally….. )
EXERCISE 1: n-induced fission cs («σ») at given energy E 232Th(n,f) (reference: 238U(n,f) reaction)
What is the value you obtain????
Uncertainties????
Notes: sigma=0.362 b

## Slide 13
White pulsed neutron beam => Various neutron energies (En)
EXERCISE 2: Fission cross section measurements with the TOF technique
FF
FF
tar
e-
GAS
Φtar
NEUTRON BEAM
ref
Εn
=> tof

## Slide 14
EXERCISE 2: Fission cross section measurements with the TOF technique
2a) The neutron energy resolution with the TOF technique and how it affects results
primary beam
~δλ
(dL)
~pulse width (tb)
(dt_ns)
Decide δλ from simulations for th-1keV and put pulse width (typically 1-10 ns)
Notes: Answers 2a i) / +2a (iii) /+2aiv) effect of resolution function show on notebook 26

## Slide 15
EXERCISE 2: Fission cross section measurements with the TOF technique
2b) Cross section calculation over a wide energy range 230Th(n,f) at 600keV < En < 1 GeV (reference: 235U(n,f) reaction)
2b) i) Check the corrected Fission Fragment Counts for 600keV < En < 1 GeV for 230Th and 235U and the corresponding reference cross section (235U(n,f)).
2b) ii) Cross section calculation with the above corrected Fission Fragment Counts at the energy range 600keV < En < 1 GeV with selected Binning: 100 bins/energy decade (PLOT)
Εn
~100MeV-10MeV
~10MeV-1MeV
TOF
TOF bins
Counts
………
Notes: 27

## Slide 16
EXERCISE 2: Fission cross section measurements with the TOF technique
bin-per-bin
σref interpolation at bin center
x
=
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024
Which factors of σ change over energy???
Notes: subthreshold ff correction, pile-up, flux ratios 30

## Slide 17
2c: Sensitivity on choice of reference reaction
EXERCISE 2: Fission cross section measurements with the TOF technique
Effect of two different reference reactions, 235U(n,f) and 10B(n,a) in the extraction of σ(243Am(n,f)).
Which one is better to use (PLOT & DISCUSSION)
Notes: 30

## Slide 18
2c: Sensitivity on choice of reference reaction
EXERCISE 2: Fission cross section measurements with the TOF technique
Effect of two different reference reactions, 235U(n,f) and 10B(n,a) in the extraction of σ(243Am(n,f)).
Which one is better to use (PLOT & DISCUSSION)
2c) i) Comment on the ratios calculated below for the 243Am(n,f) counts with the two different reference reactions.
WHAT WOULD YOU EXPECT????
WHAT DO YOU GET??????
Notes: 35

## Slide 19
2c ii) Zoom in different energy regions to see how the structures of the Target and Reference reactions evolve (TOF to energy conversion)
EXERCISE 2: Fission cross section measurements with the TOF technique
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024

## Slide 20
EXERCISE 2: Fission cross section measurements with the TOF technique
2c iii) Effect of small neutron energy uncertainty in the fission cross section results
Energy uncertainty due to uncertainties in resolution function.
From your results, which reference reaction would you prefer to measure the cross section of the 243Am(n,f)
reaction at the energy range 1-100 eV (Resolved Resonance Region) ?
235U(n,f) or 10B(n,a) ???????????
2d) Choice of the proper binning (JUST PLOT, ZOOM
AND DISCUSS):
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024
Notes: 40

## Slide 21
Neutron producing reaction: 3H(d,n)4He
En: ~16.5 MeV
EXERCISE 3: Fission cross section measurements with Quasi-monoenergetic beams
FF
FF
tar
e-
GAS
ref
TARGET 7Li,2H,3H
Ion beam (p,d)
5-10 μm
Mo foils
Ta, Pt, Cu
Ion beam stops
θ
n
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024

## Slide 22
Φ at quasi-monoenergetic neutron beams :
A) Main neutron beam - width :
1) Energy straggling of the ion beam.
2) Diﬀerential cross section and kinematics:
Typically θ=5-10ο => ~monoenergetic and isotropic
B) ”Parasitic neutrons” :
Parasitic ion-induced reactions with structural materials of
the target and the beam line (Mo, Ti, Ta, Cu, O, C….)
2) Deuteron breakup (2H(d,np)) reaction for Ed ≥ 4.45 MeV
3) Neutron scattering in the surrounding materials
EXERCISE 3: Fission cross section measurements with Quasi-monoenergetic beams
TARGET 7Li,2H,3H
Ion beam (p,d)
5-10 μm
Mo foils
Ta, Pt, Cu
Ion beam stops
θ
n

## Slide 23
3a) Plot the main neutron peak (Monte Carlo simulation)
3b) Fit the main peak, find the mean neutron energy and extract an energy uncertainty: VERY IMPORTANT FOR FINAL RESULTS GIVEN AT EXFOR.
3c) Estimate the effect of lower energy parasitic neutrons at the fission cross section results for three different reactions: 232Th(n,f) (fertile) , 235U(n,f) (fissile) and 238U(n,f) (fertile): PLOT AND DISCUSS THE SENSITIVITY TO LOWER ENERGY NEUTRONS
3d) Estimate the fission reaction rate for the three different reactions: 232Th(n,f) , 235U(n,f) and 238U(n,f), taking into account the lower energy parasitic neutron "tail”.
3e) Estimate the ratio (parasitic fission reaction rate)/(total reaction rate) for the three different reactions: 232Th(n,f) , 235U(n,f) and 238U(n,f), and decide which reference reaction (235U(n,f) or 238U(n,f)) you would use to measure the 232Th(n,f) minimising the uncertainty from the fission events created from the parasitic neutron tail.
ANY IDEAS????
EXERCISE 3: Fission cross section measurements with Quasi-monoenergetic beams

## Slide 24
Congratulations!!
You estimated your first neutron induced fission cross sections both for monoenergetic and white neutron beams!!!
Systematic uncertainties???
2) Important factors to consider when designing a new measurement?
3) Now you should give your new data to EXFOR:
a) absolute cross section data AND the ratio
b) statistical uncertainties AND the different systematic uncertainties SEPARATELY,
c) total uncertainty with the propagation (with covariance).
d) The maximum info relevant to experiment useful to subsequent evaluation.
FIESTA 2024 – Practical on Fission Cross Sections – M. Diakaki
November 18-22, 2024

## Slide 25
an EXFOR entry….
example of reported systematic uncertainties :