SECTION 13065

BULLET RESISTANT ARCHITECTURAL ASSEMBLIES

Display hidden notes to specifier. (Don't know how? Click Here)

Copyright 2018-2019 ARCAT, Inc. - All rights reserved

** NOTE TO SPECIFIER **  Chicago Bullet Proof Systems; Bullet resistant architectural assemblies.

This section is based on the products of Chicago Bullet Proof Systems, which is located at:

2595 Bond St.

University Park, IL  60484

Phone:  708-534-9102

Fax:  708-534-9132

Email:  max@chicagobulletproof.com

Web:  www.chicagobulletproof.com

[Click Here] for additional information.

Chicago Bullet Proof Systems is a high quality designer and manufacturer of architectural products dedicated to providing the best protection available to the financial, government, commercial and private industries.

Established in 1912, Chicago Bullet Proof is a leader in the bullet resistant industry with innovative engineering, UL testing, and quality manufacturing.

Chicago Bullet Proof Systems’ products are listed and labeled by Underwriters Laboratories, according to UL 752 Standards.

GENERAL

SECTION INCLUDES

** NOTE TO SPECIFIER **  Delete items below not required for project.

Bullet Resistant Vision Windows.

Bullet Resistant Transaction Windows.

RELATED SECTIONS

** NOTE TO SPECIFIER ** Delete any sections below not relevant to this project; add others as required.

Section 05100 - Structural Metal Framing; Panel Supporting Members.

Section 05500 - Metal Fabrications; Panel Supporting Members.

Section 06100 - Rough Carpentry; Panel Supporting Members.

Section 08710 - Door Hardware.

Section 08800 - Glazing.

Section 09900 - Paints and Coatings.

REFERENCES

** NOTE TO SPECIFIER **  Delete references from the list below that are not actually required by the text of the edited section.

Underwriters Laboratories (UL):

UL 10B – Standard for Fire Tests of Door Assemblies.

UL 752 – Standard for Bullet-Resisting Equipment.

SUBMITTALS

Submit under provisions of Section 01300.

Product Data:

Manufacturer's data sheets on each product to be used.

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Typical installation methods.

** NOTE TO SPECIFIER **  Delete selection samples if colors have already been selected.

    - Selection Samples:  For each finish product specified, two complete sets of color chips representing manufacturer's full range of available colors and patterns.

Verification Samples:  For each finish product specified, two samples, minimum size 6 inches (150 mm) square representing actual product, color, and patterns.

Shop Drawings:  Include details of materials, construction and finish. Include relationship with adjacent construction.

QUALITY ASSURANCE

Manufacturer Qualifications:  Company specializing in manufacturing products specified in this section with a minimum five years documented experience.

Installer Qualifications:  Company specializing in performing Work of this section with minimum two years documented experience with projects of similar scope and complexity.

Source Limitations:  Provide each type of product from a single manufacturing source to ensure uniformity.

PRE-INSTALLATION CONFERENCE

Convene a conference approximately two weeks before scheduled commencement of the Work. Attendees shall include Architect, Contractor and trades involved. Agenda shall include schedule, responsibilities, critical path items and approvals.

DELIVERY, STORAGE, AND HANDLING

Store and handle in strict compliance with manufacturer's written instructions and recommendations.

Protect from damage due to weather, excessive temperature, and construction operations.

PROJECT CONDITIONS

Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results. Do not install products under environmental conditions outside manufacturer's recommended limits.

SEQUENCING

Ensure that products of this section are supplied to affected trades in time to prevent interruption of construction progress.

WARRANTY

Manufacturer's Warranty:  Provide manufacturer's standard limited warranty.

PRODUCTS

MANUFACTURERS

Acceptable Manufacturer: Chicago Bullet Proof Systems which is located at: 2595 Bond St.; University Park, IL  60484; Tel:  708-534-9102; Fax:  708-534-9132; Email:  max@chicagobulletproof.com; Web:  www.chicagobulletproof.com.

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions: Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

** NOTE TO SPECIFIER **  Delete article if not required.

Basis of Design:  Standard Vision Window, Model SAVL; as manufactured by Chicago Bullet Proof Systems.

Performance and Design Requirements:

** NOTE TO SPECIFIER **  Delete bullet resistance options not required. Higher levels are achievable. Contact manufacturer for more information.

Bullet Resistance:  UL 752, Level 1.

Bullet Resistance:  UL 752, Level 2.

Bullet Resistance:  UL 752, Level 3.

Bullet Resistance:  UL 752, Level 4.

** NOTE TO SPECIFIER **  Delete finish option not required.

      - Finish:  Anodized. Satin.

Finish:  Anodized. Clear.

Finish:  Anodized. Dark bronze.

Finish:  Powder Coated. Color:  Chosen from manufacturer’s standard offering.

Frame:  Aluminum.

** NOTE TO SPECIFIER **  Delete opening size not required.

Opening Size:  As indicated on Drawings.

Opening Size (WxH, in/mm):  ______ .

Profile:  1-7/16 x 4-7/8 inch (37 x 124 mm).

Corners mitered, welded, and ground smooth.

Glass Armor:  UL 752 listed bullet resistant transparent armor.

** NOTE TO SPECIFIER **  Delete article if not required.

Basis of Design:  Standard Aluminum Transaction Window, Model SATW; as manufactured by Chicago Bullet Proof Systems.

Performance and Design Requirements:

** NOTE TO SPECIFIER **  Delete bullet resistance options not required. Higher levels are achievable. Contact manufacturer for more information.

Bullet Resistance:  UL 752, Level 1.

Bullet Resistance:  UL 752, Level 2.

Bullet Resistance:  UL 752, Level 3.

Bullet Resistance:  UL 752, Level 4.

** NOTE TO SPECIFIER **  Delete finish option not required.

Finish:  Anodized. Satin.

Finish:  Anodized. Clear.

Finish:  Anodized. Dark bronze.

Finish:  Powder Coated.

Frame:  Aluminum.

** NOTE TO SPECIFIER **  Delete opening size option size not required.

Opening Size:  As indicated on Drawings.

Opening Size (WxH, in/mm):  ______ .

Profile:  1-7/16 x 4-7/8 inch (37 x 124 mm).

Three sided frame bolted to deal tray and voice panel sill.

Corners mitered, welded, and ground smooth.

** NOTE TO SPECIFIER **  Delete sill option not required.

Sill:  Standard sill:

Material:  Stainless steel.

Integral deal tray and voice panel.

Profile:  3 x 11 inches (76 x 279 mm) deep by width of window.

Bolted to window frame.

Sill:  Mortise sill:

Material:  Stainless steel.

Integral deal tray and natural voice transmission.

Profile:  3 x 9 inches (76 x 229 mm) deep by width of window.

Recessed into countertop.

** NOTE TO SPECIFIER **  Delete tray option not required.

Deal Tray and Voice Panel Sill:

Single deal tray with voice panels adjacent to deal tray in sill.

Deal tray sized to pass items not exceeding 12-3/4  x 1-5/8 inches (324 x 41 mm).

Voice panel shall include an acoustically balanced natural voice transmission system.

Material:  Stainless steel.

Drop-in Tray:  Modified non-labeled assembly with 3-sided frame:

Natural voice transmission spacers.

Stainless steel glass channel.

Deal Tray:  Model NDT, bullet resistant non-ricochet drop-in deal tray, 16-3/8 x 11 x 1-5/8 inches (416 x 279 x 41 mm).

Writing Ledge:  Stainless steel writing ledge:

Integral to sill.

Size:  6-1/2 inches (165 mm) by width of window.

** NOTE TO SPECIFIER **  Delete ledge installation location options not required.

Ledge Installation Location:  Threat side.

Ledge Installation Location:  Non-threat side.

Ledge Installation Location:  Threat side and non-threat side.

Glass Armor:  UL 752 listed bullet resistant transparent armor.

** NOTE TO SPECIFIER **  Composed of bullet resistant glazing materials and framing but do not meet all aspects of UL 752 standards and will not bear a UL label. Glazing materials are tested in 12 inch square samples and three test rounds are fired into a four inch triangle for each respective ballistic level; Level 1:  9 mm 124 gr. FMJ lead core. Level 2:  .357 mag. 240 gr. JSP. Level 3:  .44 mag. 240 gr. Gas Checked SWC.

EXECUTION

EXAMINATION

Do not begin installation until substrates have been properly constructed and prepared.

If substrate preparation is the responsibility of another installer, notify Architect in writing of unsatisfactory preparation before proceeding.

PREPARATION

Clean surfaces thoroughly prior to installation.

Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

INSTALLATION

Install in accordance with manufacturer's instructions, approved submittals, and UL 752, and in proper relationship with adjacent construction.

Install all equipment plumb, level, rigid and in true alignment.

Set equipment in accordance with the manufacturer's printed recommendations. Use proper anchoring devices for the material to be anchored to. All exposed anchor holes shall be used for anchoring.

Anchor frames securely in place to supports. Use attachment methods permitting adjustment for construction tolerances, irregularities, alignment, and expansion and contraction.

Installation tolerances: Do not exceed the following installation tolerances:

Squareness: Plus or minus 1/16 inch (1.6 mm) measured on a line, 90 degrees from one jamb, at the upper corner of the frame at the other jamb.

Alignment: Plus or minus 1/16 inch (1.6 mm) measured on jambs on a horizontal line parallel to the plane of the wall

Twist: Plus or minus 1/16 inch (1.6 mm) measured at face corners of jambs on parallel lines perpendicular to the plane of the wall.

Plumb: Plus or minus 1/16 inch (1.6 mm) measured on the jamb at the floor.

Adjust installed doors for correct function and smooth operation.

FIELD QUALITY CONTROL

Field Inspection:  Coordinate field inspection in accordance with appropriate sections in Division 01.

** NOTE TO SPECIFIER **  Include if manufacturer provides field quality control with onsite personnel for instruction or supervision of product installation, application, erection or construction. Delete if not required.

Manufacturer’s Services:  Coordinate manufacturer’s services in accordance with appropriate sections in Division 01.

CLEANING AND PROTECTION

    - Clean products in accordance with the manufacturers recommendations.

Touch-up, repair or replace damaged products before Substantial Completion.

Protect installed products until completion of project.

END OF SECTION