## Slide 1: Weibull Intro
Copyright 2006 - Wes Fulton
Introduction to Dr. Bob’s Weibull Engineering Workshop by Wes Fulton and Carl Tarum
<number>
Notes: 2018 11 27 Previous version
2020 05 20 Removed LLC on slide 8
<number>

## Slide 2: What Students Can Do After Graduating from the Weibull Workshop …
Copyright 2006 - Wes Fulton
Select and fit a variability model for most measurements
Interpret non-linear data patterns on probability scaling
Forecast risk using the selected model with added usage rate
Simulate random samples to answer difficult questions
Choose between graphical and non-graphical solutions
Form a database of previous results to improve accuracy
Plan a test to demonstrate capability or reliability
Evaluate test results (standard, accelerated, or step-stress)
Establish lower and upper confidence bounds for results
Apply simple related probability models when needed
Perform general trend analysis for tracking progress
<number>
Notes: Mention Monte Carlo
<number>

## Slide 3: Student Intro’s
Copyright 2006 - Wes Fulton
Your name
Your current job
Your experience with Weibull (if any)
Your goals for the class
<number>

## Slide 4: To Begin
Copyright 2006 - Wes Fulton
What is reliability?
Point estimates related to reliability
Variability vs. Point estimates
Standard variability distributions
New product development techniques
Service data analysis ... warranty data
The most important thing
<number>
Notes: SW can convert various Warranty data
There are classes on Life Cycle, Production Reliability (Barringer
Most important thing: Weibull Library…. teaser
<number>

## Slide 5: What Is Reliability?
Copyright 2006 - Wes Fulton
Reliability (R) = probability of success
Or … R = 1 - (probability of failure)
  Need a good specification of what is acceptable and what is not acceptable
Actual reliability can change:
  With different design or with different assembly
  With different length of service requirements
  With different duty cycle and different loading
  With different environments
  With changes in quality
  With changes in maintenance practice
So … reliability is a moving target ! ! !
<number>
Notes: <number>

## Slide 6: Point Estimates Related to Reliability
Copyright 2006 - Wes Fulton
R estimate = (successes) / (trial quantity)
Mean time between failure ... “MTBF”
  Meaningful for repairable items
  Cumulative MTBF (easy!) = (total time) / (total failures)
  Instantaneous MTBF … get from Crow/AMSAA
Mean time to failure – “MTTF”
  Meaningful for non-repairable items
  1st moment of life distribution … “expected life”
Availability = (total up-time) / (total time)
<number>
Notes: AMSAA = Army Material Systems Analysis Activity
<number>

## Slide 7: Variability Vs. Point Estimates
Copyright 2006 - Wes Fulton
Trials (go/no-go) without failure … point estimate.
  100 trials … R = 100%.
  1 trial … R = 100% … same! … Is this point estimate useful?
Binomial w/90% confidence … variability estimate.
  100 trials … R >= 97.7 %.
  1 trial … R >= 10 % … so! They are different.
Variability estimates can often be more useful.
Which type of variability model to use?
  Non-parametric: 1st moment, 2nd, ... ( e.g. mean, median, range)
  Parametric: Weibull, lognormal … (y=Par1(x) +Par2)
Parametric accuracy is much better than non-parametric … if model is correct.
<number>
Notes: Parametric: Fit to an equation: y=mx+b. Parameters are m and b
Mean is non parametric. No parameters. Just add and divide
<number>

## Slide 8
Copyright 2006 - Wes Fulton
<number>

## Slide 9: Standard Parametric Variability Distributions and Their Relationship
Copyright 2006 - Wes Fulton
Binomial … for discrete outcomes … only two choices.
Poisson … for discrete outcomes … events occurring vs. Operating time, wire length, inspection area, etc.
Exponential … first term of the Poisson.
Normal… aka “Gaussian” or “bell curve.”
Lognormal… log-values of data have normal distribution.
Extreme value … every individual data value is the smallest (or largest) from a group of samples.
Weibull … extreme value type III smallest … can be 1-parameter, 2-parameter (standard), or 3-parameter
  NOTE: Mixtures could have even more parameters (4, 5, 7)
<number>
Notes: Binomial 2 outcomes
Poisson: counting things
Exponential
Normal has mean, standard deviation. Doesn’t work well for lifetime cases
Talk about mixtures
Extreme values, Gumbel
3 Parameter, a delay shift
?What are the 6 extreme value models?
<number>

## Slide 10: Binomial Distribution
Copyright 2006 - Wes Fulton
<number>

## Slide 11: Poisson Distribution
Copyright 2006 - Wes Fulton
<number>

## Slide 12: Exponential Distribution
Copyright 2006 - Wes Fulton
<number>

## Slide 13: Normal Distribution
Copyright 2006 - Wes Fulton
<number>

## Slide 14: Lognormal Distribution
Copyright 2006 - Wes Fulton
<number>

## Slide 15: Extreme Value Distribution Type I Only … (II & III Not Shown)
Copyright 2006 - Wes Fulton
<number>

## Slide 16: Weibull Distribution … Extreme Value Type III Smallest … USEFUL!
Copyright 2006 - Wes Fulton
PDF
CDF
<number>
Notes: Note that area under each curve = 1, definition of probability density function
Note definition of cumulative distribution function, CDF
Note that the shapes are different because of beta, or slope. These lines have the same eta, or characteristic life
Note that CDF goes to 1
<number>

## Slide 17: Experience Data Vs. Age Data
Copyright 2006 - Wes Fulton
Experience data is useful for general trends
  Total accumulated operation of all equipment
  Total accumulated events
  Use technique such as Crow/AMSAA to evaluate
Age data is useful for more precise Weibull engineering:
  Age = amount of use since new for each equipment
  For standard analysis each data value is either…
    Occurrence (= age to failure for reliability)
    Suspension [= length of successful operation for reliability)
<number>

## Slide 18: New Product Development
Copyright 2006 - Wes Fulton
Preliminary models (parts count, R, MTBF)
1st principles: physics of failure (POF) and probabilistic analysis by Monte Carlo simulation
Development testing (“Weibayes” substantiation)
Crow/AMSAA for test, analyze and fix (TAAF) effort
Accelerated testing (& step-stress)
Prototypes & lead-the-fleet equipment
… Weibull library = essential
<number>

## Slide 19: Service & Maintenance Data Analysis
Copyright 2006 - Wes Fulton
Reliability Centered Maintenance (RCM)
Need good age-to-failure records on failed items
  Failure type is IMPORTANT to know for corrective action!
Also need age on successful items (“suspensions”)
Warranty: Failure ages known (but suspensions?)
Warranty: Month of Production (M.O.P.) vs Months in Service (M.I.S.) includes suspension info
SuperSMITH® can convert from M.O.P.-M.I.S. data
… Weibull library = essential
<number>

## Slide 20: Finally … The Most Important Thing Is:
Copyright 2006 - Wes Fulton
The Weibull library.
So plan for the future...
Start and maintain a good Weibull library...
Save results from every analysis…
  Type of equipment analyzed
  Type of usage of analyzed equipment
  Type of failure under investigation
  Model type, fit type, parameter values
  … And other information as appropriate
<number>

## Slide 21: Next … the Rest of the Story ...
Copyright 2006 - Wes Fulton
<number>