## Slide 1: Estimating Missing Data
Software: SuperSMITH 6.0AA 31 Dec 2021
Note: For more detail, see the RAMS paper: Estimating Quantity of Missing Data in Tails of Distribution
RAMS 2021, The 67th Annual Reliability & Maintainability Symposium,
May 24-27, 2021, Orlando, FL
Carl Tarum, Bathtub Software LLC, Wes Fulton, Fulton Findings
https://ieeexplore.ieee.org/document/9605766

## Slide 2: Causes of missing data
Many distributions are modeled with Weibull, Lognormal, or Normal Distributions.
Sometimes fits are poor because data are missing
  Quantity of scrapped parts may not be recorded
  Sections of data may be missing due to records issues
  Decision to start recording data may be delayed, and early failures were not recorded.
  Supplier may remove parts close to the target to ship elsewhere at a premium price

## Slide 3: Methods to Analyze Missing Early Data.
Crow-AMSAA can be used if there is enough new data. The instantaneous failure rate will become correct
Historically, a 3-parameter Weibull could be used
With ”snapshot” data, Kaplan-Meier techniques can also be used.
A new technique, presented in 2021, uses the traits of the distribution to estimate missing data. This can be used on Early, Late, or Intermediate missing data if there are enough points

## Slide 4: Point Pattern Impact: Weibull Scaling
This is a “precise fit”. Note the Benard plotting positions for the 3rd point and 3rd from last point

## Slide 5: Effect of missing points
Suppose that the previous slide with 30 points was “Truth”
But unknown to us, the first two points, 4 points in the middle, and 2 points at the end are missing.
What would the fit look like?

## Slide 6: Data as received
We think the 3rd point is really the 1st point, so it gets plotted at 3.1% instead of the true 8.8%
We think the 28th point is the last point, so it gets plotted at 96.9% instead of the true 91.6%

## Slide 7: t0 actually worse pve% than a straight line

## Slide 8: What if we knew how many points were missing?
Suppose we knew exactly how many points were missing, but not sure of the x values?
We can add the points and use Inspection Option 1

## Slide 9: Add Missing points Restores original fit (Inspection Option 1)
The points now plot at correct position, and we have pve = 100%
On Right tail, we add suspensions, since inspection plots the top of the stack.
Add points at end of a gap

## Slide 10: Comparison
The following slide shows the 4 fits
Note that the final fit has the same B values and fits
The set with missing data is optimistic

## Slide 11: Set Comparison
t0 is optimistic at lower b values, and doesn’t fit the upper part well

## Slide 12: How can we decide how many points to add?
If we knew how many points to add, we could get back to near the original fit
This would give better estimates of life
Next slides cover Criteria, Benefits, and Methods
Tried several methods to estimate points to add

## Slide 13: Criteria and Benefits
Criteria
Appropriate model (Weibull, Lognormal, Normal)
Explanation of missing data
At least 100 points, no more than 20% missing
Adjusted fit is better
Distribution Analysis confirms best model selection.
Benefits
Alternative to Minimum Life Model
Parameter prediction closer to true value
Fit improvement may lead to better model
Improvement in life prediction

## Slide 14: Monte Carlo to check Exit Criteria
MC sample and fits calculated.
Points removed, new fit calculated
Points added per criteria choice
Best r²
Quadratic=0.
First point above line.
Any of first 3 points above line
Two of first 3 points above line with full data set
First point above fit line, or points 2 and 3 above line (Best choice for rank regression)
Minimum of 4 methods:
Average of 1st point above, Quadratic
For MLE, increase Discovery points until Minimum Life = 0

## Slide 15: Results Comparison
Ideally, the adjusted fit would equal the original fit
There is variation, because the variation of the points removed is lost and unknown.
Following charts show the median values of the adjusted fits correspond well to the original fits, using MRR (Median Rank Regression)
Monte Carlo sample size of 500.
  Remove 20 points on left
  Add exactly 20 points at first point
  Switch to Inspect Option 1
  Gives estimate of resulting variation
  Look at variation on B5 around 20%, and Beta around 4
  Repeated for 1000 sets

## Slide 16: Remove and add 20 points
B5 Before adjust
B5 After adj.
B5 Ideal Line
β before adj.
β adjusted

## Slide 17: Remove and add 20 points Impact on B5
Original: 18 < B5 < 22 Reduced: 24 < B5 < 29
Original: 18 < B5 < 22 Adjusted: 17 < B5 < 22
Best outcome when Exact # of points is used still has scatter, but is close to original data

## Slide 18: Remove and add 20 points Impact on β
β = 2
β = 4
4
6
β
Original: 3.8 < β < 4.2 Reduced: 4.6 < β < 5.3
Original: 3.8 < β < 4.2 Adjusted: 3.7 < β < 4.4

## Slide 19: Best Results
Previous slides show the impact if we knew EXACTLY how many points were missing. The adjusted points don’t go back to the straight line, because we have lost the variation in the first 20 points.
The following slide shows the results of using the best method for left tail missing data:
  Adding points until the first point goes above the fit line, OR
  Points 2 and 3 go above the fit line.
  Since half of the time the first point will be below the fit line, we then adjust the count down by 1 and see if there is a better fit.
  Similar logic for intermediate and right tail missing data
Note the variation in B5 and beta when points are missing (Reduced set), and how they are closer to the original values when adjusted

## Slide 20: Weibull Distribution Results
Original: 18 < B5 < 22 Reduced: 25 < B5 < 32
Adjusted: 15 < B5 < 27
Original: 3.8 < β < 4.2 Reduced: 4.6 < β < 5.5
Adjusted: 3.5 < β < 5.0
Best method. Median values are on target, but more scatter

## Slide 21: Large Sample sizes are necessary
Previous studies were with a sample size of 500.
Can we use this technique with smaller samples?
Yes, but there is much more variation. Look at the variation of the sets when we only had 10 missing points on a set of 100.
  The reduced sets are very optimistic.
    A B5 of 20 on the original set might be around 30 on the reduced set.
    Beta of 4 in the original set could be around 6.5 with the reduced set
  Adding points brought the medians back down to the original values, but there was more variation

## Slide 22: More Scatter with N=100
Original: 18 < B5 < 22 Reduced: 28 < B5 < 39
Adjusted: 11 < B5 < 30
Original: 3.8 < β < 4.2 Reduced: 5.1 < β < 8.2
Adjusted: 2.9 < β < 6.5
Smaller sets and increased % of missing points increase scatter

## Slide 23: Method Summary
Method can reasonably estimate missing data (left-tail, intermediate, right-tail) for Weibull, Normal, and Lognormal data
Suitable data set (>100 observations, reason for missing data, no large quantity of right suspensions)
Use Rank Regression. Turn off t0 minimum life, turn on Inspection option
Add failures(suspensions) until exit criteria are reached: 1st point above, or next 2 points above.
Review results. (Better fit, <20% added points)

## Slide 24: MLE: Maximum Likelihood Estimation
MLE can be used to estimate left tail missing points
Calculate MLE with a minimum life, t0. If t0 is >0, then there is a curve. Add points as discoveries at the first observation until t0 = 0, indicating no curvature. Then turn t0 off.
  Discoveries and t0 are inherently incompatible because they are two different techniques to address a similar issue. But they are used together in this method to determine points to add.
MRR (Median Rank Regression) can be used to calculate missing parts, and then an MLE solution can be applied. MRR and MLE will be similar fits.

## Slide 25: Example – Fig 3-11 in Handbook
Buried cables were installed in 1971, 1972, and 1973.
In 1976, the utility started recording data, but there were no records from prior years.
Method shown in the handbook is to use a t0, which is an acceptable method. Lets look at how a Missing Data Analysis would compare

## Slide 26: Fig 3-11, NWH

## Slide 27: Using SuperSMITH™ with missing data
Open Fig3-11. This is in the SmithDat directory provided with the software
Clear the t0. Click Icon, and select N, Reset All
Change the method to rank regression and select inspection option #1
Select the Missing Data icon under the tools group
Select 1971

## Slide 28: Verify options, then select OK or Activate

## Slide 29: Results
Adds 67 points
Less than 20% points added
Comparison of parameters
Click to Add to plot as new set

## Slide 30: New line for 1971 data on plot

## Slide 31: Repeat for other years
You can repeat for the other years
The following graphic shows all 3 sets with rank regression and MLE solutions.
  Fits are very similar (Compare beta, eta, B values)

## Slide 32: Vintage Cables missing data
‘71 rr 67 pts
mle 53 pts
‘72 rr 22 pts
mle 15 pts
‘73 rr 61 pts
mle 64 pts
MLE
mle
rr

## Slide 33: Comments
Method is based on Rank Regression (Least Squares) fits.
MLE can be used to optimize for missing left tail data, or to plot MRR results for intermediate or right tail
Number of required points for analysis and maximum percentage of points added is a recommendation, not a hard number based on simulations. Use judgement in your conditions.
Use caution if you have many right-tail suspensions. (More than 30%) It could be a batch issue
Method applies to other distributions (like lognormal), but they are not programmed yet