## Slide 1: Weibull Library Organization Data Collection Recommendations
Wes Fulton & Carl Tarum
SuperSMITH™ 6.0AA (Released December 2021)and later

## Slide 2: Weibull Library Goals
Searchable index of previous results
Summary of analysis + reference to full data
Simple text format for future flexibility
Save intermediate file (w/ later verification)
Standard organization
  No more than 20 fields
  Essential universal info
  Additional info in comments

## Slide 3: Weibull Library
Most Important Part of Weibull Engineering
  Useful as Lessons-Learned database
  Enables and justifies Weibayes for improved results
Software Can Help Easily Generate Library Items after Each Analysis
Easily Generate Library Items

## Slide 4: Many Features in New Library
Load a reference file to look for data
Search or reset the reference file

## Slide 5: Use Menu to Review or Update choices
Can copy type/Comment from set 1 to rest of the sets
Each data set gets its own line in the output
Cyan with “"ø“: Data from plot (no change)
Green with “"•“: Data Entered. (can change)
Yellow with “"o“: Data needed. (Click to change)

## Slide 6: Fixed List Menu Items
Most menu items are from Defined Lists.
Choose the most appropriate
Example when “Device” is selected

## Slide 7: Variable Entry items (Comments)
1. Optional: Click a template.
(“Part #:” or “Part Name:”)
2. Add to the text, or replace it
Part #: 12345

## Slide 8: Copy/Save the Data
Each Copy/Save will save one data set from the file. If you have 3 data sets in the file, you will need to do 3 “saves” to save them.
Turn the Headers/Titles On or Off
Copy to clipboard to paste into Excel or other database
Save this Data set to the current Data File

## Slide 9: Each Weibull Library Record (* = Automatic From Analysis)
* Path\Filename of complete analysis … (update if changed)
* Title … at top of Weibull plot
* Date record created … YYYY-MM-DD
* By … person saving the record … including password ID designation …
Type of device … bearing, seal, housing, shaft, solder joint, connector, IC, lamp...
Type of equipment … actuator, motor, valve, pump, conveyor, controller, display …
Type of mechanism (root cause) … fracture, thinning, leaking, open-circuit, mixed ..
Type of customer duty cycle … continuous, on-off schedule, load level, impact …
Type of environment … humid, hot, sub-zero, 20DegC-35DegC, vibration, shock …
* Model type … W, N, L, G-, G+ …
* Fit type … rr, rrs, mle, RBAmd, …
* Confidence type … pvD90, fm-95, ...
* Data units … hours, cycles, months, miles, inches, degK, ...
* Data typical value … Eta, Mu, MuAL, Xi (lo-med-hi) …
* Data variability value … Beta, Sigma, SigF, Del (lo-med-hi) …
* Data t0 value … t0 (lo-med-hi value) …
Comment fields(Qty = 4) … customizable for each individual library
* Set(Set Number)Set size/Suspensions

## Slide 10: Weibull Library Comment Field Possibilities
Comment 1: Detailed Item Description
  Part Number
  Part Name
Comment 2: Detailed Application Description
  Product Line or Product Model
  Customer
  Military or Non-Military
Comment 3: Detailed Time Period
  Record Reference Number
  Beginning of Period to End of Period (Calendar Time)
Comment 4: References
  Report Number
  Test Procedure

## Slide 11: WLR_Smithdat.csv File (Typical Weibull Library File) 1 Header Row and 2 Records Shown
Path\File,Title 1,Date,By,Device,Equipment,Cause,Duty,Environment,Model,Fit Method,Confidence,Unit,Typical (Lo/Med/Hi),Variability (Lo/Med/Hi),t0 (Lo/Med/Hi),Comment 1,Comment 2,Comment 3,Comment 4,Set()n/s
C:\Smithdat\18WHEELR.W,18 Wheeler Steering Failures,Y2020M05D09,rba,,,,,,W2P,RR,,miles,69362,3.2569,,,,,,Set(1)10010/10000
C:\Smithdat\BWSOPAC.W,Southern Pacific BiWeibull,Y2020M05D09,,,,,,,W2P,RR,U90,units,242.62,1.194,,,,,,Set(1)304/238
NOTE: Can aggregate individual data files into a Master File

## Slide 12: Under the hood
In the %appdata% directory, there is an ini
  SSWLib.ini
    Stores Definition Files and Reference Files
Definition File (Usually starts with “WLD”
  Defines Data file, Headers, and what user can change.
Reference File (Usually starts with “WLR”)
  Typically a modified data fie, but can have any number of columns and rows
Data File (Usually starts with “WD”)
  Data saved by SuperSMITH™ according to the Definition File.

## Slide 13: Coming Soon..
Ability to customize Definition Files
Added documentation on protecting and backing up your reference data. Treat it like product drawing information for backup and security.
Additional guides to setting up a library.