## Slide 1: Weibull Library Organization Data Collection Recommendations
<number>
Wes Fulton
SuperSMITH™ 5.0DT (December 2021) and EARLIER

## Slide 2: Weibull Library Goals
<number>
Searchable index of previous results
Summary of analysis + reference to full data
Simple text format for future flexibility
Save intermediate file (w/ later verification)
Standard organization
  No more than 20 fields
  Essential universal info
  Additional info in comments

## Slide 3: Weibull Library
<number>
Most Important Part of Weibull Engineering
  Useful as Lessons-Learned database
  Enables and justifies Weibayes for improved results
Software Can Help Easily Generate Library Items after Each Analysis
Easily Generate Library Items

## Slide 4
<number>
C…Save Library Item As Text Line Upon File Save
D…(TBD) Add Library Item To Library -----------------
E…(TBD) Edit Library --------------------------------------
F…(TBD) Find / View Former Results In Library ------
1. Get search input from user … load into items
2. Search LIB-W-FF.TXT for related record(s)
3. Show located information
1. Put present results into items for record
2. Search LIB-W-FF.TXT for related record(s)
3. If similar then insert record there, ELSE append
1. Add, alter, delete records in LIB-W-FF.TXT
NOTE(1): A password may be needed for options D,E,F. Each password is scrambled and saved in an intialization file.
NOTE(2): Phantom duplicate library file needed for safety.
(No Password)
Software Weibull Library Selections
(For typical library file LIB-W-FF.TXT)

## Slide 5: Each Weibull Library Record (* = Automatic From Analysis)
<number>
* Path\Filename of complete analysis … (update if changed)
* Title … at top of Weibull plot
* Date record created … YYYY-MM-DD
* By … person saving the record … including password ID designation …
Type of device … bearing, seal, housing, shaft, solder joint, connector, IC, lamp...
Type of equipment … actuator, motor, valve, pump, conveyor, controller, display …
Type of mechanism (root cause) … fracture, thinning, leaking, open-circuit, mixed ..
Type of customer duty cycle … continuous, on-off schedule, load level, impact …
Type of environment … humid, hot, sub-zero, 20DegC-35DegC, vibration, shock …
* Model type … W, N, L, G-, G+ …
* Fit type … rr, rrs, mle, RBAmd, …
* Confidence type … pvD90, fm-95, ...
* Data units … hours, cycles, months, miles, inches, degK, ...
* Data typical value … Eta, Mu, MuAL, Xi (lo-med-hi) …
* Data variability value … Beta, Sigma, SigF, Del (lo-med-hi) …
* Data t0 value … t0 (lo-med-hi value) …
(Qty = 4) Comment fields … customizable for each individual library

## Slide 6: Weibull Library Comment Field Possibilities
<number>
Comment 1: Detailed Item Description
  Part Number
  Part Name
Comment 2: Detailed Application Description
  Product Line or Product Model
  Customer
  Military or Non-Military
Comment 3: Detailed Time Period
  Record Reference Number
  Beginning of Period to End of Period (Calendar Time)
Comment 4: References
  Report Number
  Test Procedure

## Slide 7: LIB-W-FF.TXT File (Typical Weibull Library File) 1 Header Row and 2 Records Shown
<number>
“Path/file”, “Title”, “Date”, “By”, “Device”, “Equipment”, “Cause”, “Duty”, “Environment”, “Model”, “Fit”, “Confidence”, “Units”, “Typical (lo/med/hi)”, “Variability (lo/med/hi)”, “t0 (lo/med/hi)”, “Comment1”, “Comment2”, “Comment3”, “Comment4”
“H:\data\motor3.w”, “Cyclone 447 Prototype”, “2002/06/25”, “WF(CY4P)”, “Housing”, “Motor”, “Fracture”, “Continuous@180% N. O. Load”, “90% Humidity”, “Weibull”, “rr”, “pvD90”, “Hours”, “4.3/8.7/11.5”, “2.8/3.6/5.1”, “0/0/0”,”Part#=55232”,”Name=Tri-Cities Traction”, “Analysis 1997/03/01 - 2001/08/22”, “Reliability Report R-887”
“H:\data\valve16.w”, “Series II Bypass Valve”, “2002/07/04”, “WF(CY4P)”, “Set(1)Journal Bearing:Set(2)Journal Bearing”, “Set(1)Valve:Set(2)Valve”, “Set(1)Contamination:Set(2)Contamination”, “Set(1)Pressure=32psi:Set(2)Pressure=27psi”, “Set(1)320degK:Set(2)340degK”, “Weibull”, “rr”, “pvD90”, “Cycles”, “Set(1)20015/24552/32813:Set(2)38744/43272/48923”, “Set(1)2.3/2.9/3.5:Set(2)1.8/2.2/2.6”, “Set(1)0/415/0:Set(2)0/-1352/0”, “Part#=61248”, “Name=S2”, “Analysis 1995/07/15 - 2002/02/19”, “Warranty Analysis Report W-293”
NOTE(1): The “:” sign (colon) is used for the entry separator … for example for multiple data sets
NOTE(2): Can aggregate individual LIB-W-FF.TXT files into Master Library...