## Slide 1: Network Training BY “ITChefrobin”

## Slide 2: Networking Basics

## Slide 3: Internet Service Providers
Internet
Service
Provider
(ISP)
An Internet Service Provider (ISP) provisions any building, allowing users to build networks to connect to the web. We’ll use Comcast in this example
There are loads of ISPs, but typically any building is limited to the providers in their area. Dense urban areas will likely have multiple options, while more rural areas might be restricted to only smaller, local and independent ISPs.
Although most big-name ISPs will provide internet that is strong and fast enough for Brink, it’s important to know a customer’s ISP. A local provider may only offer relatively slow speeds due to rural infrastructure

## Slide 4: Let’s build a simple network
Internet
Service
Provider
(ISP)
An Internet Service Provider (ISP) provisions any building, allowing users to build networks to connect to the web. We’ll use Comcast in this example

## Slide 5: Modems
ISP
Modem
A modem is the is the physical piece of equipment that allows a user to connect to the ISP. Think of this as the power outlet for internet in a building.
The modem will need to be connected to wherever the ISP has provisioned cables in the building. In restaurants, this is often the back office, basement or IT closet.
Modems are usually provided by the ISP. The only real thing to consider as a sales rep regarding modems is where they are in the building.

## Slide 6: Routers
ISP
Modem
Router
The router is the piece of equipment that takes internet from the modem, creates a network and “routes” it to devices (like tablets or laptops) to make it accessible.
Routers can create wired or wireless networks that allow devices to access the internet.
Different routers will have unique features and abilities. Speed, maximum number of connected devices, wired vs. wireless connection (or both), wireless coverage strength/distance, support tools/analytics, and more are all factors that your choice of router will affect.

## Slide 7: Types of Routers 1
Meraki Z1 Router
Network Type: Wired or Wireless
Wireless Coverage: Approx. 1000 square feet
Maximum # of Connected Devices: Approx. 10 devices
Offers Cloud Analytics and support tools (Toast support remote access and troubleshooting)
4 Ethernet ports for hard wired connections
The Z1 is The essential small deal workhorse. It’s relatively inexpensive, provides strong cloud analytics and creates a wireless network that covers most small spaces. For basic setups with under 10 devices, the Z1 covers all the bases. 3 Year Cloud license included with purchase.

## Slide 8: Types of Routers 2
Meraki MX64 Router
Network Type: Wired only
Wireless Coverage: None - requires access points to create Wi-Fi Network
Maximum # of Connected Devices: Approx. 100 devices
Offers Cloud Analytics and support tools (Toast support remote access and troubleshooting)
4 Ethernet ports for hard wired connections
The MX64 is a big step up from the Z1 and covers all setups larger than 10 connected devices. It is a more robust router that is essential for larger installs. It does not create a wireless network on its own, so if your deal needs Wi-Fi (even in a small space), an access point will be necessary. 3 Year Cloud License included with purchase.

## Slide 9: Next step… devices!
ISP
Modem
Router
Now that we know about the differences in the routers, let’s start connecting devices! Let’s pretend we are using a Z1 to start - so that we can hardwire, as well as wirelessly connect devices.

## Slide 10: Next step… devices!
ISP
Modem
Z1
Let’s start with hardwiring some terminals

## Slide 11: Hardwiring
ISP
Modem
Z1
Terminal 1

## Slide 12: Hardwiring
ISP
Modem
Z1
Terminal 1
Terminal 2

## Slide 13: Hardwiring
ISP
Modem
Z1
T1
T2
T 4
T 3

## Slide 14: Hardwiring
ISP
Modem
Z1
T 1
T2
T 4
T 3
T5
!?

## Slide 15: Uh oh...
The Z1 only has 4 ethernet ports, and we have 5 terminals that need to be hardwired.
What happens now?

## Slide 16: Switches
Here is where switches come in!
A switch is basically a splitter, or power strip for ethernet. We can use a switch to turn 1 port into multiple ports! Simply plug the switch into the router, then plug the terminals into the switch.

## Slide 17: Switches
Here is where switches come in!
A switch is basically a splitter, or power strip for ethernet. We can use a switch to turn 1 port into multiple ports! Simply plug the switch into the router, then plug the terminals into the switch.
All hardwired PAR/Brink Terminals, printers and access points (which we’ll cover soon) need to be connected to the router somehow. Depending on the situation, you could need anywhere from 1 to 100 ethernet cables to connect to a single router. Toast has a variety of switches available to cover all possible setups.

## Slide 18: Switches
4-5 Port Switch
8 Port Switch
16 Port Switch
Switches are simple. You just need the correct number of ports covered.
These are the basic switches. Once we cover access point’s we’ll look at more advanced switches.
Pro Tip: Switches also allow you to be more flexible with wiring. If you have 5 terminals upstairs that need to be hardwired, but your modem and router are in the basement, you could use a switch to connect all the terminals upstairs, and only have to run one ethernet cable to the basement, saving a ton of time and energy.

## Slide 19: Hardwiring
ISP
Modem
Z1
T 1
T 2
T 4
T3
T5
Switch

## Slide 20: Hardwiring
ISP
Modem
Z1
T1
T 2
T 4
T 3
T 5
Switch
Problem solved!

## Slide 21: If we add more equipment...
ISP
Modem
Z1
T 1
T 2
T 4
T3
T 5
Switch
All the same rules apply. Even when the setup starts to look more complicated - it’s just connecting wires and getting them to the router.

## Slide 22: If we add more equipment...
ISP
Modem
Z1
T 1
T 2
T4
T3
T5
Switch
There are endless potential combinations as the # of ports increase.
Kitchen Printers

## Slide 23: If we add more equipment...
ISP
Modem
Z1
T1
T2
T 4
T3
T 5
Switch
Add another switch, and connect to the first switch?
Kitchen Printers

## Slide 24: If we add more equipment...
ISP
Modem
Z1
T 1
T2
T 4
T3
T5
Switch
Add another switch,
and connect to the router?
Kitchen Printers

## Slide 25: If we add more equipment...
ISP
Modem
Z1
T 1
T 2
T 4
T 3
T5
Switch
Add a bigger switch? 16 Port
Kitchen Printers

## Slide 26: Just focus on the basics
Networking can seem overwhelming to many people. In reality, the basic rules of networking are quite simple.
Every device needs to connect to the router, if there isn’t space, make some!

## Slide 27: Speaking of devices,
Before diving into how wireless works, first let’s make sure we all agree what a “device” is (with regards to networking).

## Slide 28: Speaking of devices
Before diving into how wireless works, first let’s make sure we all agree what a “device” is (with regards to networking).
A device is any object connected to the router to access the internet
that has an IP Address.

## Slide 29: What’s an IP Address?
Simply put, an
IP address
is the unique identifier for a device that is assigned when it connects to the router. This allows the router to differentiate between devices.

## Slide 30: What’s an IP Address?
Simply put, an
IP address
is the unique identifier for a device that is assigned when it connects to the router.
This allows the router to differentiate between devices.
Easy example: Bob and Mary both have tablets in the same room as a router. Bob connects to the router’s wireless network by entering the password. The router assigns Bob’s tablet the IP address - 192.168.1.1 and starts routing internet to the tablet. Bob’s on the web! Mary, however, isn’t on the web, since she hasn’t connected to the network by entering the password. That means the router doesn’t know how to route internet to Mary’s tablet, since it doesn’t have an IP address to send it to.

## Slide 31: So, what has an IP address?
The devices with IP addresses
(relevant to Brink, that is)
are:
Tablets (Terminals, Handhelds, KDS - ANY tablet)
Printers
Access Points (which we’ll cover in just a moment)

## Slide 32: So, what has an IP address?
The devices with IP addresses (relevant to Brink, that is) are:
Tablets (Terminals, Handhelds, KDS - ANY tablet)
Printers
Access Points (which we’ll cover in just a moment)
So if my restaurant has 2 Terminals, 1 Handheld, 1 Receipt printer, 2 Kitchen printers and 2 Access Points - you could say I have 8 devices with IP addresses that need to connect to the router and access the internet.

## Slide 33: Why does this matter?
If you remember the slides on Brink routers, you’ll remember that each router has a maximum number of devices
it can support.

## Slide 34: Why does this matter?
If you remember the slides on Brink routers, you’ll remember that each router has a maximum number of devices it can support.
Meraki Z1
Maximum # of Devices: Approx. 10

## Slide 35: Why does this matter?
If you remember the slides on Brink routers, you’ll remember that each router has a maximum number of devices it can support.
Meraki Z1
Maximum # of Devices: Approx. 10
Meraki MX64
Maximum # of Devices: Approx. 100
So the number of devices affects our router choice.

## Slide 36: Don’t fall for the easy mistake!
Number of Devices
does not equal
Number of Tablets.
A tablet is just one of the
3 types of devices.

## Slide 37: Don’t fall for the easy mistake!
Number of Devices
does not equal Number of Tablets.
A tablet is just one of the 3 types of devices.
Common mistake:
“It’s just a simple 6 Terminal setup - a Z1 will be fine”

## Slide 38: Don’t fall for the easy mistake!
Number of Devices
does not equal Number of Tablets.
A tablet is just one of the 3 types of devices.
Common mistake:
“It’s just a simple 6 Terminal setup - a Z1 will be fine”
Not necessarily - you need to account for printers and access points as well. If the total number of Tablets + Printers + Access points is ≤ 10, then a Z1 will do. If that total number of devices is > 10, then you will need an MX64.

## Slide 39: Now that we all agree,
Let’s dive into wireless. We’ll go back to our original network setup and remove the hardwired terminals to keep things simple.

## Slide 40: Wireless
ISP
Modem
Z1
Alright, back to the Z1 Network we set up.
We learned earlier that the Z1 can broadcast a wireless network and cover approx. 1000 square feet. Let’s add some wireless devices!

## Slide 41: Wireless
ISP
Modem
Z1
Handheld 1

## Slide 42: Wireless
ISP
Modem
Z1
Handheld 1
Handheld 2

## Slide 43: Wireless
ISP
Modem
Z1
Handheld 1
Handheld 2
Handheld 3

## Slide 44: Wireless
ISP
Modem
Z1
Handheld 1
Handheld 2
Handheld 3
Now we’ll look at distance. Let’s outline what 1000 square foot coverage looks like coming from the Z1:

## Slide 45: Wireless
ISP
Modem
Z1
Handheld 1
Handheld 2
Handheld 3
Wireless Network Coverage

## Slide 46: Wireless
ISP
Modem
Z1
Handheld 1
Handheld 2
Handheld 3
Wireless Network Coverage
Looks like Handhelds 1 and 2 are covered, but Handheld 3 is outside of the range of the Z1. We’ll need to extend the coverage somehow, or Handheld 3 won’t be able to access the Internet

## Slide 47: Cue Access Points!
An Access Point
serves as a wireless network extender. Access Points allow us to cover large spaces with
Wi-Fi
so that customers can take advantage of Toast’s wireless solutions.

## Slide 48: Cue Access Points!
An Access Point
serves as a wireless network extender. Access Points allow us to cover large spaces with
Wi-Fi
so that customers can take advantage of Brink’s wireless solutions.
Brink offers 3 Access Points to cover all scenarios:

## Slide 49: Types of AP’s (1)
Open Mesh Dual Band Access Point
Standard go-to Access Point used in all basic scenarios. These are the least expensive AP’s that are used to easily extend wireless over large or tricky spaces.

## Slide 50: Types of AP’s (2)
Open Mesh Dual Band Access Point
Standard go-to Access Point used in all basic scenarios. These are the least expensive AP’s that are used to easily extend wireless over large or tricky spaces.
Each Dual Band will cover approx. 1000 square feet of space in addition to the Z1.
This AP does not have any advanced features.

## Slide 51: Types of AP’s (3)
Open Mesh MR1750 Access Point
The step up from the Dual Band, the MR1750 covers a slightly larger range and provides some additional features.

## Slide 52: Types of AP’s (3)
Open Mesh MR1750 Access Point
The step up from the Dual Band, the MR1750 covers a slightly larger range and provides some additional features.
The MR1750 has cloud analytics & support tools, so as wireless configurations become more complex and demanding, the MR1750’s supportability becomes well worth the very slight price increase from the Dual Band.

## Slide 53: Types of AP’s (4)
Meraki MR18 Access Point
The MR18 is the most powerful access point Brink offers, with advanced cloud support tools and an extremely robust network strength.

## Slide 54: Types of AP’s (4)
Meraki MR18 Access Point
The MR18 is the most powerful access point Toast offers, with advanced cloud support tools and an extremely robust network strength.
The MR18 is the premium access point, but also comes with a premium price tag. However, any technically demanding setup (heavy reliance on wifi, many handhelds) will need to consider the MR18 for it’s reliability and support tools.

## Slide 55: Wireless
ISP
Modem
Z1
Handheld 1
Handheld 2
Handheld 3
Wireless Network Coverage
Now, let’s use an access point to help get Handheld 3 onto our wireless network.

## Slide 56: Wireless
ISP
Modem
Z1
Handheld 1
Handheld 2
Handheld 3
Wireless Network Coverage
Thanks Access Point!

## Slide 57: What about MX64s?
Remember, although Z1 Routers can broadcast wirelessly (as well as support hardwired connections), the
MX64
does not broadcast wirelessly out of the box.

## Slide 58: What about MX64s?
Remember, although Z1 Routers can broadcast wirelessly (as well as support hardwired connections), the MX64 does not broadcast wirelessly out of the box.
If you need an MX64 router for your setup, and need wireless, you just need to add an access point.

## Slide 59: MX64
ISP
Modem
Z1
Handheld 1
Handheld 2
Handheld 3
Wireless Network Coverage
Switch to MX64

## Slide 60: MX64
ISP
Modem
MX64
Handheld 1
Handheld 2
Handheld 3
Notice we lose our wireless network when switching to the MX64. Let’s add an access point to fix this

## Slide 61: MX64
ISP
Modem
MX64
Handheld 1
Handheld 2
Handheld 3

## Slide 62: MX64
ISP
Modem
MX64
Handheld 1
Handheld 2
Handheld 3

## Slide 63: Basics Recap

## Slide 64: What we’ve covered
Basic Hardware
  Routers, Switches, Access Points
Internet Basics
  ISP, Modems, Hardwired and Wireless connections
Some Specifics
  IP addresses, varying combinations, router nuances

## Slide 65: Advanced Networking

## Slide 66: Let’s pick up where we left off
At the end of Networking Basics training, we covered setting up access points with routers to extend wireless coverage.
There is one thing we overlooked though...

## Slide 67: MX64
ISP
Modem
Handheld 1
Handheld 2
Handheld 3
Here is our last setup, where we added an AP to cover some handhelds. Simple enough! Let’s remove some things to clear up some space.
MX64

## Slide 68: Our previous setup
ISP
Modem
MX64
What we didn’t consider, is how that access point is going to be powered. Just like all our other electronics, this AP is going to need power!
We know that the AP needs to be connected to the router to establish an internet connection.

## Slide 69: Our previous setup
ISP
Modem
MX64
There we go. Let’s focus on this access point.
We know that the AP needs to be connected to the router to establish an internet connection.

## Slide 70: Our previous setup
ISP
Modem
MX64
Access points are generally placed where they provide the best coverage. Often this means mounting them to a wall or drop ceiling.

## Slide 71: Our previous setup
ISP
Modem
MX64
Access points are generally placed where they provide the best coverage. Often this means mounting them to a wall or drop ceiling.
Unless you get lucky, there probably will not be a power outlet where you happen to need your access point installed.

## Slide 72: Our previous setup
ISP
Modem
MX64
Access points are generally placed where they provide the best coverage. Often this means mounting them to a wall or drop ceiling.
Unless you get lucky, there probably will not be a power outlet where you happen to need your access point installed.
That’s where PoE comes in

## Slide 73: Power over Ethernet (PoE)
Power over Ethernet
allows you to send electricity through an ethernet cable to power a PoE compatible device.

## Slide 74: Power over Ethernet (PoE)
Power over Ethernet
allows you to send electricity through an ethernet cable to power a PoE compatible device.
With PoE equipment, you can turn any ethernet cable into an internet/electric hybrid.

## Slide 75: PoE Injector
PoE Injector - for a single device
Plug the router to the injector via ethernet, then plug the injector to the access point via ethernet and plug the injector to an outlet with an adapter.

## Slide 76: PoE Injector
PoE Injector - for a single device
Plug the router to the injector via ethernet, then plug the injector to the access point via ethernet and plug the injector to an outlet with an adapter.
In other words, just put a PoE injector in between the router and the access point along the ethernet cable to provide power! This gives you the freedom to place the AP wherever you need, and the PoE will provide power from the source.

## Slide 77: How PoE works
MX64
AP
Ethernet cable
PoE

## Slide 78: How PoE works
MX64
AP
Ethernet cable
PoE
Connect to outlet
Device is powered!

## Slide 79: But what about multiple devices?
Now we know how to handle that tricky access point that needs power. But what if there are multiple access points?
Of course you could just use multiple PoE injectors. In fact for 1, 2 or 3 access points, that is probably your best bet. Once you start to encounter more than a few access points needing PoE, however, having lots of individual PoE injectors all plugged into outlets near the router gets cumbersome, and more difficult to manage

## Slide 80: The PoE Switch
Netgear Prosafe 16 Port PoE Switch
PoE + Switch = PoE Switch
Looks just like a regular switch, but every port can be enabled with PoE to accommodate multiple devices!
PoE switches can be used just like a regular switch that also offers PoE. This means you can use a PoE switch for all ethernet devices and provide the necessary APs with electricity.

## Slide 81: The PoE Switch
Netgear Prosafe 16 Port PoE Switch
PoE + Switch = PoE Switch
Looks just like a regular switch, but every port can be enabled with PoE to accommodate multiple devices!
PoE switches can be used just like a regular switch that also offers PoE. This means you can use a PoE switch for all ethernet devices, and provide the necessary APs with electricity.

## Slide 82: What else?
So now we can build a simple wired network, a simple wireless network, make sure all ethernet ports are accounted for with switches, cover large wireless network areas with access points
AND make sure those Aps
are powered with PoE.

## Slide 83: What else?
So now we can build a simple wired network, a simple wireless network, make sure all ethernet ports are accounted for with switches, cover large wireless network areas with access points AND make sure those APs are powered with PoE.
Is there anything else we need to consider
when building these networks?

## Slide 84: 1 Simple Exception
There is 1 Simple Exception that you should be aware of when building simple networks, and it has to do with running access points in wireless setups.
Let’s go back to a wireless setup with a Z1 and an Open Mesh Access Point

## Slide 85
ISP
Modem
Z1
Handheld 2
Handheld 3
So here we are - this setup has a Z1 broadcasting a wireless network (covering roughly 1,000 square feet), and a single open mesh access point covering another 1,000. Together, they cover all the handhelds, right?
Handheld 1

## Slide 86
ISP
Modem
Z1
Handheld 2
Handheld 3
The networks that Z1’s broadcast and the networks that Open Mesh APs broadcast are actually slightly different. Think of them as “speaking different languages”.
You can encounter issues when you allow both to broadcast simultaneously.
Handheld 1

## Slide 87
ISP
Modem
Z1
Handheld 2
Handheld 3
If Handheld 3 moved from where it is now (connecting to the Open Mesh AP) into the coverage of the Z1…
It would have to jump from “speaking 1 wireless language to another”. This would cause issues for the tablet, that’s just trying to connect to the internet.
?
Handheld 1

## Slide 88
This sort of interference can really disrupt the handheld user’s experience. We need to make it easy for the tablet to connect to the internet, so service isn’t interrupted. To do this, we just need to make sure all the devices broadcasting wireless are “speaking the same language”.

## Slide 89
ISP
Modem
Z1
Handheld 2
Handheld 3
If Handheld 3 moved from where it is now (connecting to the Open Mesh AP) into the coverage of the Z1...

## Slide 90
This sort of interference can really disrupt the handheld user’s experience. We need to make it easy for the tablet to connect to the internet, so service isn’t interrupted. To do this, we just need to make sure all the devices broadcasting wireless are “speaking the same language”.
Since Open Mesh access points all speak the same language, we can build networks with Open Mesh that tablets can wander through without worrying about interference or speaking different languages.

## Slide 91
✅
This sort of interference can really disrupt the handheld user’s experience. We need to make it easy for the tablet to connect to the internet, so service isn’t interrupted. To do this, we just need to make sure all the devices broadcasting wireless are “speaking the same language”.
Since Open Mesh access points all speak the same language, we can build networks with Open Mesh that tablets can wander through without worrying about interference or speaking different languages. Just like when you’re roaming on a cell phone, you can move between 2 different towers’ coverage areas without dropping the call - wireless works the same way!

## Slide 92
ISP
Modem
Z1
Handheld 2
Handheld 3
So in our original example, we just have to turn off the Z1 from broadcasting, so our 2nd language isn’t disruptive.
Handheld 1

## Slide 93
ISP
Modem
Z1
Handheld 2
Handheld 3
So in our original example, we just have to turn off the Z1 from broadcasting, so our 2nd language isn’t disruptive.
Handheld 1

## Slide 94
ISP
Modem
Z1
Handheld 2
Handheld 3
Once the Z1 is not broadcasting, we can add another open mesh access point to broadcast in its place!
Handheld 1
Looks like we’re covered!
AP
AP

## Slide 95: The “Same Language” Rule
This “same language” rule applies to all wireless networking devices. You can’t mix a Meraki Z1’s signal with an Open Mesh AP’s signal. The same would go for mixing an Open Mesh AP and a Meraki MR18 AP.
Make sure to keep this in mind when adding access points to setups with Z1s. An 1,800 square foot space can’t use a Z1 + an Open Mesh, but rather needs 2 Open Mesh access points.

## Slide 96: Advanced Networking

## Slide 97: Advanced Recap
What we covered:
PoE (Power over Ethernet)
  PoE Injectors
  PoE Switches
The Same Language Rule
  Mixing Z1 Wireless signals with Open Mesh signals is a NO GO
  Wireless devices can move through “Same Language” space without issue

## Slide 98: Covering Complex Spaces

## Slide 99: Complex Space
So, we have a pretty good understanding of covering spaces with wireless routers and access points using different types of equipment, and the rules that come along with them (POE, switches, POE switches, APs, the “Same Language Rule”, etc.)

## Slide 100: Complex Space
So, we have a pretty good understanding of covering spaces with wireless routers and access points using different types of equipment, and the rules that come along with them (POE, switches, POE switches, APs, the “Same Language Rule”, etc.)
When it comes to wireless installs, we know our basic rule of thumb is 1 access point for every 1,000 square feet. But as we all know, not all restaurants are segmented into perfect 1,000 sq. ft bubble shapes to make it easy on our access points...

## Slide 101: Complex Space
So, we have a pretty good understanding of covering spaces with wireless routers and access points using different types of equipment, and the rules that come along with them (POE, switches, POE switches, APs, the “Same Language Rule”, etc.)
When it comes to wireless installs, we know our basic rule of thumb is 1 access point for every 1,000 square feet. But as we all know, not all restaurants are segmented into perfect 1,000 sq. ft bubble shapes to make it easy on our access points…
Multiple floors, multiple rooms, extremely large spaces, building materials and intended use are just a few of the many factors considered when building a network

## Slide 102: Building Materials
Wireless signals are simple radio waves and behave like them. That means the materials they travel through matter.

## Slide 103: Building Materials
Wireless signals are simple radio waves and behave like them. That means the materials they travel through matter.
Simply put - Radio waves do not travel well through metal, brick, or very thick concrete walls or spaces. The worse the material, the weaker the signal

## Slide 104: Building Materials
Wireless signals are simple radio waves and behave like them. That means the materials they travel through matter.
Simply put - Radio waves do not travel well through metal, brick, or very thick concrete walls or spaces. The worse the material, the weaker the signal
Glass, thin wood

## Slide 105: Building Materials
Wireless signals are simple radio waves and behave like them. That means the materials they travel through matter.
Simply put - Radio waves do not travel well through metal, brick, or very thick concrete walls or spaces. The worse the material, the weaker the signal
Glass, thin wood
Thicker wood, thin concrete

## Slide 106: Building Materials
Wireless signals are simple radio waves and behave like them. That means the materials they travel through matter.
Simply put - Radio waves do not travel well through metal, brick, or very thick concrete walls or spaces. The worse the material, the weaker the signal
Glass, thin wood
Thicker wood, thin concrete
Brick, thin metal

## Slide 107: Building Materials
Wireless signals are simple radio waves and behave like them. That means the materials they travel through matter.
Simply put - Radio waves do not travel well through metal, brick, or very thick concrete walls or spaces. The worse the material, the weaker the signal
Glass, thin wood
Thicker wood, thin concrete
Brick, thin metal
Thick Metal

## Slide 108: Careful with Materials!
Safe to say, don’t expect wireless to travel through brick walls or metal. Metal is very common in kitchens, so if wireless is needed in a kitchen (rare) make sure there is an access point inside the room.

## Slide 109: Careful with Materials!
Safe to say, don’t expect wireless to travel through brick walls or metal. Metal is very common in kitchens, so if wireless is needed in a kitchen (rare) make sure there is an access point inside the room.
This may factor into even smaller spaces. Let’s take a 1,400 sq. ft space - if it is just 1 room, you might get by with just 1 source of wireless. If it’s 2 separated rooms, the barrier will impede the signal.

## Slide 110: Careful with Materials!
Safe to say, don’t expect wireless to travel through brick walls or metal. Metal is very common in kitchens, so if wireless is needed in a kitchen (rare) make sure there is an access point inside the room.
This may factor into even smaller spaces. Let’s take a 1,400 sq ft space - if it is just 1 room, you might get by with just 1 source of wireless. If it’s 2 separated rooms, the barrier will impede the signal.
1,600 sq ft
*skewed to fit screen: AP range outline would be larger
✅

## Slide 111: Careful with Materials!
Safe to say, don’t expect wireless to travel through brick walls or metal. Metal is very common in kitchens, so if wireless is needed in a kitchen (rare) make sure there is an access point inside the room.
This may factor into even smaller spaces. Let’s take a 1,400 sq ft space - if it is just 1 room, you might get by with just 1 source of wireless. If it’s 2 separated rooms, the barrier will impede the signal.
1,600 sq ft
?
*skewed to fit screen: AP range outline would be larger

## Slide 112: Careful with Materials!
Safe to say, don’t expect wireless to travel through brick walls or metal. Metal is very common in kitchens, so if wireless is needed in a kitchen (rare) make sure there is an access point inside the room.
This may factor into even smaller spaces. Let’s take a 1,400 sq ft space - if it is just 1 room, you might get by with just 1 source of wireless. If it’s 2 separated rooms, the barrier will impede the signal.
1,600 sq ft
✅
*skewed to fit screen: AP range outline would be larger

## Slide 113: Where? The Most Important Question
Let’s look at 2 scenarios: a wired setup (no wireless) and a wireless setup and focus on what is important for each.

## Slide 114: Where? The Most Important Question
Let’s look at 2 scenarios: a wired setup (no wireless) and a wireless setup and focus on what is important for each.
Wired: Where are your PAR hardwired Terminals going to be? Are all the necessary terminated wires already run and available?

## Slide 115: Where? The Most Important Question
Let’s look at 2 scenarios: a wired setup (no wireless) and a wireless setup and focus on what is important for each.
Wired: Where are your Par hardwired Terminals going to be? Are all the necessary terminated wires already run and available?
Wireless: Where are you planning on using the wireless tablets? Is there wireless coverage available wherever the tablets will be?

## Slide 116: Where? The Most Important Question
Where tablets will be used is the most important question, as it influences the entire install. Let’s dive into each scenario again.

## Slide 117: Where? The Most Important Question
Where tablets will be used is the most important question, as it influences the entire install. Let’s dive into each scenario again.
Wired:
“Where do you want to use Par Terminals?”
  Are you currently using POS terminals in the same places? (existing ethernet wiring setup already available & can be reused)

## Slide 118: Where? The Most Important Question
Where tablets will be used is the most important question, as it influences the entire install. Let’s dive into each scenario again.
Wired:
“Where do you want to use Toast Terminals?”
  Are you currently using POS terminals in the same places? (existing ethernet wiring setup already available & can be reused)
  “Do you want a terminal where you currently do not have a POS terminal installed?” (this may require additional ethernet cable wiring & termination, which is a service PAR typically does not provide)

## Slide 119: Where? The Most Important Question
So the key with wired setups is looking where the current POS is being used, ensuring there is ethernet available there, and if there isn’t, that new wiring is addressed. Now let’s look at Wireless
Wireless:
“Where do you want to use your wireless PAR tablets?” (where will access points need to be placed to cover these tablets?)
Is there wiring available to install these access points?
“Are these tablets going to roam/leave a designated space?” (wherever the tablet might be used, coverage is needed. This could be just a single section - or it could mean the entire restaurant)

## Slide 120: Where where where?
“Where” can solve tons of problems and avoid unnecessary effort.
10,000 sq. ft space w/ handhelds?
“Where will you use them?” - Answer: “Oh, the handhelds are only used for the beer garden, which is only an 800 sq. ft space near the kitchen”.
  Only 1 AP needed. Crisis avoided

## Slide 121: Where where where?
“Where” can solve tons of problems and avoid unnecessary effort.
10,000 sq. ft space w/ handhelds?
“Where will you use them?” - Answer: “Oh, the handhelds are only used for the beer garden, which is only an 800 sq. ft space near the kitchen”.
  Only 1 AP needed. Crisis avoided
40,000 sq. ft space
“Where are you using PAR?” - Answer: “We are just using hard-wired terminals, and they are just replacing our existing terminals”
  No APs or wiring needed. Another crisis avoided

## Slide 122: Real Life Example
Let’s look at a real floorplan for a customer who was considering a bunch of hardwired terminals and 3-4 handhelds. Floorplans are always extremely helpful (and sometimes necessary) to collect.

## Slide 123
As you can see, this customer has a rather large space with a dining area, bar, a pool area, and outdoor beer garden, as well as some “in between” spaces.
This space is roughly 8,500 square feet

## Slide 124
As you can see, this customer has a rather large space with a dining area, bar, a pool area, and outdoor beer garden, as well as some “in between” spaces.
This space is roughly 8,500 square feet
If we just looked at this deal on paper, we would see: 8,500 sq feet and 4 handhelds - which would lead anyone to simply think…

## Slide 125
As you can see, this customer has a rather large space with a dining area, bar, a pool area, and outdoor beer garden, as well as some “in between” spaces.
This space is roughly 8,500 square feet
If we just looked at this deal on paper, we would see: 8,500 sq. feet and 4 handhelds - which would lead anyone to simply think…
“This deal needs 8-9 access points”

## Slide 126
Yikes! 8-9 access points is a lot and will be a notable expense for the customer. We better make sure that they are all necessary

## Slide 127
Yikes! 8-9 access points is a lot and will be a notable expense for the customer. We better make sure that they are all necessary
“Where do you hope to use the handhelds, Mr./Mrs. Customer?”

## Slide 128
Yikes! 8-9 access points is a lot, and will be a notable expense for the customer. We better make sure that they are all necessary
“Where do you hope to use the handhelds, Mr./Mrs. Customer?”
“We have the stationary terminals for the bar, beer garden and 1 for the pool area - we were thinking we could use them for the dining area and to help speed up the pool area”
Glad we asked...

## Slide 129
Looks like we only need wireless coverage here and here.
This significantly cuts back the networking equipment needs. The dining area totals about 800 sq. ft, and the pool area totals about 1,700 sq. ft.

## Slide 130
Looks like we only need wireless coverage here and here.
This significantly cuts back the networking equipment needs. The dining area totals about 800 sq. ft, and the pool area totals about 1,700 sq. ft.
Now we can strategically place our access points to cover the area. Here we can take into account walls/ceilings and existing ethernet cables run.
Let’s look at the relevant materials!

## Slide 131
What is this barrier made from?
As we learned, the material may influence how wireless propagates through it, and thus how we set up the network .

## Slide 132
What is this barrier made from?
As we learned, the material may influence how wireless propagates through it, and thus how we set up the network .
After asking the customer, it looks like that barrier isn’t a wall, just a low railing to divide the rooms with some cabinets to store electronics and host the stationary POS terminals. That means wireless won’t have much trouble traveling through it!

## Slide 133
What is this barrier made out of?
As we learned, the material may influence how wireless propagates through it, and thus how we set up the network .
After asking the customer, it looks like that barrier isn’t a wall, just a low railing to divide the rooms with some cabinets to store electronics and host the stationary POS terminals. That means wireless won’t have much trouble traveling through it!
Also, since there are electronics and stations for their current POS equipment there, this might be an ideal spot to plug in an access point or 2!

## Slide 134
Since we can hide them right in the cabinets, let’s put 2 APs along this barrier to cover the dining space as well as some of the pool area!

## Slide 135
Since we can hide them right in the cabinets, let’s put 2 APs along this barrier to cover the dining space as well as some of the pool area!
Note: this is a simplified image - it’s not great to have significant overlap between APs - they shouldn’t be too close to each other!

## Slide 136
Since we can hide them right in the cabinets, let’s put 2 APs along this barrier to cover the dining space as well as some of the pool area!
Note: this is a simplified image - it’s not great to have significant overlap between APs - they shouldn’t be too close to each other!
Now that the dining room is mostly covered, we should look at the pool area. What’s up with the walls around the perimeter of the pool room?

## Slide 137
Looks like these walls are made out of brick, and there aren’t any ethernet cables run through them.
Drilling through brick to run a cable isn’t going to be easy, and running a cable along the wall looks tacky & totally kills the ambiance (right?)
So if we can’t install an access point on the wall, where can we put it to finish covering the space?
Let’s look up!

## Slide 138
What is the ceiling of the pool room made from?
Looks like it’s a Drop Ceiling! Drop ceilings are ideal for running wires, since you can easily push up the ceiling tiles and move them back into place.
We can have a cable run and place the AP right where it needs to be to cover the space!

## Slide 139: Covering Complex Space Recap

## Slide 140: Covering Space Recap
What we covered:
Building Materials MATTER!
  Metal, Brick and thick Concrete are Wifi killers
  Building materials influence how we address an installation (walls, ceilings, barriers, rooms, etc.)
“Where” is the most important question
  Where are you using your hardwired tablets
  Where are you using your wireless tablets
Site surveys/Floorplans are our friend
  Looking at a space specifically helps us avoid unnecessary effort, or concentrate VERY necessary resources towards a tougher project

## Slide 141: Congrats! You’ve completed PAR’S Networking Training!