BRAKE LIGHT SWITCH WITH TIMER INSTRUCTIONS

- Connect the 12 Volt power to one wire on the  brake light switch

- Connect the other wire on the brake light switch to terminal #2

- Connect the Ground wire to terminal # 3

- Connect the tail lights red wire to Terminal #1

- Use the small bracket to attach to the brake cable jam nut

- Mount the switch and bracket to the cart

When the switch is pulled it will power the timer and if the parking brake is applied the timer will shut off after 30 seconds.

The timer will reset when the power is removed when the brake is taken off park and will re start when the brake is applied.