BATTERY METER INSTALLATION   36V or 48V

Connecting To Your Cart

BATTERY METER INSTRUCTIONS FOR DISPLAY ON ALL THE TIME

Find the 2 points with a voltage meter across the 6 battery pack on the cart that has 36 or 48 Volts depending on your carts voltage.

RED WIRE = Battery Positive + Connects to the vehicle’s main positive (+) battery terminal.

Use as short a wire as practical.

BLACK WIRE = Battery Neg. –Connects to the vehicle’s main negative (–) battery terminal

Use as short a wire as practical.

BATTERY METER INSTALL FOR DISPLAY ONLY WHEN THE KEY IS OWN

The battery meter can be wired to only display when the carts key is own.

If the carts key switch has the carts voltage (36 or 48 Volts) at the key switch then the RED WIRE can be connected to that terminal on the key switch and the battery meter will only display when the key is own.

Use as short a wire as needed to the switch.

The battery meter has a very small LED Display and uses very little power so either connection is OK.