## Slide 1
Denture Clone
Denture in one
or
2 visits.
No CAD, No Computer
With in-house Lab.
With an independent Lab.

## Slide 2: Upper, Lower Impression and VDO are taken

## Slide 3
Measure VDO using Lab Putty of choice

## Slide 4
Choose from 5 different Denture Clone sizes

## Slide 5: To open or close the arch, Soak in warm water for 20s at 125°F

## Slide 6
Adjust to arch size
Do not attempt to adjust denture Clone when cold

## Slide 7
Very Important.
Denture Clone need to be cooled down before applying the PVS wash material or trying in the mouth

## Slide 8: Cool down in cold water and check the fit

## Slide 9: Load with medium PVS material of choice

## Slide 10: Position Denture Clone with: Correct Mid line and Smile line.

## Slide 11: Approximate setting time 3min

## Slide 12: Check all landmarks for proper positions
Repeat or add PVS material if necessary

## Slide 13: Denture Clone with wash ready for Lab process

## Slide 14: Lab procedure

## Slide 15: Upper & Lower at the lab

## Slide 16: Models poured up

## Slide 17: Upper, Lower and bite at the lab

## Slide 18: Case articulated with bite & VDO

## Slide 19: Models ready to accept Denture Clone

## Slide 20: Transfer Denture clone to the model

## Slide 21: Wax up completed and processed

## Slide 22: Denture delivered:
Same visit with in-house lab or 2nd visit with independent lab