## Slide 1
Synergy between IX & RO as complimentary technologies in sustainable water and process treatment
Improve recovery by reducing fouling
Hardness reduction to increase % recovery
Ultra-Pure Water for Hydrogen Electrolysers
Contaminants removal (eg PFAS & mining)
Organic scavenger
Feed
Permeate
Softening / decarbo.
Feed
Permeate
Sea or Brackish Water
MB
Permeate
UPW
Feed
Permeate
PFAS Concen-trate
Beneficial re-use
IXR columns
Adsorptive IX Resins as pre-treatment to the RO system as a scavenger
Application: high dissolved organics in the feed water
Reduction of organic fouling on RO membranes
Brine Regeneration
WAC & SAC resins to partially soften water
Application: Industrial water with high carbonate hardness
Reduction of scaling inside the RO
Overall reduction in water, chemical consumption and energy foot-print
Contaminant concentration with RO membranes, followed by selective IX Resins
Application: Wastewater and Potable water treatment
Reduction in resin inventory & disposal costs
Safe drinking water and environmental compliance
Water demineralization RO system with Mixed Bed polishing
Application: Industrial water with high quality requirements
Ultra pure water quality
Robust design offers consistent quality & flexibility
RO
RO
RO
RO/NF
Treated Water